## Slide 1
WSQ · TGS-2023037854
Cisco Certified Network Associate (CCNA)
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
1
Implement, diagnose and verify
IPv4/IPv6 enterprise networks
5 days · 40 hours
38 training + 2 assessment
Current exam v1.1 · announced v2.0 transition
CCNA
Tertiary Infotech Academy Pte Ltd
UEN: 201200696W · Version 7.0 ·13 September 2026

## Slide 2
COURSE ADMINISTRATION
Digital Attendance (Mandatory)
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
2
Digital attendance
Use the QR code or attendance link issued on the LMS. Digital attendance and TRAQOM feedback are separate requirements.
TRAQOM feedback
TRAQOM measures training quality and outcomes through feedback surveys. Complete the survey using the provider-issued link.
Assessment attendance
Complete assessment digital attendance at the scheduled assessment block.

## Slide 3
COURSE ADMINISTRATION
About the Trainer · general template
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
3
Trainer name
[Trainer name]
[Role and organisation]
Technical experience
[Cisco credentials]
[Routing/switching projects]
[Operational experience]
Delivery / support
[Contact details]
[Availability]
[Class support arrangements]
?

## Slide 4
COURSE ADMINISTRATION
About the Trainer · named example
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
4
Dr Alfred Ang
Named trainer example
Current delivery assignment is confirmed separately by the provider.
Example profile
Demonstrations, guided technical analysis and supervised activities.
Provider confirms credentials and assignment.
Contact / support
enquiry@tertiaryinfotech.com
+65 6100 0613
LMS: lms-tms.tertiaryinfotech.com
AA

## Slide 5
COURSE ADMINISTRATION
Learner Introduction
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
5
Your environment
Name, role and network responsibilities.
Example equipment/platform used.
Your diagnostic evidence
Describe a symptom and a command/capture that helped locate it.
Your learning target
Identify one addressing, switching, routing or security task you need to verify.

## Slide 6
COURSE ADMINISTRATION
Ground Rules
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
6
Isolated practice
Use synthetic addresses and credentials. Never paste live secrets into AI prompts or public artifacts.
Evidence first
Record commands, outputs and target identity; distinguish simulated evidence from hardware execution.
Collaborative class
Ask questions, respect equipment and peers, and keep activity files organized for review.

## Slide 7
COURSE ADMINISTRATION
Course Outline / Lesson Plan
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
7
Days 1-2
Network Fundamentals and Network Access
Addressing, physical links, VLANs, trunks, STP and WLANs.
Days 3-4
IP Connectivity, IP Services and Security
Static/OSPF, NAT, DHCP/DNS, ACLs and access controls.
Day 5
Automation, integrated verification and announced v2.0 transition
Written and practical assessment.

## Slide 8
COURSE ADMINISTRATION
Learning Outcomes · TSC ICT-DIT-3009-1.1
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
8
A1-A2 requirements
Analyze requirements and select interdependent components using capacity, addressing and path evidence.
A3-A4 implementation
Implement devices and access controls; interpret observable configuration and network state.
A5-A6 operations
Select management tools; report stability and remediation from verified operational evidence.

## Slide 9
COURSE ADMINISTRATION
Briefing for Assessment
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
9
Written Assessment
1 hour, open book; knowledge questions aligned to K1-K6. Use current course guide and supplied references.
Practical Performance
1 hour, open book; device/network implementation and verification aligned to A1-A6.
Evidence / submission
Assessment is separate from learning activities and external CCNA practice. Submit using trainer-issued LMS instructions.

## Slide 10
COURSE ADMINISTRATION
Assessment & Funding
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
10
Attendance gate
Minimum attendance requirement and assessment eligibility are checked against the current programme requirements.
Assessment criteria
Competency is judged using the approved WSQ assessment criteria; Cisco exam passing rules are separate.
Funding terms
Refer to current official course page and provider eligibility terms. Funding depends on learner eligibility.

## Slide 11
COURSE ADMINISTRATION
LMS Courseware and Assessment
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
11
Current courseware
Use the course LMS entry for slides, guide and activities. Verify title and TGS code before downloading.
Private assessments
Candidate assessment papers and submission links are trainer-issued. Answer keys remain trainer-only.
Support
https://lms-tms.tertiaryinfotech.com/
Report mismatched course links to the trainer.

## Slide 12
EXAM BLUEPRINT
Current CCNA v1.1 domain model
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
12
Chart: 
| Fundamentals | Access | IP routing | IP services | Security | Automation
Exam weighting (%) | 20 | 20 | 25 | 10 | 15 | 10
Network Fundamentals 20%
Network Access 20%
IP Connectivity 25%
IP Services 10%
Security Fundamentals 15%
Automation and Programmability 10%
Current v1.1 until 2 Feb 2027.
What the data shows: Network Fundamentals 20%

## Slide 13
FORMULA · 2^HOSTBITS - 2
VLSM allocation: demand versus capacity
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
13
Chart: 
| 60-host demand | 28-host demand | 12-host demand
Usable hosts | 62 | 30 | 14
Usable capacity:62,30,14
Prefixes:/26,/27,/28
Allocate aligned blocks largest first.
No overlap is permitted.
What the data shows: Usable capacity:62,30,14

## Slide 14
SUBNET CAPACITY
Five VLANs: /26 versus /27
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
14
Chart: 
| /26 available | Required VLANs | /27 available
Subnet count | 4 | 5 | 8
A /24 borrowed 2 bits gives 4 subnets
Borrow 3 bits gives 8 subnets
Five equalVLANs require /27
Each block has 30 usable addresses.
What the data shows: A /24 borrowed 2 bits gives 4 subnets

## Slide 15
HARDWARE CAPACITY
PoE budget: allocated versus available
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
15
Chart: 
| 8 APs required | Switch budget
Watts | 123.2 | 120
123.2 W required >120 W available
Shortfall 3.2 W
Check per-port class plus total budget.
Link-up is not proof of delivered power.
What the data shows: 123.2 W required >120 W available

## Slide 16
20% · CURRENT CCNA V 1.1
Network Fundamentals
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
16
Network Fundamentals
Named boundaries -> runtime trace -> exact contract -> failure/control -> acceptance evidence

## Slide 17
NETWORK FUNDAMENTALS · ARCHITECTURE
Frame and packet boundaries · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
17
Host NIC
Source/destination L2 addresses
Access switch
Learn and forward within VLAN
Default gateway
Terminate subnet and rewrite L2
Ethernet dst 00:11:22:33:44:55
TCP src 49152 dst 443
Boundary to inspect
A remote IP never becomes a local destination MAC
Capture both sides of R1: IP endpoints persist without NAT; source and destination MAC change

## Slide 18
NETWORK FUNDAMENTALS · MECHANISM
Frame and packet boundaries · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
18
1
Application bytes enter TCP
2
IP selects destination
3
Ethernet selects next-hop MAC
4
Router rewrites L2 at each hop
State/input
Ethernet dst 00:11:22:33:44:55
Observable consequence
TCP src 49152 dst 443
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 19
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Frame and packet boundaries · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
19
Ethernet dst 00:11:22:33:44:55
IPv4 src 192.0.2.10 dst 198.51.100.20
TCP src 49152 dst 443
INPUT / IDENTITY
Host NIC · Application bytes enter TCP
DECISION / STATE
Ethernet selects next-hop MAC
READBACK / RESULT
Router rewrites L2 at each hop
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 20
NETWORK FUNDAMENTALS · DIAGNOSIS
Frame and packet boundaries · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
20
Does the observed state satisfy the contract?
Mismatch / control
A remote IP never becomes a local destination MAC. Validate ARP for the gateway, not the remote server.
Conforming / verification
Capture both sides of R1: IP endpoints persist without NAT; source and destination MAC change. TTL decreases by one.
Ethernet dst 00:11:22:33:44:55
Inspect
Default gateway
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 21
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Frame and packet boundaries · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
21
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Host NIC -> Default gateway | Ethernet dst 00:11:22:33:44:55
Mechanism / state | Router rewrites L2 at each hop | TCP src 49152 dst 443
Result / boundary | Capture both sides of R1: IP endpoints persist without NAT; source and destination MAC change. TTL decreases by one. | A remote IP never becomes a local destination MAC. Validate ARP for the gateway, not the remote server.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 22
NETWORK FUNDAMENTALS · ARCHITECTURE
Router and switch forwarding · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
22
CAM table
Source-MAC learning and destination-MAC lookup
Routing table
Destination-IP longest-prefix lookup
ARP table
IPv4 next-hop to MAC resolution
MAC VLAN 10 0011.2233.4455 Gi1/0/1
ARP 192.0.2.1 00aa.bbcc.ddee
Boundary to inspect
Unknown unicast floods only within its VLAN
show mac address-table; show ip route; show ip arp

## Slide 23
NETWORK FUNDAMENTALS · MECHANISM
Router and switch forwarding · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
23
1
Switch learns source MAC
2
Lookup uses destination MAC
3
Router performs longest prefix match
4
ARP resolves egress next hop
State/input
MAC VLAN 10 0011.2233.4455 Gi1/0/1
Observable consequence
ARP 192.0.2.1 00aa.bbcc.ddee
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 24
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Router and switch forwarding · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
24
MAC VLAN 10 0011.2233.4455 Gi1/0/1
Route 198.51.100.0/24 via 192.0.2.1
ARP 192.0.2.1 00aa.bbcc.ddee
INPUT / IDENTITY
CAM table · Switch learns source MAC
DECISION / STATE
Router performs longest prefix match
READBACK / RESULT
ARP resolves egress next hop
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 25
NETWORK FUNDAMENTALS · DIAGNOSIS
Router and switch forwarding · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
25
Does the observed state satisfy the contract?
Mismatch / control
Unknown unicast floods only within its VLAN. A missing route is not solved by adding a MAC entry.
Conforming / verification
show mac address-table; show ip route; show ip arp. Separate L2 learning from L3 path selection.
MAC VLAN 10 0011.2233.4455 Gi1/0/1
Inspect
ARP table
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 26
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Router and switch forwarding · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
26
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | CAM table -> ARP table | MAC VLAN 10 0011.2233.4455 Gi1/0/1
Mechanism / state | ARP resolves egress next hop | ARP 192.0.2.1 00aa.bbcc.ddee
Result / boundary | show mac address-table; show ip route; show ip arp. Separate L2 learning from L3 path selection. | Unknown unicast floods only within its VLAN. A missing route is not solved by adding a MAC entry.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 27
NETWORK FUNDAMENTALS · ARCHITECTURE
Firewall and IPS control points · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
27
Inside segment
Local protected network
Policy firewall
Tuple/state-based policy enforcement
Inline IPS
Payload inspection and verdict
Session TCP 192.0.2.10:49152 -> 203.0.113.5:443
IPS verdict: alert / block
Boundary to inspect
Stateful permit does not imply payload is safe
Compare policy hit counters, session entries and IPS event timestamps

## Slide 28
NETWORK FUNDAMENTALS · MECHANISM
Firewall and IPS control points · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
28
1
Session initiates outbound
2
State table records tuple
3
Return tuple matches state
4
IPS inspects permitted payload
State/input
Session TCP 192.0.2.10:49152 -> 203.0.113.5:443
Observable consequence
IPS verdict: alert / block
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 29
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Firewall and IPS control points · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
29
Session TCP 192.0.2.10:49152 -> 203.0.113.5:443
State ESTABLISHED
IPS verdict: alert / block
INPUT / IDENTITY
Inside segment · Session initiates outbound
DECISION / STATE
Return tuple matches state
READBACK / RESULT
IPS inspects permitted payload
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 30
NETWORK FUNDAMENTALS · DIAGNOSIS
Firewall and IPS control points · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
30
Does the observed state satisfy the contract?
Mismatch / control
Stateful permit does not imply payload is safe. Asymmetric routing can prevent return traffic matching the expected state.
Conforming / verification
Compare policy hit counters, session entries and IPS event timestamps. A permitted session can still be blocked by inspection.
Session TCP 192.0.2.10:49152 -> 203.0.113.5:443
Inspect
Inline IPS
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 31
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Firewall and IPS control points · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
31
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Inside segment -> Inline IPS | Session TCP 192.0.2.10:49152 -> 203.0.113.5:443
Mechanism / state | IPS inspects permitted payload | IPS verdict: alert / block
Result / boundary | Compare policy hit counters, session entries and IPS event timestamps. A permitted session can still be blocked by inspection. | Stateful permit does not imply payload is safe. Asymmetric routing can prevent return traffic matching the expected state.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 32
NETWORK FUNDAMENTALS · ARCHITECTURE
Wireless controller boundaries · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
32
Wireless client
Association and encryption endpoint
Access point
RF access and CAPWAP endpoint
WLC
WLAN policy and AP management
CAPWAP control UDP 5246
SSID Staff -> VLAN 20
Boundary to inspect
Do not infer data path from control connectivity
Identify AP mode, WLAN-to-VLAN mapping and client IP

## Slide 33
NETWORK FUNDAMENTALS · MECHANISM
Wireless controller boundaries · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
33
1
Client associates to AP
2
CAPWAP carries AP control
3
WLC applies WLAN policy
4
Data uses central or local switching
State/input
CAPWAP control UDP 5246
Observable consequence
SSID Staff -> VLAN 20
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 34
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Wireless controller boundaries · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
34
CAPWAP control UDP 5246
CAPWAP data UDP 5247
SSID Staff -> VLAN 20
INPUT / IDENTITY
Wireless client · Client associates to AP
DECISION / STATE
WLC applies WLAN policy
READBACK / RESULT
Data uses central or local switching
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 35
NETWORK FUNDAMENTALS · DIAGNOSIS
Wireless controller boundaries · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
35
Does the observed state satisfy the contract?
Mismatch / control
Do not infer data path from control connectivity. FlexConnect local switching may keep client traffic at the site.
Conforming / verification
Identify AP mode, WLAN-to-VLAN mapping and client IP. Control tunnel reachability and client gateway reachability are different tests.
CAPWAP control UDP 5246
Inspect
WLC
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 36
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Wireless controller boundaries · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
36
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Wireless client -> WLC | CAPWAP control UDP 5246
Mechanism / state | Data uses central or local switching | SSID Staff -> VLAN 20
Result / boundary | Identify AP mode, WLAN-to-VLAN mapping and client IP. Control tunnel reachability and client gateway reachability are different tests. | Do not infer data path from control connectivity. FlexConnect local switching may keep client traffic at the site.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 37
NETWORK FUNDAMENTALS · ARCHITECTURE
Endpoint and server dependencies · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
37
Client
Resolver and application initiator
DNS service
Name-to-address response
Application server
Service listener and authorization
DNS A app.example.test 192.0.2.50
HTTP status 200 after TLS
Boundary to inspect
A successful ping proves neither DNS nor application authorization
Compare DNS result, TCP connection and HTTP response

## Slide 38
NETWORK FUNDAMENTALS · MECHANISM
Endpoint and server dependencies · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
38
1
Name resolves to address
2
Client opens transport session
3
Server authorizes request
4
Response returns on routed path
State/input
DNS A app.example.test 192.0.2.50
Observable consequence
HTTP status 200 after TLS
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 39
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Endpoint and server dependencies · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
39
DNS A app.example.test 192.0.2.50
TCP SYN dst 443
HTTP status 200 after TLS
INPUT / IDENTITY
Client · Name resolves to address
DECISION / STATE
Server authorizes request
READBACK / RESULT
Response returns on routed path
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 40
NETWORK FUNDAMENTALS · DIAGNOSIS
Endpoint and server dependencies · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
40
Does the observed state satisfy the contract?
Mismatch / control
A successful ping proves neither DNS nor application authorization. Diagnose each dependency using its own evidence.
Conforming / verification
Compare DNS result, TCP connection and HTTP response. Record addresses and time so the test is reproducible.
DNS A app.example.test 192.0.2.50
Inspect
Application server
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 41
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Endpoint and server dependencies · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
41
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Client -> Application server | DNS A app.example.test 192.0.2.50
Mechanism / state | Response returns on routed path | HTTP status 200 after TLS
Result / boundary | Compare DNS result, TCP connection and HTTP response. Record addresses and time so the test is reproducible. | A successful ping proves neither DNS nor application authorization. Diagnose each dependency using its own evidence.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 42
NETWORK FUNDAMENTALS · ARCHITECTURE
PoE power budgets · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
42
PoE switch
Allocates per-port and total watts
Powered AP
Consumes negotiated PoE power
Power supply
Limits available total budget
8 APs x 15.4 W = 123.2 W
Deficit = 3.2 W
Boundary to inspect
A port can have a working data link while power is denied or constrained
show power inline

## Slide 43
NETWORK FUNDAMENTALS · MECHANISM
PoE power budgets · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
43
1
Device signature detected
2
Power class negotiated
3
Budget reserves watts
4
Link and radio initialize
State/input
8 APs x 15.4 W = 123.2 W
Observable consequence
Deficit = 3.2 W
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 44
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
PoE power budgets · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
44
8 APs x 15.4 W = 123.2 W
Switch available budget = 120 W
Deficit = 3.2 W
INPUT / IDENTITY
PoE switch · Device signature detected
DECISION / STATE
Budget reserves watts
READBACK / RESULT
Link and radio initialize
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 45
NETWORK FUNDAMENTALS · DIAGNOSIS
PoE power budgets · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
45
Does the observed state satisfy the contract?
Mismatch / control
A port can have a working data link while power is denied or constrained. Budget and per-port limits both matter.
Conforming / verification
show power inline. Sum allocated power, examine denied ports and compare hardware PoE class support.
8 APs x 15.4 W = 123.2 W
Inspect
Power supply
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 46
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
PoE power budgets · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
46
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | PoE switch -> Power supply | 8 APs x 15.4 W = 123.2 W
Mechanism / state | Link and radio initialize | Deficit = 3.2 W
Result / boundary | show power inline. Sum allocated power, examine denied ports and compare hardware PoE class support. | A port can have a working data link while power is denied or constrained. Budget and per-port limits both matter.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 47
NETWORK FUNDAMENTALS · ARCHITECTURE
Two-tier and three-tier paths · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
47
Access layer
Endpoint attachment and VLAN membership
Distribution pair
Gateway/policy and route aggregation
Core layer
High-capacity routed transit
Access VLAN 10 -> Distribution SVI
Core has no user access ports
Boundary to inspect
L2 stretched across distribution increases failure scope
Mark default gateway ownership and L2/L3 boundaries on the topology

## Slide 48
NETWORK FUNDAMENTALS · MECHANISM
Two-tier and three-tier paths · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
48
1
Endpoint traffic enters access
2
Distribution applies gateway/policy
3
Core transports aggregated routes
4
Return path follows destination lookup
State/input
Access VLAN 10 -> Distribution SVI
Observable consequence
Core has no user access ports
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 49
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Two-tier and three-tier paths · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
49
Access VLAN 10 -> Distribution SVI
Distribution routed uplink -> Core
Core has no user access ports
INPUT / IDENTITY
Access layer · Endpoint traffic enters access
DECISION / STATE
Core transports aggregated routes
READBACK / RESULT
Return path follows destination lookup
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 50
NETWORK FUNDAMENTALS · DIAGNOSIS
Two-tier and three-tier paths · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
50
Does the observed state satisfy the contract?
Mismatch / control
L2 stretched across distribution increases failure scope. Core design prioritizes fast routed transport over edge policy complexity.
Conforming / verification
Mark default gateway ownership and L2/L3 boundaries on the topology. Verify independent uplinks and equal-cost routes.
Access VLAN 10 -> Distribution SVI
Inspect
Core layer
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 51
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Two-tier and three-tier paths · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
51
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Access layer -> Core layer | Access VLAN 10 -> Distribution SVI
Mechanism / state | Return path follows destination lookup | Core has no user access ports
Result / boundary | Mark default gateway ownership and L2/L3 boundaries on the topology. Verify independent uplinks and equal-cost routes. | L2 stretched across distribution increases failure scope. Core design prioritizes fast routed transport over edge policy complexity.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 52
NETWORK FUNDAMENTALS · ARCHITECTURE
Spine-leaf forwarding · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
52
Leaf A
Host-facing fabric attachment
Spine pair
Equal-cost inter-leaf transport
Leaf B
Destination host attachment
Leaf A -> Spine 1 -> Leaf B
Inter-leaf routed path: two fabric links
Boundary to inspect
Leaf-to-leaf links are not required in a standard spine-leaf fabric
Count equal-cost paths and hop symmetry

## Slide 53
NETWORK FUNDAMENTALS · MECHANISM
Spine-leaf forwarding · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
53
1
Host enters local leaf
2
Leaf selects a spine
3
Spine forwards to destination leaf
4
Leaf delivers locally
State/input
Leaf A -> Spine 1 -> Leaf B
Observable consequence
Inter-leaf routed path: two fabric links
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 54
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Spine-leaf forwarding · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
54
Leaf A -> Spine 1 -> Leaf B
Alternative Leaf A -> Spine 2 -> Leaf B
Inter-leaf routed path: two fabric links
INPUT / IDENTITY
Leaf A · Host enters local leaf
DECISION / STATE
Spine forwards to destination leaf
READBACK / RESULT
Leaf delivers locally
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 55
NETWORK FUNDAMENTALS · DIAGNOSIS
Spine-leaf forwarding · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
55
Does the observed state satisfy the contract?
Mismatch / control
Leaf-to-leaf links are not required in a standard spine-leaf fabric. Oversubscription still depends on link capacities.
Conforming / verification
Count equal-cost paths and hop symmetry. Compare downlink aggregate bandwidth with uplink bandwidth.
Leaf A -> Spine 1 -> Leaf B
Inspect
Leaf B
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 56
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Spine-leaf forwarding · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
56
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Leaf A -> Leaf B | Leaf A -> Spine 1 -> Leaf B
Mechanism / state | Leaf delivers locally | Inter-leaf routed path: two fabric links
Result / boundary | Count equal-cost paths and hop symmetry. Compare downlink aggregate bandwidth with uplink bandwidth. | Leaf-to-leaf links are not required in a standard spine-leaf fabric. Oversubscription still depends on link capacities.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 57
NETWORK FUNDAMENTALS · ARCHITECTURE
WAN and SOHO boundaries · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
57
LAN router
Local subnet and default gateway
Provider WAN
Provider transport and next hop
Remote service
Destination application endpoint
LAN 192.168.10.0/24
Default via 203.0.113.1
Boundary to inspect
Private addressing cannot traverse the public Internet without a suitable translation or tunnel path
Test LAN gateway, provider next hop and a remote address separately; record where loss begins.

## Slide 58
NETWORK FUNDAMENTALS · MECHANISM
WAN and SOHO boundaries · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
58
1
LAN packet reaches CPE
2
CPE routes or translates
3
Provider transports traffic
4
Remote gateway delivers
State/input
LAN 192.168.10.0/24
Observable consequence
Default via 203.0.113.1
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 59
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
WAN and SOHO boundaries · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
59
LAN 192.168.10.0/24
CPE WAN 203.0.113.2/30
Default via 203.0.113.1
INPUT / IDENTITY
LAN router · LAN packet reaches CPE
DECISION / STATE
Provider transports traffic
READBACK / RESULT
Remote gateway delivers
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 60
NETWORK FUNDAMENTALS · DIAGNOSIS
WAN and SOHO boundaries · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
60
Does the observed state satisfy the contract?
Mismatch / control
Private addressing cannot traverse the public Internet without a suitable translation or tunnel path. WAN failure can leave LAN healthy.
Conforming / verification
Test LAN gateway, provider next hop and a remote address separately; record where loss begins.
LAN 192.168.10.0/24
Inspect
Remote service
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 61
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
WAN and SOHO boundaries · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
61
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | LAN router -> Remote service | LAN 192.168.10.0/24
Mechanism / state | Remote gateway delivers | Default via 203.0.113.1
Result / boundary | Test LAN gateway, provider next hop and a remote address separately; record where loss begins. | Private addressing cannot traverse the public Internet without a suitable translation or tunnel path. WAN failure can leave LAN healthy.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 62
NETWORK FUNDAMENTALS · ARCHITECTURE
Cloud and on-premises ownership · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
62
Local LAN
Enterprise address and route ownership
Cloud VPC/VNet
Cloud subnet routes and security policy
Provider edge
WAN/cloud connectivity boundary
Local 10.10.0.0/16
Tunnel routes must avoid overlap
Boundary to inspect
Overlapping RFC 1918 ranges make routing ambiguous
Check both route tables, tunnel state and cloud security rules

## Slide 63
NETWORK FUNDAMENTALS · MECHANISM
Cloud and on-premises ownership · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
63
1
Traffic exits enterprise edge
2
Encrypted connection crosses WAN
3
Cloud route selects subnet
4
Security policy filters destination
State/input
Local 10.10.0.0/16
Observable consequence
Tunnel routes must avoid overlap
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 64
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Cloud and on-premises ownership · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
64
Local 10.10.0.0/16
Cloud 10.20.0.0/16
Tunnel routes must avoid overlap
INPUT / IDENTITY
Local LAN · Traffic exits enterprise edge
DECISION / STATE
Cloud route selects subnet
READBACK / RESULT
Security policy filters destination
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 65
NETWORK FUNDAMENTALS · DIAGNOSIS
Cloud and on-premises ownership · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
65
Does the observed state satisfy the contract?
Mismatch / control
Overlapping RFC 1918 ranges make routing ambiguous. Provider responsibility does not cover a customer's route or security-rule error.
Conforming / verification
Check both route tables, tunnel state and cloud security rules. State who owns each control before changing it.
Local 10.10.0.0/16
Inspect
Provider edge
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 66
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Cloud and on-premises ownership · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
66
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Local LAN -> Provider edge | Local 10.10.0.0/16
Mechanism / state | Security policy filters destination | Tunnel routes must avoid overlap
Result / boundary | Check both route tables, tunnel state and cloud security rules. State who owns each control before changing it. | Overlapping RFC 1918 ranges make routing ambiguous. Provider responsibility does not cover a customer's route or security-rule error.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 67
NETWORK FUNDAMENTALS · ARCHITECTURE
Copper and optical link contracts · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
67
Transceiver
Optic/PHY capability and wavelength
Physical medium
Distance and medium compatibility
Peer interface
Negotiated speed and receive state
1000BASE-T: copper twisted pair
1000BASE-LX: longer-wave optical
Boundary to inspect
Connector fit alone does not prove compatibility
Read both interface/transceiver specifications; inspect optical receive power and interface errors.

## Slide 68
NETWORK FUNDAMENTALS · MECHANISM
Copper and optical link contracts · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
68
1
PHY negotiates capabilities
2
Signal crosses matched medium
3
Receiver recovers symbols
4
MAC reports link state
State/input
1000BASE-T: copper twisted pair
Observable consequence
1000BASE-LX: longer-wave optical
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 69
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Copper and optical link contracts · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
69
1000BASE-T: copper twisted pair
1000BASE-SX: multimode optical
1000BASE-LX: longer-wave optical
INPUT / IDENTITY
Transceiver · PHY negotiates capabilities
DECISION / STATE
Receiver recovers symbols
READBACK / RESULT
MAC reports link state
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 70
NETWORK FUNDAMENTALS · DIAGNOSIS
Copper and optical link contracts · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
70
Does the observed state satisfy the contract?
Mismatch / control
Connector fit alone does not prove compatibility. Match wavelength, fiber type, supported optic and distance rating.
Conforming / verification
Read both interface/transceiver specifications; inspect optical receive power and interface errors.
1000BASE-T: copper twisted pair
Inspect
Peer interface
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 71
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Copper and optical link contracts · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
71
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Transceiver -> Peer interface | 1000BASE-T: copper twisted pair
Mechanism / state | MAC reports link state | 1000BASE-LX: longer-wave optical
Result / boundary | Read both interface/transceiver specifications; inspect optical receive power and interface errors. | Connector fit alone does not prove compatibility. Match wavelength, fiber type, supported optic and distance rating.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 72
NETWORK FUNDAMENTALS · ARCHITECTURE
Duplex and interface errors · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
72
Local interface
Local speed, duplex and counters
Physical cable
Signal quality and physical continuity
Peer interface
Peer speed, duplex and counters
show interfaces Gi1/0/1
Speed 100 Mb/s; duplex half
Boundary to inspect
Late collisions suggest duplex or distance issues on half-duplex Ethernet; CRCs also arise from cable/optical faults.
Compare speed/duplex on both ends and monitor counter deltas after remediation rather than relying on old totals.

## Slide 73
NETWORK FUNDAMENTALS · MECHANISM
Duplex and interface errors · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
73
1
Frames transmit
2
Collision/error counters increment
3
Protocol retransmits lost data
4
Throughput falls despite link-up
State/input
show interfaces Gi1/0/1
Observable consequence
Speed 100 Mb/s; duplex half
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 74
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Duplex and interface errors · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
74
show interfaces Gi1/0/1
CRC: 240; late collisions: 12
Speed 100 Mb/s; duplex half
INPUT / IDENTITY
Local interface · Frames transmit
DECISION / STATE
Protocol retransmits lost data
READBACK / RESULT
Throughput falls despite link-up
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 75
NETWORK FUNDAMENTALS · DIAGNOSIS
Duplex and interface errors · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
75
Does the observed state satisfy the contract?
Mismatch / control
Late collisions suggest duplex or distance issues on half-duplex Ethernet; CRCs also arise from cable/optical faults.
Conforming / verification
Compare speed/duplex on both ends and monitor counter deltas after remediation rather than relying on old totals.
show interfaces Gi1/0/1
Inspect
Peer interface
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 76
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Duplex and interface errors · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
76
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Local interface -> Peer interface | show interfaces Gi1/0/1
Mechanism / state | Throughput falls despite link-up | Speed 100 Mb/s; duplex half
Result / boundary | Compare speed/duplex on both ends and monitor counter deltas after remediation rather than relying on old totals. | Late collisions suggest duplex or distance issues on half-duplex Ethernet; CRCs also arise from cable/optical faults.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 77
NETWORK FUNDAMENTALS · ARCHITECTURE
TCP session state · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
77
Client socket
Sequence, flags and source port
Network path
Loss, latency and filtering
Server socket
Listener, state and destination port
Client SYN seq=1000
Client ACK seq=1001 ack=7001
Boundary to inspect
A SYN retransmission can indicate filtering or an absent listener
Read flags and sequence/ack fields in a capture

## Slide 78
NETWORK FUNDAMENTALS · MECHANISM
TCP session state · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
78
1
SYN proposes sequence
2
SYN-ACK acknowledges client
3
ACK establishes session
4
FIN or RST terminates
State/input
Client SYN seq=1000
Observable consequence
Client ACK seq=1001 ack=7001
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 79
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
TCP session state · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
79
Client SYN seq=1000
Server SYN-ACK seq=7000 ack=1001
Client ACK seq=1001 ack=7001
INPUT / IDENTITY
Client socket · SYN proposes sequence
DECISION / STATE
ACK establishes session
READBACK / RESULT
FIN or RST terminates
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 80
NETWORK FUNDAMENTALS · DIAGNOSIS
TCP session state · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
80
Does the observed state satisfy the contract?
Mismatch / control
A SYN retransmission can indicate filtering or an absent listener. A RST indicates a different failure from silence.
Conforming / verification
Read flags and sequence/ack fields in a capture. Confirm whether the handshake completed before testing application data.
Client SYN seq=1000
Inspect
Server socket
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 81
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
TCP session state · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
81
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Client socket -> Server socket | Client SYN seq=1000
Mechanism / state | FIN or RST terminates | Client ACK seq=1001 ack=7001
Result / boundary | Read flags and sequence/ack fields in a capture. Confirm whether the handshake completed before testing application data. | A SYN retransmission can indicate filtering or an absent listener. A RST indicates a different failure from silence.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 82
NETWORK FUNDAMENTALS · ARCHITECTURE
UDP delivery and application recovery · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
82
Sender process
Datagram creation and retry logic
UDP/IP path
Best-effort transport with port/checksum
Receiver process
Application transaction matching
UDP src 53000 dst 53
Response must match transaction ID
Boundary to inspect
UDP does not establish a transport session or guarantee order
Correlate request and response using application identifiers, endpoints and timestamps; inspect loss separately from latency.

## Slide 83
NETWORK FUNDAMENTALS · MECHANISM
UDP delivery and application recovery · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
83
1
Application creates datagram
2
UDP supplies ports/checksum
3
IP attempts delivery
4
Application handles loss or retry
State/input
UDP src 53000 dst 53
Observable consequence
Response must match transaction ID
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 84
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
UDP delivery and application recovery · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
84
UDP src 53000 dst 53
DNS query ID 0x1234
Response must match transaction ID
INPUT / IDENTITY
Sender process · Application creates datagram
DECISION / STATE
IP attempts delivery
READBACK / RESULT
Application handles loss or retry
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 85
NETWORK FUNDAMENTALS · DIAGNOSIS
UDP delivery and application recovery · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
85
Does the observed state satisfy the contract?
Mismatch / control
UDP does not establish a transport session or guarantee order. A protocol can implement retries above UDP.
Conforming / verification
Correlate request and response using application identifiers, endpoints and timestamps; inspect loss separately from latency.
UDP src 53000 dst 53
Inspect
Receiver process
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 86
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
UDP delivery and application recovery · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
86
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Sender process -> Receiver process | UDP src 53000 dst 53
Mechanism / state | Application handles loss or retry | Response must match transaction ID
Result / boundary | Correlate request and response using application identifiers, endpoints and timestamps; inspect loss separately from latency. | UDP does not establish a transport session or guarantee order. A protocol can implement retries above UDP.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 87
NETWORK FUNDAMENTALS · ARCHITECTURE
IPv4 subnet boundaries · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
87
Network bits
Fixed prefix identifies network
Host bits
Variable bits provide host capacity
Broadcast boundary
All-one host bits identify broadcast
192.0.2.65/26
Network .64; usable .65-.126; broadcast .127
Boundary to inspect
Do not include network or broadcast in a traditional subnet's host allocation
2^(32-26)-2 = 62 usable addresses

## Slide 88
NETWORK FUNDAMENTALS · MECHANISM
IPv4 subnet boundaries · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
88
1
Prefix fixes network portion
2
Host bits vary
3
All-zero host identifies network
4
All-one host identifies broadcast
State/input
192.0.2.65/26
Observable consequence
Network .64; usable .65-.126; broadcast .127
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 89
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
IPv4 subnet boundaries · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
89
192.0.2.65/26
Mask 255.255.255.192
Network .64; usable .65-.126; broadcast .127
INPUT / IDENTITY
Network bits · Prefix fixes network portion
DECISION / STATE
All-zero host identifies network
READBACK / RESULT
All-one host identifies broadcast
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 90
NETWORK FUNDAMENTALS · DIAGNOSIS
IPv4 subnet boundaries · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
90
Does the observed state satisfy the contract?
Mismatch / control
Do not include network or broadcast in a traditional subnet's host allocation. /31 point-to-point links are a special case.
Conforming / verification
2^(32-26)-2 = 62 usable addresses. Check that each assigned address remains within .64-.127.
192.0.2.65/26
Inspect
Broadcast boundary
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 91
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
IPv4 subnet boundaries · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
91
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Network bits -> Broadcast boundary | 192.0.2.65/26
Mechanism / state | All-one host identifies broadcast | Network .64; usable .65-.126; broadcast .127
Result / boundary | 2^(32-26)-2 = 62 usable addresses. Check that each assigned address remains within .64-.127. | Do not include network or broadcast in a traditional subnet's host allocation. /31 point-to-point links are a special case.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 92
NETWORK FUNDAMENTALS · ARCHITECTURE
VLSM address allocation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
92
Address pool
Available aggregate address space
Largest subnet
First aligned highest-capacity block
Smaller subnets
Later aligned nonoverlapping blocks
10.10.0.0/24
12 hosts -> .96/28
Boundary to inspect
Choosing an unaligned starting boundary causes overlap
Prove allocated ranges do not intersect; compare usable host counts 62, 30, 14 with requirements 60, 28, 12.

## Slide 93
NETWORK FUNDAMENTALS · MECHANISM
VLSM address allocation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
93
1
Sort host demands descending
2
Choose prefix for each need
3
Allocate aligned blocks
4
Reserve remaining address space
State/input
10.10.0.0/24
Observable consequence
12 hosts -> .96/28
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 94
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
VLSM address allocation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
94
10.10.0.0/24
60 hosts -> .0/26
28 hosts -> .64/27
12 hosts -> .96/28
INPUT / IDENTITY
Address pool · Sort host demands descending
DECISION / STATE
Allocate aligned blocks
READBACK / RESULT
Reserve remaining address space
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 95
NETWORK FUNDAMENTALS · DIAGNOSIS
VLSM address allocation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
95
Does the observed state satisfy the contract?
Mismatch / control
Choosing an unaligned starting boundary causes overlap. VLSM addresses capacity; routes must also be advertised correctly.
Conforming / verification
Prove allocated ranges do not intersect; compare usable host counts 62, 30, 14 with requirements 60, 28, 12.
10.10.0.0/24
Inspect
Smaller subnets
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 96
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
VLSM address allocation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
96
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Address pool -> Smaller subnets | 10.10.0.0/24
Mechanism / state | Reserve remaining address space | 12 hosts -> .96/28
Result / boundary | Prove allocated ranges do not intersect; compare usable host counts 62, 30, 14 with requirements 60, 28, 12. | Choosing an unaligned starting boundary causes overlap. VLSM addresses capacity; routes must also be advertised correctly.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 97
NETWORK FUNDAMENTALS · ARCHITECTURE
Private and public addressing · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
97
RFC 1918 space
RFC 1918 internally routable scope
Enterprise edge
Public path and translation boundary
Public service
Globally reachable destination address
Private: 10/8, 172.16/12, 192.168/16
Documentation: 192.0.2/24, 198.51.100/24, 203.0.113/24
Boundary to inspect
Documentation ranges are for examples, not production Internet addressing
Classify each candidate prefix; preserve original and translated addresses in the incident report.

## Slide 98
NETWORK FUNDAMENTALS · MECHANISM
Private and public addressing · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
98
1
Private address is assigned internally
2
Edge selects Internet route
3
NAT may change source
4
Public server returns translated tuple
State/input
Private: 10/8, 172.16/12, 192.168/16
Observable consequence
Documentation: 192.0.2/24, 198.51.100/24, 203.0.113/24
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 99
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Private and public addressing · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
99
Private: 10/8, 172.16/12, 192.168/16
Documentation: 192.0.2/24, 198.51.100/24, 203.0.113/24
INPUT / IDENTITY
RFC 1918 space · Private address is assigned internally
DECISION / STATE
NAT may change source
READBACK / RESULT
Public server returns translated tuple
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 100
NETWORK FUNDAMENTALS · DIAGNOSIS
Private and public addressing · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
100
Does the observed state satisfy the contract?
Mismatch / control
Documentation ranges are for examples, not production Internet addressing. 172.15.0.0/16 is outside RFC 1918.
Conforming / verification
Classify each candidate prefix; preserve original and translated addresses in the incident report.
Private: 10/8, 172.16/12, 192.168/16
Inspect
Public service
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 101
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Private and public addressing · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
101
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | RFC 1918 space -> Public service | Private: 10/8, 172.16/12, 192.168/16
Mechanism / state | Public server returns translated tuple | Documentation: 192.0.2/24, 198.51.100/24, 203.0.113/24
Result / boundary | Classify each candidate prefix; preserve original and translated addresses in the incident report. | Documentation ranges are for examples, not production Internet addressing. 172.15.0.0/16 is outside RFC 1918.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 102
NETWORK FUNDAMENTALS · ARCHITECTURE
IPv6 address types · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
102
Global interface
Routed unicast scope
Link-local interface
Same-link FE80:: scope
Multicast group
Selected receiver group FF00::/8
Global 2001:db8:10::10/64
All nodes ff02::1; all routers ff02::2
Boundary to inspect
A link-local next hop needs an outgoing interface scope
Classify global unicast, unique-local FC00::/7, link-local and multicast

## Slide 103
NETWORK FUNDAMENTALS · MECHANISM
IPv6 address types · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
103
1
Interface gains FE80::/10 link-local
2
Global prefix identifies routed scope
3
Multicast reaches selected members
4
No broadcast exists
State/input
Global 2001:db8:10::10/64
Observable consequence
All nodes ff02::1; all routers ff02::2
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 104
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
IPv6 address types · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
104
Global 2001:db8:10::10/64
Link-local fe80::10
All nodes ff02::1; all routers ff02::2
INPUT / IDENTITY
Global interface · Interface gains FE80::/10 link-local
DECISION / STATE
Multicast reaches selected members
READBACK / RESULT
No broadcast exists
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 105
NETWORK FUNDAMENTALS · DIAGNOSIS
IPv6 address types · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
105
Does the observed state satisfy the contract?
Mismatch / control
A link-local next hop needs an outgoing interface scope. 2001:db8::/32 is documentation space.
Conforming / verification
Classify global unicast, unique-local FC00::/7, link-local and multicast. Inspect interface and route scopes.
Global 2001:db8:10::10/64
Inspect
Multicast group
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 106
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
IPv6 address types · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
106
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Global interface -> Multicast group | Global 2001:db8:10::10/64
Mechanism / state | No broadcast exists | All nodes ff02::1; all routers ff02::2
Result / boundary | Classify global unicast, unique-local FC00::/7, link-local and multicast. Inspect interface and route scopes. | A link-local next hop needs an outgoing interface scope. 2001:db8::/32 is documentation space.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 107
NETWORK FUNDAMENTALS · ARCHITECTURE
IPv6 neighbor and SLAAC state · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
107
Host
SLAAC address and DAD state
IPv6 router
RA prefix and default-router source
Neighbor cache
IPv6-to-MAC neighbor state
RA: prefix 2001:db8:10::/64 A=1
NS target 2001:db8:10::20
Boundary to inspect
Blocking necessary ICMPv 6 breaks neighbor discovery and path operation
Verify RA prefix, tentative-to-preferred DAD state and neighbor cache entry

## Slide 108
NETWORK FUNDAMENTALS · MECHANISM
IPv6 neighbor and SLAAC state · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
108
1
RS solicits routers
2
RA advertises prefix/default router
3
Host performs DAD
4
NS/NA resolves neighbor MAC
State/input
RA: prefix 2001:db8:10::/64 A=1
Observable consequence
NS target 2001:db8:10::20
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 109
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
IPv6 neighbor and SLAAC state · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
109
RA: prefix 2001:db8:10::/64 A=1
Default router fe80::1
NS target 2001:db8:10::20
INPUT / IDENTITY
Host · RS solicits routers
DECISION / STATE
Host performs DAD
READBACK / RESULT
NS/NA resolves neighbor MAC
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 110
NETWORK FUNDAMENTALS · DIAGNOSIS
IPv6 neighbor and SLAAC state · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
110
Does the observed state satisfy the contract?
Mismatch / control
Blocking necessary ICMPv 6 breaks neighbor discovery and path operation. SLAAC does not derive a default gateway from DHCPv 6.
Conforming / verification
Verify RA prefix, tentative-to-preferred DAD state and neighbor cache entry. Confirm a usable default route separately.
RA: prefix 2001:db8:10::/64 A=1
Inspect
Neighbor cache
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 111
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
IPv6 neighbor and SLAAC state · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
111
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Host -> Neighbor cache | RA: prefix 2001:db8:10::/64 A=1
Mechanism / state | NS/NA resolves neighbor MAC | NS target 2001:db8:10::20
Result / boundary | Verify RA prefix, tentative-to-preferred DAD state and neighbor cache entry. Confirm a usable default route separately. | Blocking necessary ICMPv 6 breaks neighbor discovery and path operation. SLAAC does not derive a default gateway from DHCPv 6.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 112
NETWORK FUNDAMENTALS · ARCHITECTURE
Wireless channel and virtual boundaries · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
112
Radio channel
Shared RF airtime and contention
SSID/VLAN mapping
Wireless logical security/network mapping
Virtual switch
VM attachment and VLAN policy
2.4 GHz nonoverlap example: 1, 6, 11
VM vNIC -> port group VLAN 20
Boundary to inspect
Overlapping channels increase contention
Compare channel utilization, SSID security, VM VLAN tag and host IP/gateway; separate RF evidence from virtual-switch evidence.

## Slide 113
NETWORK FUNDAMENTALS · MECHANISM
Wireless channel and virtual boundaries · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
113
1
Radio shares airtime
2
SSID assigns policy domain
3
Virtual switch connects VM NIC
4
L3 gateway routes between subnets
State/input
2.4 GHz nonoverlap example: 1, 6, 11
Observable consequence
VM vNIC -> port group VLAN 20
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 114
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Wireless channel and virtual boundaries · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
114
2.4 GHz nonoverlap example: 1, 6, 11
Staff SSID -> VLAN 20
VM vNIC -> port group VLAN 20
INPUT / IDENTITY
Radio channel · Radio shares airtime
DECISION / STATE
Virtual switch connects VM NIC
READBACK / RESULT
L3 gateway routes between subnets
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 115
NETWORK FUNDAMENTALS · DIAGNOSIS
Wireless channel and virtual boundaries · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
115
Does the observed state satisfy the contract?
Mismatch / control
Overlapping channels increase contention. A VM port-group VLAN mismatch looks like a physical network failure.
Conforming / verification
Compare channel utilization, SSID security, VM VLAN tag and host IP/gateway; separate RF evidence from virtual-switch evidence.
2.4 GHz nonoverlap example: 1, 6, 11
Inspect
Virtual switch
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 116
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Wireless channel and virtual boundaries · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
116
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Radio channel -> Virtual switch | 2.4 GHz nonoverlap example: 1, 6, 11
Mechanism / state | L3 gateway routes between subnets | VM vNIC -> port group VLAN 20
Result / boundary | Compare channel utilization, SSID security, VM VLAN tag and host IP/gateway; separate RF evidence from virtual-switch evidence. | Overlapping channels increase contention. A VM port-group VLAN mismatch looks like a physical network failure.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 117
NETWORK FUNDAMENTALS · ARCHITECTURE
IPv6 interface and anycast contracts · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
117
Router interface
Owns configured IPv6 address/prefix
Unicast host
One destination interface
Anycast service
One address on multiple service nodes
interface Gi0/1
ipv6 enable
Boundary to inspect
Anycast uses unicast address format; it is not multicast fan-out
show ipv 6 interface brief; compare configured /64 and address scope

## Slide 118
NETWORK FUNDAMENTALS · MECHANISM
IPv6 interface and anycast contracts · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
118
1
Interface receives global/link-local addresses
2
Unicast identifies one interface
3
Anycast address exists on multiple nodes
4
Routing delivers to topologically nearest member
State/input
interface Gi0/1
Observable consequence
ipv 6 enable
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 119
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
IPv6 interface and anycast contracts · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
119
interface Gi0/1
ipv6 address 2001:db8:10::1/64
ipv6 address fe80::1 link-local
ipv6 enable
INPUT / IDENTITY
Router interface · Interface receives global/link-local addresses
DECISION / STATE
Anycast address exists on multiple nodes
READBACK / RESULT
Routing delivers to topologically nearest member
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 120
NETWORK FUNDAMENTALS · DIAGNOSIS
IPv6 interface and anycast contracts · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
120
Does the observed state satisfy the contract?
Mismatch / control
Anycast uses unicast address format; it is not multicast fan-out. Nearest means routing metric, not geographic distance.
Conforming / verification
show ipv 6 interface brief; compare configured /64 and address scope. Anycast response comes from one reachable service member.
interface Gi0/1
Inspect
Anycast service
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 121
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
IPv6 interface and anycast contracts · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
121
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Router interface -> Anycast service | interface Gi0/1
Mechanism / state | Routing delivers to topologically nearest member | ipv 6 enable
Result / boundary | show ipv 6 interface brief; compare configured /64 and address scope. Anycast response comes from one reachable service member. | Anycast uses unicast address format; it is not multicast fan-out. Nearest means routing metric, not geographic distance.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 122
NETWORK FUNDAMENTALS · ARCHITECTURE
VRF routing isolation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
122
VRF BLUE
Independent BLUE route/forwarding context
VRF GREEN
Independent GREEN route/forwarding context
Shared physical router
Common hardware with isolated tables
BLUE route 10.10.0.0/16 via 10.0.0.2
show ip route vrf BLUE
Boundary to inspect
Do not inspect the global route table and assume a VRF-bound interface has the same paths
Verify interface VRF assignment and VRF-specific route/ARP evidence; same prefix can validly use different next hops.

## Slide 123
NETWORK FUNDAMENTALS · MECHANISM
VRF routing isolation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
123
1
Interface binds to VRF
2
Each VRF owns separate RIB/FIB
3
Overlapping prefixes remain isolated
4
Leak occurs only with explicit policy
State/input
BLUE route 10.10.0.0/16 via 10.0.0.2
Observable consequence
show ip route vrf BLUE
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 124
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
VRF routing isolation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
124
BLUE route 10.10.0.0/16 via 10.0.0.2
GREEN route 10.10.0.0/16 via 10.0.0.6
show ip route vrf BLUE
INPUT / IDENTITY
VRF BLUE · Interface binds to VRF
DECISION / STATE
Overlapping prefixes remain isolated
READBACK / RESULT
Leak occurs only with explicit policy
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 125
NETWORK FUNDAMENTALS · DIAGNOSIS
VRF routing isolation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
125
Does the observed state satisfy the contract?
Mismatch / control
Do not inspect the global route table and assume a VRF-bound interface has the same paths. Isolation is separate from encryption.
Conforming / verification
Verify interface VRF assignment and VRF-specific route/ARP evidence; same prefix can validly use different next hops.
BLUE route 10.10.0.0/16 via 10.0.0.2
Inspect
Shared physical router
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 126
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
VRF routing isolation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
126
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | VRF BLUE -> Shared physical router | BLUE route 10.10.0.0/16 via 10.0.0.2
Mechanism / state | Leak occurs only with explicit policy | show ip route vrf BLUE
Result / boundary | Verify interface VRF assignment and VRF-specific route/ARP evidence; same prefix can validly use different next hops. | Do not inspect the global route table and assume a VRF-bound interface has the same paths. Isolation is separate from encryption.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 127
NETWORK FUNDAMENTALS · ARCHITECTURE
MAC aging and unknown-unicast scope · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
127
Source MAC learner
Refreshes source location on received frames
CAM aging timer
Expires idle dynamic MAC entries
VLAN flood domain
Eligible ports in the same VLAN
VLAN 10 MAC0011.2233.4455 portGi 1/0/1
Unknown unicast floods VLAN 10 only
Boundary to inspect
Aging time varies by platform/configuration; a removed entry does not remove the host's IP
show mac address-table aging-time; compare entry before/after inactivity and source relearning; distinguish CAM aging from ARP aging.

## Slide 128
NETWORK FUNDAMENTALS · MECHANISM
MAC aging and unknown-unicast scope · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
128
1
Incoming source refreshes entry
2
Idle entry reaches aging threshold
3
Entry is removed
4
Unknown destination floods eligible same-VLAN ports
State/input
VLAN 10 MAC0011.2233.4455 portGi 1/0/1
Observable consequence
Unknown unicast floods VLAN 10 only
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 129
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
MAC aging and unknown-unicast scope · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
129
VLAN 10 MAC0011.2233.4455 portGi 1/0/1
Dynamic aging timer 300 s example
Unknown unicast floods VLAN 10 only
INPUT / IDENTITY
Source MAC learner · Incoming source refreshes entry
DECISION / STATE
Entry is removed
READBACK / RESULT
Unknown destination floods eligible same-VLAN ports
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 130
NETWORK FUNDAMENTALS · DIAGNOSIS
MAC aging and unknown-unicast scope · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
130
Does the observed state satisfy the contract?
Mismatch / control
Aging time varies by platform/configuration; a removed entry does not remove the host's IP. Flooding cannot cross VLAN boundary without L3 processing.
Conforming / verification
show mac address-table aging-time; compare entry before/after inactivity and source relearning; distinguish CAM aging from ARP aging.
VLAN 10 MAC0011.2233.4455 portGi 1/0/1
Inspect
VLAN flood domain
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 131
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
MAC aging and unknown-unicast scope · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
131
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Source MAC learner -> VLAN flood domain | VLAN 10 MAC0011.2233.4455 portGi 1/0/1
Mechanism / state | Unknown destination floods eligible same-VLAN ports | Unknown unicast floods VLAN 10 only
Result / boundary | show mac address-table aging-time; compare entry before/after inactivity and source relearning; distinguish CAM aging from ARP aging. | Aging time varies by platform/configuration; a removed entry does not remove the host's IP. Flooding cannot cross VLAN boundary without L3 processing.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 132
NETWORK FUNDAMENTALS · ARCHITECTURE
Modified EUI-64 address construction · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
132
48-bit NIC MAC
Input 48-bit interface identifier
Inserted FFFE
16-bit insertion in MAC-derived value
64-bit interface ID
Final low 64 bits of IPv6 address
MAC00:11:22:33:44:55
2001:db8:10:0:211:22ff:fe33:4455
Boundary to inspect
Modern clients often use privacy/stable interface IDs instead
Prove 00 xor 02 =02 and exact inserted FFFE placement; compare prefix plus 64-bit interface identifier.

## Slide 133
NETWORK FUNDAMENTALS · MECHANISM
Modified EUI-64 address construction · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
133
1
Split MAC into 24-bit halves
2
Insert hexadecimal FFFE
3
Invert universal/local bit
4
Join 64-bit ID to /64 prefix
State/input
MAC00:11:22:33:44:55
Observable consequence
2001:db8:10:0:211:22ff:fe33:4455
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 134
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Modified EUI-64 address construction · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
134
MAC00:11:22:33:44:55
ID0211:22ff:fe33:4455
2001:db8:10:0:211:22ff:fe33:4455
INPUT / IDENTITY
48-bit NIC MAC · Split MAC into 24-bit halves
DECISION / STATE
Invert universal/local bit
READBACK / RESULT
Join 64-bit ID to /64 prefix
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 135
NETWORK FUNDAMENTALS · DIAGNOSIS
Modified EUI-64 address construction · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
135
Does the observed state satisfy the contract?
Mismatch / control
Modern clients often use privacy/stable interface IDs instead. EUI-64 calculation is a specified method, not a claim every host uses it.
Conforming / verification
Prove 00 xor 02 =02 and exact inserted FFFE placement; compare prefix plus 64-bit interface identifier.
MAC00:11:22:33:44:55
Inspect
64-bit interface ID
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 136
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Modified EUI-64 address construction · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
136
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | 48-bit NIC MAC -> 64-bit interface ID | MAC00:11:22:33:44:55
Mechanism / state | Join 64-bit ID to /64 prefix | 2001:db8:10:0:211:22ff:fe33:4455
Result / boundary | Prove 00 xor 02 =02 and exact inserted FFFE placement; compare prefix plus 64-bit interface identifier. | Modern clients often use privacy/stable interface IDs instead. EUI-64 calculation is a specified method, not a claim every host uses it.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 137
NETWORK FUNDAMENTALS · ARCHITECTURE
Hypervisor VM and container isolation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
137
Hypervisor
Virtualizes guest hardware
Guest VM OS
Independent guest kernel and NIC
Container host kernel
Shared host kernel with namespaces
VM: app->guest kernel->vNIC->vSwitch
VLAN policy belongs to attachment
Boundary to inspect
A container is not a separate guest kernel
Trace address, virtual NIC/bridge, VLAN and gateway; compare host versus guest responsibilities during a connectivity incident.

## Slide 138
NETWORK FUNDAMENTALS · MECHANISM
Hypervisor VM and container isolation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
138
1
Hypervisor virtualizes hardware
2
VM owns guest kernel
3
Container shares host kernel
4
vNIC/veth attaches virtual network
State/input
VM: app->guest kernel->vNIC->vSwitch
Observable consequence
VLAN policy belongs to attachment
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 139
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Hypervisor VM and container isolation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
139
VM: app->guest kernel->vNIC->vSwitch
Container: app->shared kernel->veth/bridge
VLAN policy belongs to attachment
INPUT / IDENTITY
Hypervisor · Hypervisor virtualizes hardware
DECISION / STATE
Container shares host kernel
READBACK / RESULT
vNIC/veth attaches virtual network
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 140
NETWORK FUNDAMENTALS · DIAGNOSIS
Hypervisor VM and container isolation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
140
Does the observed state satisfy the contract?
Mismatch / control
A container is not a separate guest kernel. Network namespaces and virtual attachment policies still require isolation controls.
Conforming / verification
Trace address, virtual NIC/bridge, VLAN and gateway; compare host versus guest responsibilities during a connectivity incident.
VM: app->guest kernel->vNIC->vSwitch
Inspect
Container host kernel
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 141
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Hypervisor VM and container isolation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
141
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Hypervisor -> Container host kernel | VM: app->guest kernel->vNIC->vSwitch
Mechanism / state | vNIC/veth attaches virtual network | VLAN policy belongs to attachment
Result / boundary | Trace address, virtual NIC/bridge, VLAN and gateway; compare host versus guest responsibilities during a connectivity incident. | A container is not a separate guest kernel. Network namespaces and virtual attachment policies still require isolation controls.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 142
NETWORK FUNDAMENTALS · ARCHITECTURE
RF link-budget and interference evidence · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
142
AP transmitter
Transmit power and antenna gain
RF path
Loss and noise through RF medium
Client receiver
Received strength, SNR and retry state
RSSI-62 dBm; noise-92 dBm
RSSI alone does not establish usable throughput
Boundary to inspect
Good signal can coexist with interference/high contention
Compare SNR, utilization, retry rate and client throughput; identify whether issue is signal strength, noise or airtime contention.

## Slide 143
NETWORK FUNDAMENTALS · MECHANISM
RF link-budget and interference evidence · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
143
1
Transmit power enters antenna
2
Path loss reduces received signal
3
Noise determines signal margin
4
Rate adaptation responds to channel conditions
State/input
RSSI-62 dBm; noise-92 dBm
Observable consequence
RSSI alone does not establish usable throughput
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 144
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
RF link-budget and interference evidence · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
144
RSSI-62 dBm; noise-92 dBm
SNR=30 dB
Channel utilization 75%
RSSI alone does not establish usable throughput
INPUT / IDENTITY
AP transmitter · Transmit power enters antenna
DECISION / STATE
Noise determines signal margin
READBACK / RESULT
Rate adaptation responds to channel conditions
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 145
NETWORK FUNDAMENTALS · DIAGNOSIS
RF link-budget and interference evidence · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
145
Does the observed state satisfy the contract?
Mismatch / control
Good signal can coexist with interference/high contention. Wider channels increase capacity potential but consume spectrum and affect reuse.
Conforming / verification
Compare SNR, utilization, retry rate and client throughput; identify whether issue is signal strength, noise or airtime contention.
RSSI-62 dBm; noise-92 dBm
Inspect
Client receiver
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 146
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
RF link-budget and interference evidence · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
146
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | AP transmitter -> Client receiver | RSSI-62 dBm; noise-92 dBm
Mechanism / state | Rate adaptation responds to channel conditions | RSSI alone does not establish usable throughput
Result / boundary | Compare SNR, utilization, retry rate and client throughput; identify whether issue is signal strength, noise or airtime contention. | Good signal can coexist with interference/high contention. Wider channels increase capacity potential but consume spectrum and affect reuse.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 147
NETWORK FUNDAMENTALS · ARCHITECTURE
Cross-platform client diagnostics · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
147
Windows host
ipconfig, route print and resolver state
macOS host
ifconfig, netstat and resolver state
Linux host
ip addr, ip route and resolver state
Windows: ipconfig /all; route print
All: ping + name/service test
Boundary to inspect
Different commands expose equivalent layers
Build evidence table for address, prefix, gateway, DNS, association/security and first failing path control.

## Slide 148
NETWORK FUNDAMENTALS · MECHANISM
Cross-platform client diagnostics · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
148
1
Read address/mask
2
Read default route
3
Resolve intended name
4
Test path and service
State/input
Windows: ipconfig /all; route print
Observable consequence
All: ping + name/service test
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 149
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Cross-platform client diagnostics · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
149
Windows: ipconfig /all; route print
macOS: ifconfig; netstat -rn
Linux: ip addr; ip route
All: ping + name/service test
INPUT / IDENTITY
Windows host · Read address/mask
DECISION / STATE
Resolve intended name
READBACK / RESULT
Test path and service
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 150
NETWORK FUNDAMENTALS · DIAGNOSIS
Cross-platform client diagnostics · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
150
Does the observed state satisfy the contract?
Mismatch / control
Different commands expose equivalent layers. A disconnected wireless association is separate from a correct but unusable IP configuration.
Conforming / verification
Build evidence table for address, prefix, gateway, DNS, association/security and first failing path control.
Windows: ipconfig /all; route print
Inspect
Linux host
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 151
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Cross-platform client diagnostics · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
151
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Windows host -> Linux host | Windows: ipconfig /all; route print
Mechanism / state | Test path and service | All: ping + name/service test
Result / boundary | Build evidence table for address, prefix, gateway, DNS, association/security and first failing path control. | Different commands expose equivalent layers. A disconnected wireless association is separate from a correct but unusable IP configuration.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 152
NETWORK FUNDAMENTALS · ARCHITECTURE
Five equal subnets from a /24 · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
152
192.168.1.0/24 pool
256-address aggregate pool
Three borrowed bits
Eight aligned equal-sized blocks
Five allocated /27 VLANs
Five nonoverlapping 30-host allocations
Five VLANs from 192.168.1.0/24
VLAN 5 .128/27 gateway.158
Boundary to inspect
Do not choose /26 for five equal subnets: only four blocks fit in a /24
Each /27 has 30 usable addresses

## Slide 153
NETWORK FUNDAMENTALS · MECHANISM
Five equal subnets from a /24 · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
153
1
Need at least five subnets
2
Borrow three bits since 2^3=8
3
Use /27 blocks of 32 addresses
4
Assign last usable gateway in each block
State/input
Five VLANs from 192.168.1.0/24
Observable consequence
VLAN 5 .128/27 gateway.158
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 154
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Five equal subnets from a /24 · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
154
Five VLANs from 192.168.1.0/24
/26 gives4subnets: insufficient
/27 gives8subnets: enough
VLAN 1 .0/27 gateway.30; VLAN 2 .32/27 gateway.62
VLAN 3 .64/27 gateway.94; VLAN 4 .96/27 gateway.126
VLAN 5 .128/27 gateway.158
INPUT / IDENTITY
192.168.1.0/24 pool · Need at least five subnets
DECISION / STATE
Use /27 blocks of 32 addresses
READBACK / RESULT
Assign last usable gateway in each block
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 155
NETWORK FUNDAMENTALS · DIAGNOSIS
Five equal subnets from a /24 · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
155
Does the observed state satisfy the contract?
Mismatch / control
Do not choose /26 for five equal subnets: only four blocks fit in a /24. A Layer 2 switch management address belongs on an SVI, not an ordinary switched physical port.
Conforming / verification
Each /27 has 30 usable addresses. Gateways .30, .62, .94, .126, .158 are the last usable addresses; broadcast addresses .31, .63, .95, .127, .159 are not host assignments.
Five VLANs from 192.168.1.0/24
Inspect
Five allocated /27 VLANs
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 156
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Five equal subnets from a /24 · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
156
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | 192.168.1.0/24 pool -> Five allocated /27 VLANs | Five VLANs from 192.168.1.0/24
Mechanism / state | Assign last usable gateway in each block | VLAN 5 .128/27 gateway.158
Result / boundary | Each /27 has 30 usable addresses. Gateways .30, .62, .94, .126, .158 are the last usable addresses; broadcast addresses .31, .63, .95, .127, .159 are not host assignments. | Do not choose /26 for five equal subnets: only four blocks fit in a /24. A Layer 2 switch management address belongs on an SVI, not an ordinary switched physical port.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 157
NETWORK FUNDAMENTALS · ARCHITECTURE
Single-mode versus multimode optical paths · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
157
Single-mode fibre
One propagation mode and lower modal dispersion
Multimode fibre
Multiple modes and modal dispersion
Matched optic pair
Compatible transmit/receive optical contract
Single-mode: small core, one propagation mode
1000BASE-LX:1310nm class; verify exact reach/media
Boundary to inspect
Fibre jacket colour does not prove specification
Compare both-end wavelength, fibre type, supported distance and receive power; a fitted connector is insufficient evidence.

## Slide 158
NETWORK FUNDAMENTALS · MECHANISM
Single-mode versus multimode optical paths · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
158
1
Emitter selects wavelength
2
Core/mode characteristics govern propagation
3
Attenuation/dispersion limit reach
4
Receiver power must stay in supported range
State/input
Single-mode: small core, one propagation mode
Observable consequence
1000BASE-LX:1310nm class; verify exact reach/media
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 159
NETWORK FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Single-mode versus multimode optical paths · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
159
Single-mode: small core, one propagation mode
Multimode: larger core, multiple modes
1000BASE-SX: short-wave multimode example
1000BASE-LX:1310nm class; verify exact reach/media
INPUT / IDENTITY
Single-mode fibre · Emitter selects wavelength
DECISION / STATE
Attenuation/dispersion limit reach
READBACK / RESULT
Receiver power must stay in supported range
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 160
NETWORK FUNDAMENTALS · DIAGNOSIS
Single-mode versus multimode optical paths · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
160
Does the observed state satisfy the contract?
Mismatch / control
Fibre jacket colour does not prove specification. LX may have documented multimode support conditions; always check exact transceiver and cable requirements.
Conforming / verification
Compare both-end wavelength, fibre type, supported distance and receive power; a fitted connector is insufficient evidence.
Single-mode: small core, one propagation mode
Inspect
Matched optic pair
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 161
NETWORK FUNDAMENTALS · VERIFICATION BRIDGE
Single-mode versus multimode optical paths · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
161
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Single-mode fibre -> Matched optic pair | Single-mode: small core, one propagation mode
Mechanism / state | Receiver power must stay in supported range | 1000BASE-LX:1310nm class; verify exact reach/media
Result / boundary | Compare both-end wavelength, fibre type, supported distance and receive power; a fitted connector is insufficient evidence. | Fibre jacket colour does not prove specification. LX may have documented multimode support conditions; always check exact transceiver and cable requirements.
Bridge: Activity 1: addressing / Activity 2: physical and VLAN evidence
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 162
ILLUSTRATIVE IMAGE + EDITABLE TECHNICAL LABELS
Copper and fibre: inspect the contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
162
Match both ends
Verify optic support, wavelength, medium, distance and received signal.
Illustration does not verify connector type or fibre performance.
Synthetic cabling illustration; use transceiver specifications and current interface evidence for real identification.

## Slide 163
20% · CURRENT CCNA V 1.1
Network Access
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
163
Network Access
Named boundaries -> runtime trace -> exact contract -> failure/control -> acceptance evidence

## Slide 164
NETWORK ACCESS · ARCHITECTURE
Access VLAN membership · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
164
Client port
Untagged ingress classified by port
VLAN database
VLAN existence and L2 scope
SVI gateway
L3 interface for off-subnet forwarding
vlan 10
switchport access vlan 10
Boundary to inspect
A VLAN must exist and be permitted on the path
show vlan brief; show interfaces switchport

## Slide 165
NETWORK ACCESS · MECHANISM
Access VLAN membership · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
165
1
Untagged frame enters access port
2
Port assigns VLAN 10
3
Switch learns source in VLAN 10
4
SVI routes off subnet
State/input
vlan 10
Observable consequence
switchport access vlan 10
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 166
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
Access VLAN membership · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
166
vlan 10
name USERS
interface Gi1/0/1
switchport mode access
switchport access vlan 10
INPUT / IDENTITY
Client port · Untagged frame enters access port
DECISION / STATE
Switch learns source in VLAN 10
READBACK / RESULT
SVI routes off subnet
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 167
NETWORK ACCESS · DIAGNOSIS
Access VLAN membership · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
167
Does the observed state satisfy the contract?
Mismatch / control
A VLAN must exist and be permitted on the path. Access VLAN configuration alone does not create a routed gateway.
Conforming / verification
show vlan brief; show interfaces switchport. Check both operational mode and assigned access VLAN.
vlan 10
Inspect
SVI gateway
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 168
NETWORK ACCESS · VERIFICATION BRIDGE
Access VLAN membership · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
168
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Client port -> SVI gateway | vlan 10
Mechanism / state | SVI routes off subnet | switchport access vlan 10
Result / boundary | show vlan brief; show interfaces switchport. Check both operational mode and assigned access VLAN. | A VLAN must exist and be permitted on the path. Access VLAN configuration alone does not create a routed gateway.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 169
NETWORK ACCESS · ARCHITECTURE
Voice and data separation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
169
IP phone
Tagged voice and control neighbor
Attached workstation
Untagged workstation data
Access switch
Data/voice VLAN classification
interface Gi1/0/2
switchport voice vlan 20
Boundary to inspect
Trusting arbitrary endpoint QoS markings can admit inflated priority
Inspect voice VLAN, LLDP/CDP phone advertisement and the separate DHCP/IP ranges for phone and workstation.

## Slide 170
NETWORK ACCESS · MECHANISM
Voice and data separation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
170
1
Phone tags voice frames
2
PC sends untagged data
3
Port maps voice VLAN 20
4
Port maps data VLAN 10
State/input
interface Gi1/0/2
Observable consequence
switchport voice vlan 20
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 171
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
Voice and data separation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
171
interface Gi1/0/2
switchport mode access
switchport access vlan 10
switchport voice vlan 20
INPUT / IDENTITY
IP phone · Phone tags voice frames
DECISION / STATE
Port maps voice VLAN 20
READBACK / RESULT
Port maps data VLAN 10
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 172
NETWORK ACCESS · DIAGNOSIS
Voice and data separation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
172
Does the observed state satisfy the contract?
Mismatch / control
Trusting arbitrary endpoint QoS markings can admit inflated priority. Voice VLAN does not authenticate the endpoint.
Conforming / verification
Inspect voice VLAN, LLDP/CDP phone advertisement and the separate DHCP/IP ranges for phone and workstation.
interface Gi1/0/2
Inspect
Access switch
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 173
NETWORK ACCESS · VERIFICATION BRIDGE
Voice and data separation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
173
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | IP phone -> Access switch | interface Gi1/0/2
Mechanism / state | Port maps data VLAN 10 | switchport voice vlan 20
Result / boundary | Inspect voice VLAN, LLDP/CDP phone advertisement and the separate DHCP/IP ranges for phone and workstation. | Trusting arbitrary endpoint QoS markings can admit inflated priority. Voice VLAN does not authenticate the endpoint.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 174
NETWORK ACCESS · ARCHITECTURE
802.1Q trunk tagging · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
174
Switch A trunk
Tags egress VLAN membership
Tag header
TPID, PCP, DEI and VID fields
Switch B trunk
Parses tag and selects VLAN
802.1Q: TPID 0x8100
VLAN 10 tag differs from VLAN 20
Boundary to inspect
A trunk can be up while required VLANs are pruned or missing
show interfaces trunk

## Slide 175
NETWORK ACCESS · MECHANISM
802.1Q trunk tagging · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
175
1
Access frame gains VLAN tag
2
Trunk carries multiplexed VLANs
3
Peer parses VID
4
Egress access port removes tag
State/input
802.1Q: TPID 0x8100
Observable consequence
VLAN 10 tag differs from VLAN 20
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 176
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
802.1Q trunk tagging · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
176
802.1Q: TPID 0x8100
PCP 3 bits; DEI 1 bit; VID 12 bits
VLAN 10 tag differs from VLAN 20
INPUT / IDENTITY
Switch A trunk · Access frame gains VLAN tag
DECISION / STATE
Peer parses VID
READBACK / RESULT
Egress access port removes tag
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 177
NETWORK ACCESS · DIAGNOSIS
802.1Q trunk tagging · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
177
Does the observed state satisfy the contract?
Mismatch / control
A trunk can be up while required VLANs are pruned or missing. Tagging is a L2 multiplexing mechanism.
Conforming / verification
show interfaces trunk. Compare allowed, active and forwarding VLAN lists on both ends.
802.1Q: TPID 0x8100
Inspect
Switch B trunk
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 178
NETWORK ACCESS · VERIFICATION BRIDGE
802.1Q trunk tagging · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
178
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Switch A trunk -> Switch B trunk | 802.1Q: TPID 0x8100
Mechanism / state | Egress access port removes tag | VLAN 10 tag differs from VLAN 20
Result / boundary | show interfaces trunk. Compare allowed, active and forwarding VLAN lists on both ends. | A trunk can be up while required VLANs are pruned or missing. Tagging is a L2 multiplexing mechanism.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 179
NETWORK ACCESS · ARCHITECTURE
Native VLAN consistency · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
179
Trunk A
Local native VLAN interpretation
Untagged frame
No VID carried on untagged data
Trunk B
Peer native VLAN interpretation
interface Gi1/0/24
switchport trunk allowed vlan 10,20,999
Boundary to inspect
Native VLAN mismatches can join unintended broadcast domains
show interfaces trunk and CDP native-VLAN warning

## Slide 180
NETWORK ACCESS · MECHANISM
Native VLAN consistency · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
180
1
Sender transmits native traffic untagged
2
Receiver assigns local native VLAN
3
Mismatch changes VLAN interpretation
4
Control traffic reports mismatch
State/input
interface Gi1/0/24
Observable consequence
switchport trunk allowed vlan 10, 20, 999
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 181
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
Native VLAN consistency · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
181
interface Gi1/0/24
switchport mode trunk
switchport trunk native vlan 999
switchport trunk allowed vlan 10,20,999
INPUT / IDENTITY
Trunk A · Sender transmits native traffic untagged
DECISION / STATE
Mismatch changes VLAN interpretation
READBACK / RESULT
Control traffic reports mismatch
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 182
NETWORK ACCESS · DIAGNOSIS
Native VLAN consistency · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
182
Does the observed state satisfy the contract?
Mismatch / control
Native VLAN mismatches can join unintended broadcast domains. Use a consistent unused native VLAN and verify policies.
Conforming / verification
show interfaces trunk and CDP native-VLAN warning. Both ends must report native VLAN 999.
interface Gi1/0/24
Inspect
Trunk B
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 183
NETWORK ACCESS · VERIFICATION BRIDGE
Native VLAN consistency · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
183
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Trunk A -> Trunk B | interface Gi1/0/24
Mechanism / state | Control traffic reports mismatch | switchport trunk allowed vlan 10, 20, 999
Result / boundary | show interfaces trunk and CDP native-VLAN warning. Both ends must report native VLAN 999. | Native VLAN mismatches can join unintended broadcast domains. Use a consistent unused native VLAN and verify policies.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 184
NETWORK ACCESS · ARCHITECTURE
Trunk negotiation boundaries · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
184
DTP-capable port
Administrative negotiation mode
Peer port
Compatible or fixed peer mode
Operational trunk
Actual resulting tagging state
interface Gi1/0/24
switchport nonegotiate
Boundary to inspect
Do not leave user-facing ports dynamically negotiable
Compare administrative/operational modes and DTP status

## Slide 185
NETWORK ACCESS · MECHANISM
Trunk negotiation boundaries · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
185
1
Administrative mode sets negotiation
2
DTP messages advertise mode
3
Compatible modes form trunk
4
Nonnegotiating trunk is explicitly fixed
State/input
interface Gi1/0/24
Observable consequence
switchport nonegotiate
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 186
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
Trunk negotiation boundaries · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
186
interface Gi1/0/24
switchport mode trunk
switchport nonegotiate
INPUT / IDENTITY
DTP-capable port · Administrative mode sets negotiation
DECISION / STATE
Compatible modes form trunk
READBACK / RESULT
Nonnegotiating trunk is explicitly fixed
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 187
NETWORK ACCESS · DIAGNOSIS
Trunk negotiation boundaries · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
187
Does the observed state satisfy the contract?
Mismatch / control
Do not leave user-facing ports dynamically negotiable. nonegotiate disables DTP sending, not 802.1Q tagging.
Conforming / verification
Compare administrative/operational modes and DTP status. An explicitly configured trunk must still have a compatible peer.
interface Gi1/0/24
Inspect
Operational trunk
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 188
NETWORK ACCESS · VERIFICATION BRIDGE
Trunk negotiation boundaries · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
188
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | DTP-capable port -> Operational trunk | interface Gi1/0/24
Mechanism / state | Nonnegotiating trunk is explicitly fixed | switchport nonegotiate
Result / boundary | Compare administrative/operational modes and DTP status. An explicitly configured trunk must still have a compatible peer. | Do not leave user-facing ports dynamically negotiable. nonegotiate disables DTP sending, not 802.1Q tagging.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 189
NETWORK ACCESS · ARCHITECTURE
Router-on-a-stick paths · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
189
VLAN 10 client
Original subnet and gateway
Router subinterface
Tag-specific routed interface
VLAN 20 client
Destination subnet and gateway
interface Gi0/0.10
ip address 10.10.10.1 255.255.255.0
Boundary to inspect
Parent interface must be active and switch trunk must allow VLAN 10
show ip interface brief; ping each subinterface gateway; verify tags and route entries.

## Slide 190
NETWORK ACCESS · MECHANISM
Router-on-a-stick paths · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
190
1
Tagged frame reaches router
2
Subinterface matches VLAN ID
3
Router selects destination subnet
4
Frame exits with destination VLAN tag
State/input
interface Gi0/0.10
Observable consequence
ip address 10.10.10.1 255.255.255.0
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 191
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
Router-on-a-stick paths · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
191
interface Gi0/0.10
encapsulation dot1Q 10
ip address 10.10.10.1 255.255.255.0
INPUT / IDENTITY
VLAN 10 client · Tagged frame reaches router
DECISION / STATE
Router selects destination subnet
READBACK / RESULT
Frame exits with destination VLAN tag
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 192
NETWORK ACCESS · DIAGNOSIS
Router-on-a-stick paths · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
192
Does the observed state satisfy the contract?
Mismatch / control
Parent interface must be active and switch trunk must allow VLAN 10. Incorrect encapsulation binds gateway to the wrong VLAN.
Conforming / verification
show ip interface brief; ping each subinterface gateway; verify tags and route entries.
interface Gi0/0.10
Inspect
VLAN 20 client
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 193
NETWORK ACCESS · VERIFICATION BRIDGE
Router-on-a-stick paths · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
193
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | VLAN 10 client -> VLAN 20 client | interface Gi0/0.10
Mechanism / state | Frame exits with destination VLAN tag | ip address 10.10.10.1 255.255.255.0
Result / boundary | show ip interface brief; ping each subinterface gateway; verify tags and route entries. | Parent interface must be active and switch trunk must allow VLAN 10. Incorrect encapsulation binds gateway to the wrong VLAN.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 194
NETWORK ACCESS · ARCHITECTURE
Multilayer SVI routing · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
194
Access VLAN
L2 broadcast domain
SVI interface
VLAN-bound logical L3 interface
Routed uplink
L3 transit interface and next hop
ip routing
no shutdown
Boundary to inspect
SVI operational state depends on VLAN and active forwarding members
show interfaces vlan 10; show ip route connected

## Slide 195
NETWORK ACCESS · MECHANISM
Multilayer SVI routing · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
195
1
VLAN exists
2
Active member supports SVI state
3
SVI receives gateway traffic
4
ip routing enables inter-VLAN forwarding
State/input
ip routing
Observable consequence
no shutdown
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 196
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
Multilayer SVI routing · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
196
ip routing
interface Vlan 10
ip address 10.10.10.1 255.255.255.0
no shutdown
INPUT / IDENTITY
Access VLAN · VLAN exists
DECISION / STATE
SVI receives gateway traffic
READBACK / RESULT
ip routing enables inter-VLAN forwarding
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 197
NETWORK ACCESS · DIAGNOSIS
Multilayer SVI routing · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
197
Does the observed state satisfy the contract?
Mismatch / control
SVI operational state depends on VLAN and active forwarding members. A configured address is insufficient.
Conforming / verification
show interfaces vlan 10; show ip route connected. Confirm SVI up/up and routes for both VLANs.
ip routing
Inspect
Routed uplink
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 198
NETWORK ACCESS · VERIFICATION BRIDGE
Multilayer SVI routing · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
198
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Access VLAN -> Routed uplink | ip routing
Mechanism / state | ip routing enables inter-VLAN forwarding | no shutdown
Result / boundary | show interfaces vlan 10; show ip route connected. Confirm SVI up/up and routes for both VLANs. | SVI operational state depends on VLAN and active forwarding members. A configured address is insufficient.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 199
NETWORK ACCESS · ARCHITECTURE
CDP neighbor evidence · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
199
Local Cisco device
Advertises local identity/port
CDP multicast
Link-local discovery transport
Cisco neighbor
Caches peer identity/port/platform
show cdp neighbors detail
Port ID: Gi1/0/23
Boundary to inspect
CDP reveals topology and should be constrained on untrusted ports
Cross-check local port, peer port and actual cabling

## Slide 200
NETWORK ACCESS · MECHANISM
CDP neighbor evidence · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
200
1
Device advertises identity
2
Neighbor caches port/platform
3
Entry ages without refresh
4
Operator maps physical link
State/input
show cdp neighbors detail
Observable consequence
Port ID: Gi1/0/23
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 201
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
CDP neighbor evidence · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
201
show cdp neighbors detail
Device ID: SW2
Interface: Gi1/0/24
Port ID: Gi1/0/23
INPUT / IDENTITY
Local Cisco device · Device advertises identity
DECISION / STATE
Entry ages without refresh
READBACK / RESULT
Operator maps physical link
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 202
NETWORK ACCESS · DIAGNOSIS
CDP neighbor evidence · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
202
Does the observed state satisfy the contract?
Mismatch / control
CDP reveals topology and should be constrained on untrusted ports. Management address can differ from data-path address.
Conforming / verification
Cross-check local port, peer port and actual cabling. Neighbor discovery does not prove routed application reachability.
show cdp neighbors detail
Inspect
Cisco neighbor
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 203
NETWORK ACCESS · VERIFICATION BRIDGE
CDP neighbor evidence · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
203
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Local Cisco device -> Cisco neighbor | show cdp neighbors detail
Mechanism / state | Operator maps physical link | Port ID: Gi1/0/23
Result / boundary | Cross-check local port, peer port and actual cabling. Neighbor discovery does not prove routed application reachability. | CDP reveals topology and should be constrained on untrusted ports. Management address can differ from data-path address.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 204
NETWORK ACCESS · ARCHITECTURE
LLDP interoperable discovery · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
204
Local switch
Advertises chassis and port
LLDP TLVs
Mandatory/optional identity/capability fields
Non-Cisco peer
Peer identity and expiry state
lldp run
Chassis ID; Port ID; TTL; System Name
Boundary to inspect
Absence may mean LLDP is disabled rather than cable failure
Compare advertised capabilities and local/remote port IDs; use interface state as independent evidence.

## Slide 205
NETWORK ACCESS · MECHANISM
LLDP interoperable discovery · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
205
1
Chassis and port TLVs identify peer
2
TTL controls cache lifetime
3
Optional TLVs describe capabilities
4
Receiver builds neighbor view
State/input
lldp run
Observable consequence
Chassis ID; Port ID; TTL; System Name
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 206
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
LLDP interoperable discovery · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
206
lldp run
show lldp neighbors detail
Chassis ID; Port ID; TTL; System Name
INPUT / IDENTITY
Local switch · Chassis and port TLVs identify peer
DECISION / STATE
Optional TLVs describe capabilities
READBACK / RESULT
Receiver builds neighbor view
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 207
NETWORK ACCESS · DIAGNOSIS
LLDP interoperable discovery · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
207
Does the observed state satisfy the contract?
Mismatch / control
Absence may mean LLDP is disabled rather than cable failure. LLDP uses link-local Ethernet scope.
Conforming / verification
Compare advertised capabilities and local/remote port IDs; use interface state as independent evidence.
lldp run
Inspect
Non-Cisco peer
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 208
NETWORK ACCESS · VERIFICATION BRIDGE
LLDP interoperable discovery · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
208
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Local switch -> Non-Cisco peer | lldp run
Mechanism / state | Receiver builds neighbor view | Chassis ID; Port ID; TTL; System Name
Result / boundary | Compare advertised capabilities and local/remote port IDs; use interface state as independent evidence. | Absence may mean LLDP is disabled rather than cable failure. LLDP uses link-local Ethernet scope.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 209
NETWORK ACCESS · ARCHITECTURE
LACP channel negotiation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
209
Member interfaces
Physical bundle candidates
LACP actor/partner
System ID, key and negotiation
Port-channel
Logical forwarding interface
interface range Gi1/0/1 - 2
switchport mode trunk
Boundary to inspect
Passive/passive does not initiate a LACP channel
show etherchannel summary

## Slide 210
NETWORK ACCESS · MECHANISM
LACP channel negotiation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
210
1
Active side sends LACPDU
2
Partner agrees system/key
3
Compatible links bundle
4
Hash places flows on members
State/input
interface range Gi1/0/1 - 2
Observable consequence
switchport mode trunk
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 211
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
LACP channel negotiation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
211
interface range Gi1/0/1 - 2
channel-group 1 mode active
interface Port-channel1
switchport mode trunk
INPUT / IDENTITY
Member interfaces · Active side sends LACPDU
DECISION / STATE
Compatible links bundle
READBACK / RESULT
Hash places flows on members
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 212
NETWORK ACCESS · DIAGNOSIS
LACP channel negotiation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
212
Does the observed state satisfy the contract?
Mismatch / control
Passive/passive does not initiate a LACP channel. Member speed, duplex and trunk parameters must be compatible.
Conforming / verification
show etherchannel summary. Expect Po 1(SU) and bundled members marked P; investigate I or suspended members.
interface range Gi1/0/1 - 2
Inspect
Port-channel
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 213
NETWORK ACCESS · VERIFICATION BRIDGE
LACP channel negotiation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
213
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Member interfaces -> Port-channel | interface range Gi1/0/1 - 2
Mechanism / state | Hash places flows on members | switchport mode trunk
Result / boundary | show etherchannel summary. Expect Po 1(SU) and bundled members marked P; investigate I or suspended members. | Passive/passive does not initiate a LACP channel. Member speed, duplex and trunk parameters must be compatible.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 214
NETWORK ACCESS · ARCHITECTURE
EtherChannel load distribution · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
214
Flow tuple
Fields that identify traffic flow
Hash function
Maps fields to member index
Member link
Carries selected flow's packets
port-channel load-balance src-dst-ip
Flow B -> member 2
Boundary to inspect
Two 1-Gb/s members do not make one TCP flow 2 Gb/s
Compare per-member counters across multiple source/destination pairs and interpret aggregate capacity separately.

## Slide 215
NETWORK ACCESS · MECHANISM
EtherChannel load distribution · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
215
1
Switch extracts configured fields
2
Hash maps flow to member
3
Packets in flow stay ordered
4
Multiple flows can use different members
State/input
port-channel load-balance src-dst-ip
Observable consequence
Flow B -> member 2
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 216
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
EtherChannel load distribution · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
216
port-channel load-balance src-dst-ip
Flow A -> member 1
Flow B -> member 2
INPUT / IDENTITY
Flow tuple · Switch extracts configured fields
DECISION / STATE
Packets in flow stay ordered
READBACK / RESULT
Multiple flows can use different members
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 217
NETWORK ACCESS · DIAGNOSIS
EtherChannel load distribution · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
217
Does the observed state satisfy the contract?
Mismatch / control
Two 1-Gb/s members do not make one TCP flow 2 Gb/s. Hash collisions can skew utilization.
Conforming / verification
Compare per-member counters across multiple source/destination pairs and interpret aggregate capacity separately.
port-channel load-balance src-dst-ip
Inspect
Member link
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 218
NETWORK ACCESS · VERIFICATION BRIDGE
EtherChannel load distribution · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
218
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Flow tuple -> Member link | port-channel load-balance src-dst-ip
Mechanism / state | Multiple flows can use different members | Flow B -> member 2
Result / boundary | Compare per-member counters across multiple source/destination pairs and interpret aggregate capacity separately. | Two 1-Gb/s members do not make one TCP flow 2 Gb/s. Hash collisions can skew utilization.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 219
NETWORK ACCESS · ARCHITECTURE
STP root bridge election · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
219
Bridge priority
First bridge-ID election field
System ID extension
Per-VLAN bridge-ID extension
Bridge MAC
Tie-break identifier for equal priority
VLAN10: SW1 priority 24576
SW1 becomes root with lower bridge ID
Boundary to inspect
Unplanned root location can produce poor paths
show spanning-tree vlan 10

## Slide 220
NETWORK ACCESS · MECHANISM
STP root bridge election · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
220
1
Lowest bridge ID wins
2
Priority compares first
3
VLAN extension contributes ID
4
Lowest MAC breaks equal-priority tie
State/input
VLAN10: SW1 priority 24576
Observable consequence
SW1 becomes root with lower bridge ID
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 221
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
STP root bridge election · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
221
VLAN10: SW1 priority 24576
SW2 priority 32768
SW1 becomes root with lower bridge ID
INPUT / IDENTITY
Bridge priority · Lowest bridge ID wins
DECISION / STATE
VLAN extension contributes ID
READBACK / RESULT
Lowest MAC breaks equal-priority tie
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 222
NETWORK ACCESS · DIAGNOSIS
STP root bridge election · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
222
Does the observed state satisfy the contract?
Mismatch / control
Unplanned root location can produce poor paths. Changing priority influences topology and can trigger reconvergence.
Conforming / verification
show spanning-tree vlan 10. Root ID equals Bridge ID on root; compare priority plus VLAN system-ID extension.
VLAN10: SW1 priority 24576
Inspect
Bridge MAC
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 223
NETWORK ACCESS · VERIFICATION BRIDGE
STP root bridge election · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
223
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Bridge priority -> Bridge MAC | VLAN10: SW1 priority 24576
Mechanism / state | Lowest MAC breaks equal-priority tie | SW1 becomes root with lower bridge ID
Result / boundary | show spanning-tree vlan 10. Root ID equals Bridge ID on root; compare priority plus VLAN system-ID extension. | Unplanned root location can produce poor paths. Changing priority influences topology and can trigger reconvergence.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 224
NETWORK ACCESS · ARCHITECTURE
STP root and designated ports · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
224
Root bridge
Lowest bridge ID and cost root
Non-root switch
Chooses its root port toward root
Shared segment
Elects segment's designated transmitter
SW2 root cost via Gi1/0/1 = 4
Gi1/0/1 -> root port
Boundary to inspect
Root port selection uses accumulated path cost, not merely local port number
Annotate each link cost; show spanning-tree reveals root/designated/alternate roles and forwarding state.

## Slide 225
NETWORK ACCESS · MECHANISM
STP root and designated ports · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
225
1
Choose lowest root-path cost
2
Tie compares sender bridge ID
3
Next tie compares sender port ID
4
Best transmitter becomes designated
State/input
SW2 root cost via Gi1/0/1 = 4
Observable consequence
Gi1/0/1 -> root port
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 226
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
STP root and designated ports · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
226
SW2 root cost via Gi1/0/1 = 4
via Gi1/0/2 = 8
Gi1/0/1 -> root port
INPUT / IDENTITY
Root bridge · Choose lowest root-path cost
DECISION / STATE
Next tie compares sender port ID
READBACK / RESULT
Best transmitter becomes designated
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 227
NETWORK ACCESS · DIAGNOSIS
STP root and designated ports · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
227
Does the observed state satisfy the contract?
Mismatch / control
Root port selection uses accumulated path cost, not merely local port number. Alternate ports block loops.
Conforming / verification
Annotate each link cost; show spanning-tree reveals root/designated/alternate roles and forwarding state.
SW2 root cost via Gi1/0/1 = 4
Inspect
Shared segment
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 228
NETWORK ACCESS · VERIFICATION BRIDGE
STP root and designated ports · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
228
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Root bridge -> Shared segment | SW2 root cost via Gi1/0/1 = 4
Mechanism / state | Best transmitter becomes designated | Gi1/0/1 -> root port
Result / boundary | Annotate each link cost; show spanning-tree reveals root/designated/alternate roles and forwarding state. | Root port selection uses accumulated path cost, not merely local port number. Alternate ports block loops.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 229
NETWORK ACCESS · ARCHITECTURE
Rapid PVST convergence · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
229
Root port
Lowest-cost path to root
Alternate port
Ready alternative path
Point-to-point link
Rapid proposal/agreement boundary
RSTP roles: root, designated, alternate
Per-VLAN tree: Rapid PVST+
Boundary to inspect
Shared links and legacy STP neighbors can limit rapid convergence
show spanning-tree summary and vlan detail; trace role changes after a controlled uplink interruption.

## Slide 230
NETWORK ACCESS · MECHANISM
Rapid PVST convergence · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
230
1
Proposal advertises superior tree
2
Peer synchronizes other ports
3
Agreement permits rapid forwarding
4
Alternate replaces failed root path
State/input
RSTP roles: root, designated, alternate
Observable consequence
Per-VLAN tree: Rapid PVST+
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 231
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
Rapid PVST convergence · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
231
RSTP roles: root, designated, alternate
States: discarding, learning, forwarding
Per-VLAN tree: Rapid PVST+
INPUT / IDENTITY
Root port · Proposal advertises superior tree
DECISION / STATE
Agreement permits rapid forwarding
READBACK / RESULT
Alternate replaces failed root path
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 232
NETWORK ACCESS · DIAGNOSIS
Rapid PVST convergence · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
232
Does the observed state satisfy the contract?
Mismatch / control
Shared links and legacy STP neighbors can limit rapid convergence. Edge designation must be used only for endpoint-facing ports.
Conforming / verification
show spanning-tree summary and vlan detail; trace role changes after a controlled uplink interruption.
RSTP roles: root, designated, alternate
Inspect
Point-to-point link
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 233
NETWORK ACCESS · VERIFICATION BRIDGE
Rapid PVST convergence · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
233
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Root port -> Point-to-point link | RSTP roles: root, designated, alternate
Mechanism / state | Alternate replaces failed root path | Per-VLAN tree: Rapid PVST+
Result / boundary | show spanning-tree summary and vlan detail; trace role changes after a controlled uplink interruption. | Shared links and legacy STP neighbors can limit rapid convergence. Edge designation must be used only for endpoint-facing ports.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 234
NETWORK ACCESS · ARCHITECTURE
PortFast and BPDU guard · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
234
Endpoint port
Port intended for non-bridging host
Edge forwarding state
Immediate edge forwarding behavior
BPDU detector
Unexpected BPDU admission control
interface Gi1/0/10
spanning-tree bpduguard enable
Boundary to inspect
PortFast does not disable STP
show interfaces status err-disabled; show logging

## Slide 235
NETWORK ACCESS · MECHANISM
PortFast and BPDU guard · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
235
1
Edge port forwards immediately
2
BPDU arrives unexpectedly
3
Guard err-disables port
4
Recovery follows corrected attachment
State/input
interface Gi1/0/10
Observable consequence
spanning-tree bpduguard enable
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 236
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
PortFast and BPDU guard · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
236
interface Gi1/0/10
spanning-tree portfast
spanning-tree bpduguard enable
INPUT / IDENTITY
Endpoint port · Edge port forwards immediately
DECISION / STATE
Guard err-disables port
READBACK / RESULT
Recovery follows corrected attachment
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 237
NETWORK ACCESS · DIAGNOSIS
PortFast and BPDU guard · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
237
Does the observed state satisfy the contract?
Mismatch / control
PortFast does not disable STP. BPDU guard protects intended edge ports; switch attachment must be corrected before recovery.
Conforming / verification
show interfaces status err-disabled; show logging. Identify bpduguard cause and restore only after removing the unintended bridge.
interface Gi1/0/10
Inspect
BPDU detector
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 238
NETWORK ACCESS · VERIFICATION BRIDGE
PortFast and BPDU guard · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
238
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Endpoint port -> BPDU detector | interface Gi1/0/10
Mechanism / state | Recovery follows corrected attachment | spanning-tree bpduguard enable
Result / boundary | show interfaces status err-disabled; show logging. Identify bpduguard cause and restore only after removing the unintended bridge. | PortFast does not disable STP. BPDU guard protects intended edge ports; switch attachment must be corrected before recovery.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 239
NETWORK ACCESS · ARCHITECTURE
Root guard boundary · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
239
Designated access link
Expected designated downstream link
Superior BPDU
Claim of unauthorized superior root
Root-inconsistent state
Protective port role/state
interface Gi1/0/20
show spanning-tree inconsistentports
Boundary to inspect
Do not place root guard where the root port is legitimately expected
Verify root-inconsistent reason and root bridge remains authorized

## Slide 240
NETWORK ACCESS · MECHANISM
Root guard boundary · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
240
1
Downstream BPDU claims better root
2
Root guard rejects takeover
3
Port becomes root-inconsistent
4
Port recovers after superior BPDUs cease
State/input
interface Gi1/0/20
Observable consequence
show spanning-tree inconsistentports
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 241
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
Root guard boundary · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
241
interface Gi1/0/20
spanning-tree guard root
show spanning-tree inconsistentports
INPUT / IDENTITY
Designated access link · Downstream BPDU claims better root
DECISION / STATE
Port becomes root-inconsistent
READBACK / RESULT
Port recovers after superior BPDUs cease
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 242
NETWORK ACCESS · DIAGNOSIS
Root guard boundary · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
242
Does the observed state satisfy the contract?
Mismatch / control
Do not place root guard where the root port is legitimately expected. It preserves root ownership, not every kind of loop.
Conforming / verification
Verify root-inconsistent reason and root bridge remains authorized. Recovery is automatic after superior BPDUs stop.
interface Gi1/0/20
Inspect
Root-inconsistent state
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 243
NETWORK ACCESS · VERIFICATION BRIDGE
Root guard boundary · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
243
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Designated access link -> Root-inconsistent state | interface Gi1/0/20
Mechanism / state | Port recovers after superior BPDUs cease | show spanning-tree inconsistentports
Result / boundary | Verify root-inconsistent reason and root bridge remains authorized. Recovery is automatic after superior BPDUs stop. | Do not place root guard where the root port is legitimately expected. It preserves root ownership, not every kind of loop.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 244
NETWORK ACCESS · ARCHITECTURE
Loop guard and BPDU filter · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
244
Non-designated port
Root/alternate path depends on BPDUs
BPDU continuity
Periodic tree-control evidence
Loop-inconsistent state
Guarded state when evidence disappears
interface Gi1/0/24
BPDU filter suppresses BPDUs: use cautiously
Boundary to inspect
Interface-level BPDU filtering can effectively remove STP protection and cause loops
show spanning-tree inconsistentports

## Slide 245
NETWORK ACCESS · MECHANISM
Loop guard and BPDU filter · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
245
1
Expected BPDUs disappear
2
Loop guard prevents unsafe forwarding
3
Port enters loop-inconsistent
4
BPDU reception permits recovery
State/input
interface Gi1/0/24
Observable consequence
BPDU filter suppresses BPDUs: use cautiously
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 246
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
Loop guard and BPDU filter · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
246
interface Gi1/0/24
spanning-tree guard loop
BPDU filter suppresses BPDUs: use cautiously
INPUT / IDENTITY
Non-designated port · Expected BPDUs disappear
DECISION / STATE
Port enters loop-inconsistent
READBACK / RESULT
BPDU reception permits recovery
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 247
NETWORK ACCESS · DIAGNOSIS
Loop guard and BPDU filter · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
247
Does the observed state satisfy the contract?
Mismatch / control
Interface-level BPDU filtering can effectively remove STP protection and cause loops. Loop guard addresses missing BPDUs, not rogue superior roots.
Conforming / verification
show spanning-tree inconsistentports. Distinguish loop-inconsistent from root-inconsistent and bpduguard err-disable.
interface Gi1/0/24
Inspect
Loop-inconsistent state
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 248
NETWORK ACCESS · VERIFICATION BRIDGE
Loop guard and BPDU filter · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
248
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Non-designated port -> Loop-inconsistent state | interface Gi1/0/24
Mechanism / state | BPDU reception permits recovery | BPDU filter suppresses BPDUs: use cautiously
Result / boundary | show spanning-tree inconsistentports. Distinguish loop-inconsistent from root-inconsistent and bpduguard err-disable. | Interface-level BPDU filtering can effectively remove STP protection and cause loops. Loop guard addresses missing BPDUs, not rogue superior roots.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 249
NETWORK ACCESS · ARCHITECTURE
AP modes and WLAN transport · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
249
Local-mode AP
Centrally switched client data path
FlexConnect AP
Optional locally switched client path
WLC policy
WLAN configuration and control owner
Local mode: client data -> WLC
Monitor mode: no client-serving WLAN
Boundary to inspect
AP mode affects data path and operation during WAN loss
Identify AP mode and switching policy; compare client gateway location with observed packet path.

## Slide 250
NETWORK ACCESS · MECHANISM
AP modes and WLAN transport · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
250
1
Local AP tunnels central data
2
FlexConnect can switch locally
3
WLC manages WLAN policy
4
Monitor-mode AP inspects RF
State/input
Local mode: client data -> WLC
Observable consequence
Monitor mode: no client-serving WLAN
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 251
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
AP modes and WLAN transport · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
251
Local mode: client data -> WLC
FlexConnect local: client data -> local VLAN
Monitor mode: no client-serving WLAN
INPUT / IDENTITY
Local-mode AP · Local AP tunnels central data
DECISION / STATE
WLC manages WLAN policy
READBACK / RESULT
Monitor-mode AP inspects RF
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 252
NETWORK ACCESS · DIAGNOSIS
AP modes and WLAN transport · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
252
Does the observed state satisfy the contract?
Mismatch / control
AP mode affects data path and operation during WAN loss. A control connection does not guarantee correct client VLAN.
Conforming / verification
Identify AP mode and switching policy; compare client gateway location with observed packet path.
Local mode: client data -> WLC
Inspect
WLC policy
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 253
NETWORK ACCESS · VERIFICATION BRIDGE
AP modes and WLAN transport · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
253
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Local-mode AP -> WLC policy | Local mode: client data -> WLC
Mechanism / state | Monitor-mode AP inspects RF | Monitor mode: no client-serving WLAN
Result / boundary | Identify AP mode and switching policy; compare client gateway location with observed packet path. | AP mode affects data path and operation during WAN loss. A control connection does not guarantee correct client VLAN.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 254
NETWORK ACCESS · ARCHITECTURE
WLAN GUI policy evidence · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
254
SSID object
SSID and authentication settings
Policy profile
VLAN, QoS and forwarding settings
VLAN/security mapping
Associates WLAN with policy profile
Catalyst 9800 objects:
Policy Tag WLAN->Profile
Boundary to inspect
A visually correct SSID can map to a wrong policy/VLAN
Read WLAN, policy profile and AP tag together

## Slide 255
NETWORK ACCESS · MECHANISM
WLAN GUI policy evidence · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
255
1
WLAN defines SSID/security
2
Policy profile defines network policy
3
Policy tag associates WLAN and profile
4
AP applies assigned tag
State/input
Catalyst 9800 objects:
Observable consequence
Policy Tag WLAN->Profile
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 256
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
WLAN GUI policy evidence · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
256
Catalyst 9800 objects:
WLAN ID + SSID
Policy Profile VLAN 20
Policy Tag WLAN->Profile
INPUT / IDENTITY
SSID object · WLAN defines SSID/security
DECISION / STATE
Policy tag associates WLAN and profile
READBACK / RESULT
AP applies assigned tag
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 257
NETWORK ACCESS · DIAGNOSIS
WLAN GUI policy evidence · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
257
Does the observed state satisfy the contract?
Mismatch / control
A visually correct SSID can map to a wrong policy/VLAN. Treat this as an object relationship, not a sequence of GUI clicks.
Conforming / verification
Read WLAN, policy profile and AP tag together. Client should receive VLAN 20 addressing and expected authorization.
Catalyst 9800 objects:
Inspect
VLAN/security mapping
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 258
NETWORK ACCESS · VERIFICATION BRIDGE
WLAN GUI policy evidence · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
258
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | SSID object -> VLAN/security mapping | Catalyst 9800 objects:
Mechanism / state | AP applies assigned tag | Policy Tag WLAN->Profile
Result / boundary | Read WLAN, policy profile and AP tag together. Client should receive VLAN 20 addressing and expected authorization. | A visually correct SSID can map to a wrong policy/VLAN. Treat this as an object relationship, not a sequence of GUI clicks.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 259
NETWORK ACCESS · ARCHITECTURE
Wireless management reachability · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
259
Administrator
Authenticated management initiator
AP/WLC management
Device policy/configuration endpoint
Cloud dashboard
Remote visibility and control endpoint
HTTPS TCP 443; SSH TCP 22
Cloud: outbound secure management connection
Boundary to inspect
Cloud visibility depends on Internet and management connectivity
Identify management transport, role permission and audit evidence

## Slide 260
NETWORK ACCESS · MECHANISM
Wireless management reachability · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
260
1
Admin uses HTTPS/SSH
2
Device verifies credential
3
Management changes persistent policy
4
Audit records actor and change
State/input
HTTPS TCP 443; SSH TCP 22
Observable consequence
Cloud: outbound secure management connection
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 261
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
Wireless management reachability · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
261
HTTPS TCP 443; SSH TCP 22
Console: local out-of-band
Cloud: outbound secure management connection
INPUT / IDENTITY
Administrator · Admin uses HTTPS/SSH
DECISION / STATE
Management changes persistent policy
READBACK / RESULT
Audit records actor and change
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 262
NETWORK ACCESS · DIAGNOSIS
Wireless management reachability · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
262
Does the observed state satisfy the contract?
Mismatch / control
Cloud visibility depends on Internet and management connectivity. Telnet/HTTP expose management traffic; use authenticated encrypted methods.
Conforming / verification
Identify management transport, role permission and audit evidence. Read back the intended WLAN policy after a change.
HTTPS TCP 443; SSH TCP 22
Inspect
Cloud dashboard
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 263
NETWORK ACCESS · VERIFICATION BRIDGE
Wireless management reachability · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
263
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Administrator -> Cloud dashboard | HTTPS TCP 443; SSH TCP 22
Mechanism / state | Audit records actor and change | Cloud: outbound secure management connection
Result / boundary | Identify management transport, role permission and audit evidence. Read back the intended WLAN policy after a change. | Cloud visibility depends on Internet and management connectivity. Telnet/HTTP expose management traffic; use authenticated encrypted methods.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 264
NETWORK ACCESS · ARCHITECTURE
Layer 3 LACP port-channel · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
264
Routed switch interfaces
Compatible no-switchport members
LACP bundle
Negotiated logical routed link
Peer router
Matching LACP and subnet endpoint
interface range Gi1/0/1 - 2
ip address 10.0.0.1 255.255.255.252
Boundary to inspect
Do not mix L2 and L3 member configuration
show etherchannel summary expects routed R flag and bundled P members; connected subnet attaches to Port-channel 1.

## Slide 265
NETWORK ACCESS · MECHANISM
Layer 3 LACP port-channel · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
265
1
Physical members enter routed mode
2
LACP negotiates bundle
3
Port-channel owns L3 address
4
Routing sees one logical link
State/input
interface range Gi1/0/1 - 2
Observable consequence
ip address 10.0.0.1 255.255.255.252
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 266
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
Layer 3 LACP port-channel · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
266
interface range Gi1/0/1 - 2
no switchport
channel-group 1 mode active
interface Port-channel1
no switchport
ip address 10.0.0.1 255.255.255.252
INPUT / IDENTITY
Routed switch interfaces · Physical members enter routed mode
DECISION / STATE
Port-channel owns L3 address
READBACK / RESULT
Routing sees one logical link
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 267
NETWORK ACCESS · DIAGNOSIS
Layer 3 LACP port-channel · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
267
Does the observed state satisfy the contract?
Mismatch / control
Do not mix L2 and L3 member configuration. Address the logical port-channel, not each bundled member independently.
Conforming / verification
show etherchannel summary expects routed R flag and bundled P members; connected subnet attaches to Port-channel 1.
interface range Gi1/0/1 - 2
Inspect
Peer router
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 268
NETWORK ACCESS · VERIFICATION BRIDGE
Layer 3 LACP port-channel · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
268
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Routed switch interfaces -> Peer router | interface range Gi1/0/1 - 2
Mechanism / state | Routing sees one logical link | ip address 10.0.0.1 255.255.255.252
Result / boundary | show etherchannel summary expects routed R flag and bundled P members; connected subnet attaches to Port-channel 1. | Do not mix L2 and L3 member configuration. Address the logical port-channel, not each bundled member independently.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 269
NETWORK ACCESS · ARCHITECTURE
Default and normal-range VLAN contracts · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
269
Default VLAN 1
Initial default switched access domain
Normal VLAN database
Normal-ID configuration and existence
Access-port membership
Ingress classification into selected VLAN
Normal range VLAN 1-1005
show vlan brief
Boundary to inspect
Do not confuse default VLAN 1 with an arbitrary native VLAN on a trunk
Read VLAN existence, access membership and operational trunk lists; explicitly distinguish default, access, native and management VLAN roles.

## Slide 270
NETWORK ACCESS · MECHANISM
Default and normal-range VLAN contracts · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
270
1
Default access membership starts in VLAN 1
2
Normal-range VLAN IDs are allocated
3
Port binds selected VLAN
4
Trunk forwards only allowed active VLANs
State/input
Normal range VLAN 1-1005
Observable consequence
show vlan brief
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 271
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
Default and normal-range VLAN contracts · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
271
Normal range VLAN 1-1005
VLAN 1002-1005 reserved legacy default VLANs
User example VLAN 10
show vlan brief
INPUT / IDENTITY
Default VLAN 1 · Default access membership starts in VLAN 1
DECISION / STATE
Port binds selected VLAN
READBACK / RESULT
Trunk forwards only allowed active VLANs
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 272
NETWORK ACCESS · DIAGNOSIS
Default and normal-range VLAN contracts · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
272
Does the observed state satisfy the contract?
Mismatch / control
Do not confuse default VLAN 1 with an arbitrary native VLAN on a trunk. Reserved legacy VLANs are not ordinary user allocations.
Conforming / verification
Read VLAN existence, access membership and operational trunk lists; explicitly distinguish default, access, native and management VLAN roles.
Normal range VLAN 1-1005
Inspect
Access-port membership
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 273
NETWORK ACCESS · VERIFICATION BRIDGE
Default and normal-range VLAN contracts · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
273
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Default VLAN 1 -> Access-port membership | Normal range VLAN 1-1005
Mechanism / state | Trunk forwards only allowed active VLANs | show vlan brief
Result / boundary | Read VLAN existence, access membership and operational trunk lists; explicitly distinguish default, access, native and management VLAN roles. | Do not confuse default VLAN 1 with an arbitrary native VLAN on a trunk. Reserved legacy VLANs are not ordinary user allocations.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 274
NETWORK ACCESS · ARCHITECTURE
AP and WLC physical attachments · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
274
Local-mode AP switchport
Management and centralized-tunnel endpoint
FlexConnect AP switchport
Management plus locally switched VLAN boundary
WLC switch attachment
Management/client VLAN attachment to wired network
Local-mode AP: commonly access management VLAN
Controller VLAN mapping must match network
Boundary to inspect
Do not apply one universal access/trunk rule to every AP mode
Compare AP mode, management addressing, trunk allowed/native VLANs, WLC attachment and client gateway location.

## Slide 275
NETWORK ACCESS · MECHANISM
AP and WLC physical attachments · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
275
1
AP management establishes IP reachability
2
Local-mode client data uses tunnel
3
Local switching emits VLAN-tagged client data
4
WLC uplinks carry mapped client/management networks
State/input
Local-mode AP: commonly access management VLAN
Observable consequence
Controller VLAN mapping must match network
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 276
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
AP and WLC physical attachments · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
276
Local-mode AP: commonly access management VLAN
FlexConnect local-switch AP: trunk for client VLANs
WLC: configured trunk/LAG attachment per platform
Controller VLAN mapping must match network
INPUT / IDENTITY
Local-mode AP switchport · AP management establishes IP reachability
DECISION / STATE
Local switching emits VLAN-tagged client data
READBACK / RESULT
WLC uplinks carry mapped client/management networks
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 277
NETWORK ACCESS · DIAGNOSIS
AP and WLC physical attachments · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
277
Does the observed state satisfy the contract?
Mismatch / control
Do not apply one universal access/trunk rule to every AP mode. WLC aggregation and AP tag behavior depend on platform and switching design.
Conforming / verification
Compare AP mode, management addressing, trunk allowed/native VLANs, WLC attachment and client gateway location.
Local-mode AP: commonly access management VLAN
Inspect
WLC switch attachment
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 278
NETWORK ACCESS · VERIFICATION BRIDGE
AP and WLC physical attachments · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
278
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Local-mode AP switchport -> WLC switch attachment | Local-mode AP: commonly access management VLAN
Mechanism / state | WLC uplinks carry mapped client/management networks | Controller VLAN mapping must match network
Result / boundary | Compare AP mode, management addressing, trunk allowed/native VLANs, WLC attachment and client gateway location. | Do not apply one universal access/trunk rule to every AP mode. WLC aggregation and AP tag behavior depend on platform and switching design.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 279
NETWORK ACCESS · ARCHITECTURE
WLAN QoS and advanced-policy evidence · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
279
WLAN security profile
Authentication, cipher and SSID contract
Policy QoS attributes
Class/marking/forwarding policy contract
Advanced client behavior
Platform-specific client session/roaming controls
Inspect actual WLC fields:
Advanced/session/roaming controls depend on release
Boundary to inspect
GUI labels and feature availability vary across WLC versions
Read current controller GUI object relationships, security, QoS and advanced settings; corroborate client VLAN/authentication and relevant policy state.

## Slide 280
NETWORK ACCESS · MECHANISM
WLAN QoS and advanced-policy evidence · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
280
1
WLAN selects authentication
2
Policy maps VLAN and QoS
3
Advanced settings influence client session/roaming
4
Observed client status verifies applied policy
State/input
Inspect actual WLC fields:
Observable consequence
Advanced/session/roaming controls depend on release
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 281
NETWORK ACCESS · ANNOTATED TECHNICAL EXHIBIT
WLAN QoS and advanced-policy evidence · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
281
Inspect actual WLC fields:
WLAN ID/SSID + WPA2PSK/AES
Policy VLAN + QoS profile
Advanced/session/roaming controls depend on release
INPUT / IDENTITY
WLAN security profile · WLAN selects authentication
DECISION / STATE
Advanced settings influence client session/roaming
READBACK / RESULT
Observed client status verifies applied policy
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 282
NETWORK ACCESS · DIAGNOSIS
WLAN QoS and advanced-policy evidence · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
282
Does the observed state satisfy the contract?
Mismatch / control
GUI labels and feature availability vary across WLC versions. A policy saved in one profile must be associated with the AP/WLAN before affecting clients.
Conforming / verification
Read current controller GUI object relationships, security, QoS and advanced settings; corroborate client VLAN/authentication and relevant policy state.
Inspect actual WLC fields:
Inspect
Advanced client behavior
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 283
NETWORK ACCESS · VERIFICATION BRIDGE
WLAN QoS and advanced-policy evidence · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
283
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | WLAN security profile -> Advanced client behavior | Inspect actual WLC fields:
Mechanism / state | Observed client status verifies applied policy | Advanced/session/roaming controls depend on release
Result / boundary | Read current controller GUI object relationships, security, QoS and advanced settings; corroborate client VLAN/authentication and relevant policy state. | GUI labels and feature availability vary across WLC versions. A policy saved in one profile must be associated with the AP/WLAN before affecting clients.
Bridge: Activities 3-5: VLAN paths, STP resilience and wireless policy
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 284
25% · CURRENT CCNA V 1.1
IP Connectivity
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
284
IP Connectivity
Named boundaries -> runtime trace -> exact contract -> failure/control -> acceptance evidence

## Slide 285
IP CONNECTIVITY · ARCHITECTURE
Route-table field interpretation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
285
Destination prefix
Subnet match and prefix length
Next hop
Route gateway resolution
Outgoing interface
Actual packet egress attachment
O 10.20.0.0/24 [110/20] via 10.0.0.2
20=OSPF metric
Boundary to inspect
Distance compares sources for the same prefix; it does not override longest prefix match for a packet.
show ip route

## Slide 286
IP CONNECTIVITY · MECHANISM
Route-table field interpretation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
286
1
Routing source proposes prefix
2
Preference selects installed route
3
FIB stores forwarding result
4
Packet uses installed longest match
State/input
O 10.20.0.0/24 [110/20] via 10.0.0.2
Observable consequence
20=OSPF metric
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 287
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
Route-table field interpretation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
287
O 10.20.0.0/24 [110/20] via 10.0.0.2
110=administrative distance
20=OSPF metric
INPUT / IDENTITY
Destination prefix · Routing source proposes prefix
DECISION / STATE
FIB stores forwarding result
READBACK / RESULT
Packet uses installed longest match
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 288
IP CONNECTIVITY · DIAGNOSIS
Route-table field interpretation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
288
Does the observed state satisfy the contract?
Mismatch / control
Distance compares sources for the same prefix; it does not override longest prefix match for a packet.
Conforming / verification
show ip route. Decode code, prefix, distance, metric, next hop and interface without conflating their roles.
O 10.20.0.0/24 [110/20] via 10.0.0.2
Inspect
Outgoing interface
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 289
IP CONNECTIVITY · VERIFICATION BRIDGE
Route-table field interpretation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
289
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Destination prefix -> Outgoing interface | O 10.20.0.0/24 [110/20] via 10.0.0.2
Mechanism / state | Packet uses installed longest match | 20=OSPF metric
Result / boundary | show ip route. Decode code, prefix, distance, metric, next hop and interface without conflating their roles. | Distance compares sources for the same prefix; it does not override longest prefix match for a packet.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 290
IP CONNECTIVITY · ARCHITECTURE
Longest-prefix matching · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
290
Destination IP
Packet address to be matched
Candidate prefixes
All installed matching route entries
FIB lookup
Highest-prefix-length forwarding decision
10.20.0.0/16 via R2
Destination 10.20.1.50 -> R3
Boundary to inspect
A less specific route with lower distance loses to an installed more specific match
List every matching prefix and choose /24 over /16 and /0; verify using destination-specific route lookup.

## Slide 291
IP CONNECTIVITY · MECHANISM
Longest-prefix matching · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
291
1
Compare matching prefixes
2
Select highest prefix length
3
Resolve next hop/interface
4
Forward packet or drop
State/input
10.20.0.0/16 via R2
Observable consequence
Destination 10.20.1.50 -> R3
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 292
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
Longest-prefix matching · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
292
10.20.0.0/16 via R2
10.20.1.0/24 via R3
Destination 10.20.1.50 -> R3
INPUT / IDENTITY
Destination IP · Compare matching prefixes
DECISION / STATE
Resolve next hop/interface
READBACK / RESULT
Forward packet or drop
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 293
IP CONNECTIVITY · DIAGNOSIS
Longest-prefix matching · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
293
Does the observed state satisfy the contract?
Mismatch / control
A less specific route with lower distance loses to an installed more specific match. Do not sort routes by metric alone.
Conforming / verification
List every matching prefix and choose /24 over /16 and /0; verify using destination-specific route lookup.
10.20.0.0/16 via R2
Inspect
FIB lookup
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 294
IP CONNECTIVITY · VERIFICATION BRIDGE
Longest-prefix matching · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
294
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Destination IP -> FIB lookup | 10.20.0.0/16 via R2
Mechanism / state | Forward packet or drop | Destination 10.20.1.50 -> R3
Result / boundary | List every matching prefix and choose /24 over /16 and /0; verify using destination-specific route lookup. | A less specific route with lower distance loses to an installed more specific match. Do not sort routes by metric alone.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 295
IP CONNECTIVITY · ARCHITECTURE
Administrative distance selection · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
295
Static source
Candidate source with configured distance
OSPF source
Candidate source with protocol distance
RIB selector
Selects best source for same prefix
Same prefix 10.20.0.0/24
Static installs if valid
Boundary to inspect
Distance is locally significant and not a bandwidth or hop-count metric
show ip route 10.20.0.0

## Slide 296
IP CONNECTIVITY · MECHANISM
Administrative distance selection · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
296
1
Sources propose same prefix
2
Lowest distance wins
3
Selected source enters RIB
4
Backup source remains candidate
State/input
Same prefix 10.20.0.0/24
Observable consequence
Static installs if valid
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 297
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
Administrative distance selection · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
297
Same prefix 10.20.0.0/24
Static AD 1 vs OSPF AD 110
Static installs if valid
INPUT / IDENTITY
Static source · Sources propose same prefix
DECISION / STATE
Selected source enters RIB
READBACK / RESULT
Backup source remains candidate
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 298
IP CONNECTIVITY · DIAGNOSIS
Administrative distance selection · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
298
Does the observed state satisfy the contract?
Mismatch / control
Distance is locally significant and not a bandwidth or hop-count metric. A static route can suppress a dynamic route.
Conforming / verification
show ip route 10.20.0.0. Change no forwarding policy until next-hop validity and exact-prefix equality are established.
Same prefix 10.20.0.0/24
Inspect
RIB selector
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 299
IP CONNECTIVITY · VERIFICATION BRIDGE
Administrative distance selection · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
299
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Static source -> RIB selector | Same prefix 10.20.0.0/24
Mechanism / state | Backup source remains candidate | Static installs if valid
Result / boundary | show ip route 10.20.0.0. Change no forwarding policy until next-hop validity and exact-prefix equality are established. | Distance is locally significant and not a bandwidth or hop-count metric. A static route can suppress a dynamic route.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 300
IP CONNECTIVITY · ARCHITECTURE
Metric comparison boundaries · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
300
Protocol candidates
Eligible same-protocol paths
Metric formula
Protocol-specific path ranking
Selected path
Installed best or equal-cost next hop
OSPF cost 20 vs cost 30 ->20
Metrics across protocols are not directly comparable
Boundary to inspect
OSPF cost and RIP hops measure different things
Explain why metric 20 from OSPF cannot be compared numerically with RIP metric 2 to select a route.

## Slide 301
IP CONNECTIVITY · MECHANISM
Metric comparison boundaries · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
301
1
Same protocol evaluates candidates
2
Metric ranks eligible paths
3
Lowest metric installs
4
Equal metrics may permit ECMP
State/input
OSPF cost 20 vs cost 30 ->20
Observable consequence
Metrics across protocols are not directly comparable
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 302
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
Metric comparison boundaries · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
302
OSPF cost 20 vs cost 30 ->20
RIP hop 2 vs hop 3 ->2
Metrics across protocols are not directly comparable
INPUT / IDENTITY
Protocol candidates · Same protocol evaluates candidates
DECISION / STATE
Lowest metric installs
READBACK / RESULT
Equal metrics may permit ECMP
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 303
IP CONNECTIVITY · DIAGNOSIS
Metric comparison boundaries · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
303
Does the observed state satisfy the contract?
Mismatch / control
OSPF cost and RIP hops measure different things. Administrative distance selects source before protocol-specific metrics decide paths.
Conforming / verification
Explain why metric 20 from OSPF cannot be compared numerically with RIP metric 2 to select a route.
OSPF cost 20 vs cost 30 ->20
Inspect
Selected path
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 304
IP CONNECTIVITY · VERIFICATION BRIDGE
Metric comparison boundaries · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
304
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Protocol candidates -> Selected path | OSPF cost 20 vs cost 30 ->20
Mechanism / state | Equal metrics may permit ECMP | Metrics across protocols are not directly comparable
Result / boundary | Explain why metric 20 from OSPF cannot be compared numerically with RIP metric 2 to select a route. | OSPF cost and RIP hops measure different things. Administrative distance selects source before protocol-specific metrics decide paths.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 305
IP CONNECTIVITY · ARCHITECTURE
Connected and local routes · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
305
Interface prefix
Configured local address and mask
Connected route
Reachable directly attached subnet
Local host route
Own router destination host address
C 10.10.10.0/24 is directly connected
Outgoing interface Vlan 10
Boundary to inspect
A shutdown interface removes connected route eligibility
show ip interface brief; show ip route connected

## Slide 306
IP CONNECTIVITY · MECHANISM
Connected and local routes · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
306
1
Interface becomes up/up
2
Connected subnet enters RIB
3
Own address enters local host route
4
Router can forward or terminate traffic
State/input
C 10.10.10.0/24 is directly connected
Observable consequence
Outgoing interface Vlan 10
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 307
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
Connected and local routes · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
307
C 10.10.10.0/24 is directly connected
L 10.10.10.1/32 is directly connected
Outgoing interface Vlan 10
INPUT / IDENTITY
Interface prefix · Interface becomes up/up
DECISION / STATE
Own address enters local host route
READBACK / RESULT
Router can forward or terminate traffic
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 308
IP CONNECTIVITY · DIAGNOSIS
Connected and local routes · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
308
Does the observed state satisfy the contract?
Mismatch / control
A shutdown interface removes connected route eligibility. The local /32 identifies the router's own address, not all hosts.
Conforming / verification
show ip interface brief; show ip route connected. Relate interface state to C and L entries.
C 10.10.10.0/24 is directly connected
Inspect
Local host route
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 309
IP CONNECTIVITY · VERIFICATION BRIDGE
Connected and local routes · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
309
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Interface prefix -> Local host route | C 10.10.10.0/24 is directly connected
Mechanism / state | Router can forward or terminate traffic | Outgoing interface Vlan 10
Result / boundary | show ip interface brief; show ip route connected. Relate interface state to C and L entries. | A shutdown interface removes connected route eligibility. The local /32 identifies the router's own address, not all hosts.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 310
IP CONNECTIVITY · ARCHITECTURE
Static next-hop recursion · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
310
Static prefix
Network to reach
Next-hop address
Gateway requiring recursive lookup
Connected adjacency
Usable on-link forwarding neighbor
ip route 10.20.0.0 255.255.255.0 10.0.0.2
Next hop resolves Gi0/0
Boundary to inspect
Recursive resolution must terminate in a usable adjacency
show ip route 10.0.0.2; show ip arp

## Slide 311
IP CONNECTIVITY · MECHANISM
Static next-hop recursion · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
311
1
RIB receives static route
2
Resolve next hop through another route
3
Find outgoing interface
4
ARP resolves on-link gateway
State/input
ip route 10.20.0.0 255.255.255.0 10.0.0.2
Observable consequence
Next hop resolves Gi0/0
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 312
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
Static next-hop recursion · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
312
ip route 10.20.0.0 255.255.255.0 10.0.0.2
10.0.0.0/30 connected Gi0/0
Next hop resolves Gi0/0
INPUT / IDENTITY
Static prefix · RIB receives static route
DECISION / STATE
Find outgoing interface
READBACK / RESULT
ARP resolves on-link gateway
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 313
IP CONNECTIVITY · DIAGNOSIS
Static next-hop recursion · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
313
Does the observed state satisfy the contract?
Mismatch / control
Recursive resolution must terminate in a usable adjacency. A next hop that is itself unreachable invalidates forwarding.
Conforming / verification
show ip route 10.0.0.2; show ip arp. Verify the static destination and the recursive next-hop route independently.
ip route 10.20.0.0 255.255.255.0 10.0.0.2
Inspect
Connected adjacency
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 314
IP CONNECTIVITY · VERIFICATION BRIDGE
Static next-hop recursion · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
314
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Static prefix -> Connected adjacency | ip route 10.20.0.0 255.255.255.0 10.0.0.2
Mechanism / state | ARP resolves on-link gateway | Next hop resolves Gi0/0
Result / boundary | show ip route 10.0.0.2; show ip arp. Verify the static destination and the recursive next-hop route independently. | Recursive resolution must terminate in a usable adjacency. A next hop that is itself unreachable invalidates forwarding.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 315
IP CONNECTIVITY · ARCHITECTURE
Fully specified static routes · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
315
Destination prefix
Network being forwarded
Next hop
Explicit gateway IPv4 address
Exit interface
Explicit local egress attachment
ip route 10.20.0.0 255.255.255.0 Gi0/0 10.0.0.2
Boundary to inspect
Interface-only static routes on Ethernet can cause ARP for many destinations
Confirm next-hop adjacency and interface state; compare ARP entries before and after fully specified configuration.

## Slide 316
IP CONNECTIVITY · MECHANISM
Fully specified static routes · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
316
1
Route identifies interface and gateway
2
ARP targets gateway
3
Ethernet frame reaches neighbor
4
Neighbor routes onward
State/input
ip route 10.20.0.0 255.255.255.0 Gi0/0 10.0.0.2
Observable consequence
ip route 10.20.0.0 255.255.255.0 Gi0/0 10.0.0.2
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 317
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
Fully specified static routes · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
317
ip route 10.20.0.0 255.255.255.0 Gi0/0 10.0.0.2
INPUT / IDENTITY
Destination prefix · Route identifies interface and gateway
DECISION / STATE
Ethernet frame reaches neighbor
READBACK / RESULT
Neighbor routes onward
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 318
IP CONNECTIVITY · DIAGNOSIS
Fully specified static routes · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
318
Does the observed state satisfy the contract?
Mismatch / control
Interface-only static routes on Ethernet can cause ARP for many destinations. Fully specified routes avoid ambiguous neighbor resolution.
Conforming / verification
Confirm next-hop adjacency and interface state; compare ARP entries before and after fully specified configuration.
ip route 10.20.0.0 255.255.255.0 Gi0/0 10.0.0.2
Inspect
Exit interface
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 319
IP CONNECTIVITY · VERIFICATION BRIDGE
Fully specified static routes · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
319
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Destination prefix -> Exit interface | ip route 10.20.0.0 255.255.255.0 Gi0/0 10.0.0.2
Mechanism / state | Neighbor routes onward | ip route 10.20.0.0 255.255.255.0 Gi0/0 10.0.0.2
Result / boundary | Confirm next-hop adjacency and interface state; compare ARP entries before and after fully specified configuration. | Interface-only static routes on Ethernet can cause ARP for many destinations. Fully specified routes avoid ambiguous neighbor resolution.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 320
IP CONNECTIVITY · ARCHITECTURE
Default IPv4 routing · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
320
Unmatched destination
No installed specific prefix match
Default prefix
Catch-all 0.0.0.0/0 entry
Upstream router
Gateway of last resort
ip route 0.0.0.0 0.0.0.0 203.0.113.1
Gateway of last resort 203.0.113.1
Boundary to inspect
A default route is not proof the upstream can reach the destination
show ip route 0.0.0.0; traceroute target

## Slide 321
IP CONNECTIVITY · MECHANISM
Default IPv4 routing · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
321
1
No more-specific prefix matches
2
0.0.0.0/0 matches every IPv4
3
Resolve upstream next hop
4
Send toward provider
State/input
ip route 0.0.0.0 0.0.0.0 203.0.113.1
Observable consequence
Gateway of last resort 203.0.113.1
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 322
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
Default IPv4 routing · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
322
ip route 0.0.0.0 0.0.0.0 203.0.113.1
Gateway of last resort 203.0.113.1
INPUT / IDENTITY
Unmatched destination · No more-specific prefix matches
DECISION / STATE
Resolve upstream next hop
READBACK / RESULT
Send toward provider
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 323
IP CONNECTIVITY · DIAGNOSIS
Default IPv4 routing · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
323
Does the observed state satisfy the contract?
Mismatch / control
A default route is not proof the upstream can reach the destination. Avoid loops where two routers point defaults at one another.
Conforming / verification
show ip route 0.0.0.0; traceroute target. Identify next-hop loop or upstream policy separately.
ip route 0.0.0.0 0.0.0.0 203.0.113.1
Inspect
Upstream router
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 324
IP CONNECTIVITY · VERIFICATION BRIDGE
Default IPv4 routing · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
324
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Unmatched destination -> Upstream router | ip route 0.0.0.0 0.0.0.0 203.0.113.1
Mechanism / state | Send toward provider | Gateway of last resort 203.0.113.1
Result / boundary | show ip route 0.0.0.0; traceroute target. Identify next-hop loop or upstream policy separately. | A default route is not proof the upstream can reach the destination. Avoid loops where two routers point defaults at one another.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 325
IP CONNECTIVITY · ARCHITECTURE
Host-specific static routes · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
325
Single target IP
One IPv4 host destination
Host route
More-specific /32 forwarding entry
Preferred gateway
Special-case egress next hop
ip route 192.0.2.50 255.255.255.255 10.0.0.6
Other 192.0.2.x uses /24 route
Boundary to inspect
A host route can be used for precise control but accumulates maintenance complexity
Compare destination .50 with .51

## Slide 326
IP CONNECTIVITY · MECHANISM
Host-specific static routes · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
326
1
Destination matches /32
2
More-specific route overrides aggregate
3
Gateway resolves
4
Only target follows special path
State/input
ip route 192.0.2.50 255.255.255.255 10.0.0.6
Observable consequence
Other 192.0.2.x uses /24 route
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 327
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
Host-specific static routes · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
327
ip route 192.0.2.50 255.255.255.255 10.0.0.6
Other 192.0.2.x uses /24 route
INPUT / IDENTITY
Single target IP · Destination matches /32
DECISION / STATE
Gateway resolves
READBACK / RESULT
Only target follows special path
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 328
IP CONNECTIVITY · DIAGNOSIS
Host-specific static routes · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
328
Does the observed state satisfy the contract?
Mismatch / control
A host route can be used for precise control but accumulates maintenance complexity. It can conceal a bad aggregate path.
Conforming / verification
Compare destination .50 with .51. Only .50 should use the /32 next hop.
ip route 192.0.2.50 255.255.255.255 10.0.0.6
Inspect
Preferred gateway
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 329
IP CONNECTIVITY · VERIFICATION BRIDGE
Host-specific static routes · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
329
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Single target IP -> Preferred gateway | ip route 192.0.2.50 255.255.255.255 10.0.0.6
Mechanism / state | Only target follows special path | Other 192.0.2.x uses /24 route
Result / boundary | Compare destination .50 with .51. Only .50 should use the /32 next hop. | A host route can be used for precise control but accumulates maintenance complexity. It can conceal a bad aggregate path.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 330
IP CONNECTIVITY · ARCHITECTURE
Floating static backup · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
330
Primary route
Installed preferred routing source
Higher-distance static
Valid backup with worse distance
Failover path
Secondary egress adjacency
ip route 10.20.0.0 255.255.255.0 10.0.0.6 200
Backup AD 200
Boundary to inspect
Floating distance must exceed primary source distance
show ip route before/after a controlled primary-link failure

## Slide 331
IP CONNECTIVITY · MECHANISM
Floating static backup · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
331
1
Primary source installs
2
Floating static remains absent
3
Primary disappears
4
Backup static becomes best valid route
State/input
ip route 10.20.0.0 255.255.255.0 10.0.0.6 200
Observable consequence
Backup AD 200
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 332
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
Floating static backup · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
332
ip route 10.20.0.0 255.255.255.0 10.0.0.6 200
OSPF primary AD 110
Backup AD 200
INPUT / IDENTITY
Primary route · Primary source installs
DECISION / STATE
Primary disappears
READBACK / RESULT
Backup static becomes best valid route
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 333
IP CONNECTIVITY · DIAGNOSIS
Floating static backup · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
333
Does the observed state satisfy the contract?
Mismatch / control
Floating distance must exceed primary source distance. Route withdrawal, not an application outage alone, triggers this basic backup.
Conforming / verification
show ip route before/after a controlled primary-link failure. Record route source, next hop and recovery timing.
ip route 10.20.0.0 255.255.255.0 10.0.0.6 200
Inspect
Failover path
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 334
IP CONNECTIVITY · VERIFICATION BRIDGE
Floating static backup · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
334
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Primary route -> Failover path | ip route 10.20.0.0 255.255.255.0 10.0.0.6 200
Mechanism / state | Backup static becomes best valid route | Backup AD 200
Result / boundary | show ip route before/after a controlled primary-link failure. Record route source, next hop and recovery timing. | Floating distance must exceed primary source distance. Route withdrawal, not an application outage alone, triggers this basic backup.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 335
IP CONNECTIVITY · ARCHITECTURE
IPv6 static-route scope · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
335
IPv6 prefix
Destination IPv6 network
Link-local next hop
Same-link scoped gateway identity
Outgoing interface
Required local link scope
ipv6 unicast-routing
ipv6 route 2001:db8:20::/64 Gi0/0 fe80::2
Boundary to inspect
Link-local addresses can repeat on different links
show ipv 6 route; show ipv 6 neighbors

## Slide 336
IP CONNECTIVITY · MECHANISM
IPv6 static-route scope · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
336
1
Destination matches IPv6 prefix
2
Link-local gateway is interface-scoped
3
Neighbor discovery resolves MAC
4
Packet forwards on selected link
State/input
ipv 6 unicast-routing
Observable consequence
ipv 6 route 2001:db8:20::/64 Gi0/0 fe80::2
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 337
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
IPv6 static-route scope · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
337
ipv6 unicast-routing
ipv6 route 2001:db8:20::/64 Gi0/0 fe80::2
INPUT / IDENTITY
IPv6 prefix · Destination matches IPv6 prefix
DECISION / STATE
Neighbor discovery resolves MAC
READBACK / RESULT
Packet forwards on selected link
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 338
IP CONNECTIVITY · DIAGNOSIS
IPv6 static-route scope · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
338
Does the observed state satisfy the contract?
Mismatch / control
Link-local addresses can repeat on different links. The route must specify the interface for a link-local next hop.
Conforming / verification
show ipv 6 route; show ipv 6 neighbors. Prove gateway fe80::2 is reachable on the intended Gi0/0.
ipv 6 unicast-routing
Inspect
Outgoing interface
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 339
IP CONNECTIVITY · VERIFICATION BRIDGE
IPv6 static-route scope · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
339
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | IPv6 prefix -> Outgoing interface | ipv 6 unicast-routing
Mechanism / state | Packet forwards on selected link | ipv 6 route 2001:db8:20::/64 Gi0/0 fe80::2
Result / boundary | show ipv 6 route; show ipv 6 neighbors. Prove gateway fe80::2 is reachable on the intended Gi0/0. | Link-local addresses can repeat on different links. The route must specify the interface for a link-local next hop.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 340
IP CONNECTIVITY · ARCHITECTURE
IPv6 default and host routes · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
340
Default ::/0
Catch-all unmatched IPv6 prefix
Host /128
One IPv6 endpoint /128
Global next hop
Routed gateway address
ipv6 route ::/0 2001:db8:0::2
ipv6 route 2001:db8:20::50/128 2001:db8:0::6
Boundary to inspect
Do not apply IPv4 broadcast assumptions to IPv6
show ipv 6 route target

## Slide 341
IP CONNECTIVITY · MECHANISM
IPv6 default and host routes · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
341
1
IPv6 destination lookup runs
2
Most specific installed prefix wins
3
Default catches unmatched traffic
4
ND resolves next hop
State/input
ipv 6 route ::/0 2001:db8:0::2
Observable consequence
ipv 6 route 2001:db8:20::50/128 2001:db8:0::6
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 342
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
IPv6 default and host routes · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
342
ipv6 route ::/0 2001:db8:0::2
ipv6 route 2001:db8:20::50/128 2001:db8:0::6
INPUT / IDENTITY
Default ::/0 · IPv6 destination lookup runs
DECISION / STATE
Default catches unmatched traffic
READBACK / RESULT
ND resolves next hop
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 343
IP CONNECTIVITY · DIAGNOSIS
IPv6 default and host routes · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
343
Does the observed state satisfy the contract?
Mismatch / control
Do not apply IPv4 broadcast assumptions to IPv6. /128 host routes can override a routed /64 subnet.
Conforming / verification
show ipv 6 route target. Compare /128, /64 and /0 matching behavior.
ipv 6 route ::/0 2001:db8:0::2
Inspect
Global next hop
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 344
IP CONNECTIVITY · VERIFICATION BRIDGE
IPv6 default and host routes · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
344
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Default ::/0 -> Global next hop | ipv 6 route ::/0 2001:db8:0::2
Mechanism / state | ND resolves next hop | ipv 6 route 2001:db8:20::50/128 2001:db8:0::6
Result / boundary | show ipv 6 route target. Compare /128, /64 and /0 matching behavior. | Do not apply IPv4 broadcast assumptions to IPv6. /128 host routes can override a routed /64 subnet.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 345
IP CONNECTIVITY · ARCHITECTURE
OSPF process and area boundaries · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
345
Local OSPF process
Local protocol instance identity
Area 0 interfaces
Topology and LSDB flooding scope
Neighbor router
Peer exchanging link-state evidence
router ospf 1
network 10.10.10.0 0.0.0.255 area 0
Boundary to inspect
Process ID is locally significant; area ID must match on the link
show ip ospf interface brief

## Slide 346
IP CONNECTIVITY · MECHANISM
OSPF process and area boundaries · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
346
1
Process selects interfaces
2
Interfaces send Hellos
3
Same-area neighbors form adjacency
4
LSDB supports shortest-path calculation
State/input
router ospf 1
Observable consequence
network 10.10.10.0 0.0.0.255 area 0
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 347
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
OSPF process and area boundaries · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
347
router ospf 1
network 10.0.0.0 0.0.0.3 area 0
network 10.10.10.0 0.0.0.255 area 0
INPUT / IDENTITY
Local OSPF process · Process selects interfaces
DECISION / STATE
Same-area neighbors form adjacency
READBACK / RESULT
LSDB supports shortest-path calculation
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 348
IP CONNECTIVITY · DIAGNOSIS
OSPF process and area boundaries · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
348
Does the observed state satisfy the contract?
Mismatch / control
Process ID is locally significant; area ID must match on the link. Wildcard errors can select unintended interfaces.
Conforming / verification
show ip ospf interface brief. Confirm only intended interfaces and area 0 membership.
router ospf 1
Inspect
Neighbor router
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 349
IP CONNECTIVITY · VERIFICATION BRIDGE
OSPF process and area boundaries · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
349
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Local OSPF process -> Neighbor router | router ospf 1
Mechanism / state | LSDB supports shortest-path calculation | network 10.10.10.0 0.0.0.255 area 0
Result / boundary | show ip ospf interface brief. Confirm only intended interfaces and area 0 membership. | Process ID is locally significant; area ID must match on the link. Wildcard errors can select unintended interfaces.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 350
IP CONNECTIVITY · ARCHITECTURE
OSPF interface activation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
350
Interface address
Connected subnet and protocol activation
OSPF area assignment
Interface belongs to specific area
Passive setting
Suppresses Hellos but still advertises subnet
interface Gi0/0
passive-interface Gi0/1
Boundary to inspect
A passive interface advertises its subnet but does not form neighbors there
show ip protocols; show ip ospf interface

## Slide 351
IP CONNECTIVITY · MECHANISM
OSPF interface activation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
351
1
Interface-level area activates OSPF
2
Hello is sent if not passive
3
Neighbor exchanges state
4
Connected prefix is advertised
State/input
interface Gi0/0
Observable consequence
passive-interface Gi0/1
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 352
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
OSPF interface activation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
352
interface Gi0/0
ip ospf 1 area 0
router ospf 1
passive-interface Gi0/1
INPUT / IDENTITY
Interface address · Interface-level area activates OSPF
DECISION / STATE
Neighbor exchanges state
READBACK / RESULT
Connected prefix is advertised
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 353
IP CONNECTIVITY · DIAGNOSIS
OSPF interface activation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
353
Does the observed state satisfy the contract?
Mismatch / control
A passive interface advertises its subnet but does not form neighbors there. Use passive access segments to reduce unwanted adjacencies.
Conforming / verification
show ip protocols; show ip ospf interface. Distinguish advertising a subnet from sending Hello packets.
interface Gi0/0
Inspect
Passive setting
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 354
IP CONNECTIVITY · VERIFICATION BRIDGE
OSPF interface activation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
354
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Interface address -> Passive setting | interface Gi0/0
Mechanism / state | Connected prefix is advertised | passive-interface Gi0/1
Result / boundary | show ip protocols; show ip ospf interface. Distinguish advertising a subnet from sending Hello packets. | A passive interface advertises its subnet but does not form neighbors there. Use passive access segments to reduce unwanted adjacencies.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 355
IP CONNECTIVITY · ARCHITECTURE
OSPF router ID selection · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
355
Configured router ID
Highest-precedence explicit identity
Loopback address
Preferred automatic-ID address class
Physical address
Fallback automatic-ID address class
router ospf 1
show ip ospf: Routing Process ID1.1.1.1
Boundary to inspect
Duplicate router IDs disrupt LSDB/neighbor operation
Compare show ip ospf on all routers

## Slide 356
IP CONNECTIVITY · MECHANISM
OSPF router ID selection · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
356
1
Explicit router ID has precedence
2
Otherwise select highest loopback IPv4
3
Otherwise highest active physical IPv4
4
Process retains selected ID
State/input
router ospf 1
Observable consequence
show ip ospf: Routing Process ID 1.1.1.1
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 357
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
OSPF router ID selection · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
357
router ospf 1
router-id 1.1.1.1
show ip ospf: Routing Process ID1.1.1.1
INPUT / IDENTITY
Configured router ID · Explicit router ID has precedence
DECISION / STATE
Otherwise highest active physical IPv4
READBACK / RESULT
Process retains selected ID
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 358
IP CONNECTIVITY · DIAGNOSIS
OSPF router ID selection · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
358
Does the observed state satisfy the contract?
Mismatch / control
Duplicate router IDs disrupt LSDB/neighbor operation. A change may require process restart under a maintenance plan.
Conforming / verification
Compare show ip ospf on all routers. Router ID need not be a reachable data-path address.
router ospf 1
Inspect
Physical address
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 359
IP CONNECTIVITY · VERIFICATION BRIDGE
OSPF router ID selection · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
359
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Configured router ID -> Physical address | router ospf 1
Mechanism / state | Process retains selected ID | show ip ospf: Routing Process ID 1.1.1.1
Result / boundary | Compare show ip ospf on all routers. Router ID need not be a reachable data-path address. | Duplicate router IDs disrupt LSDB/neighbor operation. A change may require process restart under a maintenance plan.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 360
IP CONNECTIVITY · ARCHITECTURE
OSPF Hello compatibility · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
360
Hello packet
Discovery of peer and capabilities
Area/timers
Compatibility fields for adjacency
Neighbor receiver
Checks and records neighbor identity
Hello 10 s; Dead 40 s (broadcast default)
Authentication and area options compatible
Boundary to inspect
Timer/area/authentication mismatches prevent adjacency
show ip ospf neighbor; inspect interface timers and MTU on both sides

## Slide 361
IP CONNECTIVITY · MECHANISM
OSPF Hello compatibility · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
361
1
Hello lists router ID
2
Receiver checks link parameters
3
Two-way confirms mutual discovery
4
Adjacency progresses if eligible
State/input
Hello 10 s; Dead 40 s (broadcast default)
Observable consequence
Authentication and area options compatible
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 362
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
OSPF Hello compatibility · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
362
Hello 10 s; Dead 40 s (broadcast default)
Area 0; subnet/mask compatible
Authentication and area options compatible
INPUT / IDENTITY
Hello packet · Hello lists router ID
DECISION / STATE
Two-way confirms mutual discovery
READBACK / RESULT
Adjacency progresses if eligible
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 363
IP CONNECTIVITY · DIAGNOSIS
OSPF Hello compatibility · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
363
Does the observed state satisfy the contract?
Mismatch / control
Timer/area/authentication mismatches prevent adjacency. MTU mismatch commonly stalls ExStart/Exchange after initial discovery.
Conforming / verification
show ip ospf neighbor; inspect interface timers and MTU on both sides. Diagnose stage rather than guessing.
Hello 10 s; Dead 40 s (broadcast default)
Inspect
Neighbor receiver
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 364
IP CONNECTIVITY · VERIFICATION BRIDGE
OSPF Hello compatibility · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
364
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Hello packet -> Neighbor receiver | Hello 10 s; Dead 40 s (broadcast default)
Mechanism / state | Adjacency progresses if eligible | Authentication and area options compatible
Result / boundary | show ip ospf neighbor; inspect interface timers and MTU on both sides. Diagnose stage rather than guessing. | Timer/area/authentication mismatches prevent adjacency. MTU mismatch commonly stalls ExStart/Exchange after initial discovery.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 365
IP CONNECTIVITY · ARCHITECTURE
OSPF neighbor state exchange · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
365
Neighbor state
Mutual discovery/adjacency phase
Database description
Database summary negotiation
LSA exchange
Missing advertisement synchronization
Down -> Init -> 2-Way
Broadcast DROTHER pairs may remain 2-Way
Boundary to inspect
2-Way is not always a failure on broadcast networks
Correlate neighbor role with state

## Slide 366
IP CONNECTIVITY · MECHANISM
OSPF neighbor state exchange · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
366
1
Down->Init sees peer
2
2-Way confirms self listed
3
ExStart/Exchange negotiate database
4
Loading->Full synchronizes LSDB
State/input
Down -> Init -> 2-Way
Observable consequence
Broadcast DROTHER pairs may remain 2-Way
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 367
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
OSPF neighbor state exchange · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
367
Down -> Init -> 2-Way
ExStart -> Exchange -> Loading -> Full
Broadcast DROTHER pairs may remain 2-Way
INPUT / IDENTITY
Neighbor state · Down->Init sees peer
DECISION / STATE
ExStart/Exchange negotiate database
READBACK / RESULT
Loading->Full synchronizes LSDB
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 368
IP CONNECTIVITY · DIAGNOSIS
OSPF neighbor state exchange · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
368
Does the observed state satisfy the contract?
Mismatch / control
2-Way is not always a failure on broadcast networks. Full is expected to DR/BDR and on point-to-point peers.
Conforming / verification
Correlate neighbor role with state. A stuck ExStart differs from legitimate DROTHER 2-Way.
Down -> Init -> 2-Way
Inspect
LSA exchange
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 369
IP CONNECTIVITY · VERIFICATION BRIDGE
OSPF neighbor state exchange · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
369
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Neighbor state -> LSA exchange | Down -> Init -> 2-Way
Mechanism / state | Loading->Full synchronizes LSDB | Broadcast DROTHER pairs may remain 2-Way
Result / boundary | Correlate neighbor role with state. A stuck ExStart differs from legitimate DROTHER 2-Way. | 2-Way is not always a failure on broadcast networks. Full is expected to DR/BDR and on point-to-point peers.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 370
IP CONNECTIVITY · ARCHITECTURE
OSPF point-to-point operation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
370
Router A
Local protocol endpoint
Single peer
Only remote protocol endpoint
Router B
Remote link-state exchange participant
interface Gi0/0
show ip ospf neighbor: FULL/-
Boundary to inspect
Network type must be compatible with topology and peer settings
show ip ospf interface verifies POINT_TO_POINT; neighbor should show FULL/- rather than FULL/DR.

## Slide 371
IP CONNECTIVITY · MECHANISM
OSPF point-to-point operation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
371
1
Point-to-point Hellos discover peer
2
No DR/BDR election occurs
3
Peers synchronize LSDB
4
Both reach Full adjacency
State/input
interface Gi0/0
Observable consequence
show ip ospf neighbor: FULL/-
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 372
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
OSPF point-to-point operation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
372
interface Gi0/0
ip ospf network point-to-point
show ip ospf neighbor: FULL/-
INPUT / IDENTITY
Router A · Point-to-point Hellos discover peer
DECISION / STATE
Peers synchronize LSDB
READBACK / RESULT
Both reach Full adjacency
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 373
IP CONNECTIVITY · DIAGNOSIS
OSPF point-to-point operation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
373
Does the observed state satisfy the contract?
Mismatch / control
Network type must be compatible with topology and peer settings. Do not expect DR/BDR roles on point-to-point links.
Conforming / verification
show ip ospf interface verifies POINT_TO_POINT; neighbor should show FULL/- rather than FULL/DR.
interface Gi0/0
Inspect
Router B
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 374
IP CONNECTIVITY · VERIFICATION BRIDGE
OSPF point-to-point operation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
374
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Router A -> Router B | interface Gi0/0
Mechanism / state | Both reach Full adjacency | show ip ospf neighbor: FULL/-
Result / boundary | show ip ospf interface verifies POINT_TO_POINT; neighbor should show FULL/- rather than FULL/DR. | Network type must be compatible with topology and peer settings. Do not expect DR/BDR roles on point-to-point links.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 375
IP CONNECTIVITY · ARCHITECTURE
OSPF DR and BDR election · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
375
Broadcast segment
Multiaccess neighbor discovery scope
Eligible routers
Priority/RID candidates
DR/BDR
Database exchange coordinators
R1 priority 100 RID 1.1.1.1
Priority0: ineligible for DR/BDR
Boundary to inspect
A later higher-priority router does not automatically replace an established DR
show ip ospf interface and neighbor

## Slide 376
IP CONNECTIVITY · MECHANISM
OSPF DR and BDR election · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
376
1
Highest interface priority wins DR
2
Router ID breaks tie
3
BDR backs up DR
4
Existing elected DR is nonpreemptive
State/input
R1 priority 100 RID 1.1.1.1
Observable consequence
Priority0: ineligible for DR/BDR
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 377
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
OSPF DR and BDR election · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
377
R1 priority 100 RID 1.1.1.1
R2 priority 50 RID 2.2.2.2
Priority0: ineligible for DR/BDR
INPUT / IDENTITY
Broadcast segment · Highest interface priority wins DR
DECISION / STATE
BDR backs up DR
READBACK / RESULT
Existing elected DR is nonpreemptive
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 378
IP CONNECTIVITY · DIAGNOSIS
OSPF DR and BDR election · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
378
Does the observed state satisfy the contract?
Mismatch / control
A later higher-priority router does not automatically replace an established DR. Election timing affects observed results.
Conforming / verification
show ip ospf interface and neighbor. Record priorities and election history before claiming the highest RID must be current DR.
R1 priority 100 RID 1.1.1.1
Inspect
DR/BDR
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 379
IP CONNECTIVITY · VERIFICATION BRIDGE
OSPF DR and BDR election · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
379
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Broadcast segment -> DR/BDR | R1 priority 100 RID 1.1.1.1
Mechanism / state | Existing elected DR is nonpreemptive | Priority0: ineligible for DR/BDR
Result / boundary | show ip ospf interface and neighbor. Record priorities and election history before claiming the highest RID must be current DR. | A later higher-priority router does not automatically replace an established DR. Election timing affects observed results.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 380
IP CONNECTIVITY · ARCHITECTURE
OSPF cost calculation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
380
Reference bandwidth
Numerator in local cost formula
Interface bandwidth
Denominator or configured interface cost
Path sum
Accumulated route metric
Reference 100 Mb/s
1 Gb/s link also cost 1 at default
Boundary to inspect
Default reference does not distinguish fast links well
show ip ospf interface

## Slide 381
IP CONNECTIVITY · MECHANISM
OSPF cost calculation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
381
1
Reference bandwidth divides by link bandwidth
2
Interface cost has minimum 1
3
Costs sum across path
4
Lowest total wins
State/input
Reference 100 Mb/s
Observable consequence
1 Gb/s link also cost 1 at default
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 382
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
OSPF cost calculation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
382
Reference 100 Mb/s
100 Mb/s link cost 1
10 Mb/s link cost 10
1 Gb/s link also cost 1 at default
INPUT / IDENTITY
Reference bandwidth · Reference bandwidth divides by link bandwidth
DECISION / STATE
Costs sum across path
READBACK / RESULT
Lowest total wins
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 383
IP CONNECTIVITY · DIAGNOSIS
OSPF cost calculation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
383
Does the observed state satisfy the contract?
Mismatch / control
Default reference does not distinguish fast links well. Apply a consistent reference-bandwidth policy across routers.
Conforming / verification
show ip ospf interface. Compare stated bandwidth and configured cost with the installed route metric.
Reference 100 Mb/s
Inspect
Path sum
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 384
IP CONNECTIVITY · VERIFICATION BRIDGE
OSPF cost calculation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
384
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Reference bandwidth -> Path sum | Reference 100 Mb/s
Mechanism / state | Lowest total wins | 1 Gb/s link also cost 1 at default
Result / boundary | show ip ospf interface. Compare stated bandwidth and configured cost with the installed route metric. | Default reference does not distinguish fast links well. Apply a consistent reference-bandwidth policy across routers.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 385
IP CONNECTIVITY · ARCHITECTURE
OSPF LSA and SPF boundaries · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
385
Link-state advertisement
Describes topology and prefix state
Area LSDB
Shared area link-state information
SPF tree
Locally rooted shortest-path calculation
LSDB: router ID + links + costs
Result: next hop for each prefix
Boundary to inspect
Same LSDB does not mean identical next hops because each router roots SPF at itself
show ip ospf database and show ip route ospf

## Slide 386
IP CONNECTIVITY · MECHANISM
OSPF LSA and SPF boundaries · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
386
1
Router describes topology in LSAs
2
Neighbors flood changes
3
Area databases synchronize
4
Each router computes its own shortest tree
State/input
LSDB: router ID + links + costs
Observable consequence
Result: next hop for each prefix
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 387
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
OSPF LSA and SPF boundaries · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
387
LSDB: router ID + links + costs
SPF root: local router ID
Result: next hop for each prefix
INPUT / IDENTITY
Link-state advertisement · Router describes topology in LSAs
DECISION / STATE
Area databases synchronize
READBACK / RESULT
Each router computes its own shortest tree
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 388
IP CONNECTIVITY · DIAGNOSIS
OSPF LSA and SPF boundaries · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
388
Does the observed state satisfy the contract?
Mismatch / control
Same LSDB does not mean identical next hops because each router roots SPF at itself. Link-state is not distance-vector rumor.
Conforming / verification
show ip ospf database and show ip route ospf. Connect LSDB topology to local forwarding result.
LSDB: router ID + links + costs
Inspect
SPF tree
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 389
IP CONNECTIVITY · VERIFICATION BRIDGE
OSPF LSA and SPF boundaries · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
389
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Link-state advertisement -> SPF tree | LSDB: router ID + links + costs
Mechanism / state | Each router computes its own shortest tree | Result: next hop for each prefix
Result / boundary | show ip ospf database and show ip route ospf. Connect LSDB topology to local forwarding result. | Same LSDB does not mean identical next hops because each router roots SPF at itself. Link-state is not distance-vector rumor.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 390
IP CONNECTIVITY · ARCHITECTURE
OSPF failure diagnosis · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
390
Physical adjacency
Up/up and address prerequisites
OSPF neighbor
Peer ID, role and Full state
Destination prefix
Advertised/installed remote subnet
Interface up/up
Likely interface not selected into OSPF, interface down, or wrong area
Boundary to inspect
A Full neighbor alone does not prove every needed subnet is advertised
Use show ip ospf neighbor, database and route

## Slide 391
IP CONNECTIVITY · MECHANISM
OSPF failure diagnosis · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
391
1
Link state checked first
2
Hello/adjacency state checked next
3
LSDB checked for prefix
4
RIB verifies selected route
State/input
Interface up/up
Observable consequence
Likely interface not selected into OSPF, interface down, or wrong area
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 392
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
OSPF failure diagnosis · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
392
Interface up/up
Neighbor FULL
Prefix absent from LSDB
Likely interface not selected into OSPF, interface down, or wrong area
INPUT / IDENTITY
Physical adjacency · Link state checked first
DECISION / STATE
LSDB checked for prefix
READBACK / RESULT
RIB verifies selected route
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 393
IP CONNECTIVITY · DIAGNOSIS
OSPF failure diagnosis · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
393
Does the observed state satisfy the contract?
Mismatch / control
A Full neighbor alone does not prove every needed subnet is advertised. Diagnose missing route separately from neighbor state.
Conforming / verification
Use show ip ospf neighbor, database and route. Record one observation per layer and test the specific hypothesis.
Interface up/up
Inspect
Destination prefix
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 394
IP CONNECTIVITY · VERIFICATION BRIDGE
OSPF failure diagnosis · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
394
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Physical adjacency -> Destination prefix | Interface up/up
Mechanism / state | RIB verifies selected route | Likely interface not selected into OSPF, interface down, or wrong area
Result / boundary | Use show ip ospf neighbor, database and route. Record one observation per layer and test the specific hypothesis. | A Full neighbor alone does not prove every needed subnet is advertised. Diagnose missing route separately from neighbor state.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 395
IP CONNECTIVITY · ARCHITECTURE
Equal-cost multipath forwarding · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
395
Equal OSPF routes
Same-prefix paths with equal metric
FIB hash
Chooses path from eligible next hops
Outgoing links
Carry different eligible flows
O 10.20.0.0/24 [110/20] via 10.0.0.2
Two equal next hops
Boundary to inspect
Packet or flow distribution depends on platform forwarding mode
Read installed next-hop count and interface counter deltas across several flows; do not infer per-flow doubling.

## Slide 396
IP CONNECTIVITY · MECHANISM
Equal-cost multipath forwarding · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
396
1
Same-prefix equal metrics qualify
2
RIB installs multiple next hops
3
FIB distributes eligible flows
4
Each flow follows hash decision
State/input
O 10.20.0.0/24 [110/20] via 10.0.0.2
Observable consequence
Two equal next hops
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 397
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
Equal-cost multipath forwarding · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
397
O 10.20.0.0/24 [110/20] via 10.0.0.2
via 10.0.0.6
Two equal next hops
INPUT / IDENTITY
Equal OSPF routes · Same-prefix equal metrics qualify
DECISION / STATE
FIB distributes eligible flows
READBACK / RESULT
Each flow follows hash decision
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 398
IP CONNECTIVITY · DIAGNOSIS
Equal-cost multipath forwarding · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
398
Does the observed state satisfy the contract?
Mismatch / control
Packet or flow distribution depends on platform forwarding mode. Equal cost does not guarantee equal measured utilization.
Conforming / verification
Read installed next-hop count and interface counter deltas across several flows; do not infer per-flow doubling.
O 10.20.0.0/24 [110/20] via 10.0.0.2
Inspect
Outgoing links
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 399
IP CONNECTIVITY · VERIFICATION BRIDGE
Equal-cost multipath forwarding · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
399
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Equal OSPF routes -> Outgoing links | O 10.20.0.0/24 [110/20] via 10.0.0.2
Mechanism / state | Each flow follows hash decision | Two equal next hops
Result / boundary | Read installed next-hop count and interface counter deltas across several flows; do not infer per-flow doubling. | Packet or flow distribution depends on platform forwarding mode. Equal cost does not guarantee equal measured utilization.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 400
IP CONNECTIVITY · ARCHITECTURE
FHRP virtual-gateway ownership · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
400
Two gateway routers
Active/standby pair coordinates ownership
Virtual IP/MAC
Shared stable host gateway identity
LAN hosts
Host uses unchanged gateway address
HSRP virtual IP 10.10.10.1
Group 10 virtual MAC0000.0c07.ac0a
Boundary to inspect
FHRP provides gateway redundancy, not end-to-end path guarantees
show standby brief

## Slide 401
IP CONNECTIVITY · MECHANISM
FHRP virtual-gateway ownership · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
401
1
Active router owns virtual gateway
2
Standby monitors control messages
3
Active failure transfers ownership
4
Hosts keep same default gateway
State/input
HSRP virtual IP 10.10.10.1
Observable consequence
Group 10 virtual MAC0000.0c07.ac0a
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 402
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
FHRP virtual-gateway ownership · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
402
HSRP virtual IP 10.10.10.1
R1 physical .2; R2 physical .3
Group 10 virtual MAC0000.0c07.ac0a
INPUT / IDENTITY
Two gateway routers · Active router owns virtual gateway
DECISION / STATE
Active failure transfers ownership
READBACK / RESULT
Hosts keep same default gateway
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 403
IP CONNECTIVITY · DIAGNOSIS
FHRP virtual-gateway ownership · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
403
Does the observed state satisfy the contract?
Mismatch / control
FHRP provides gateway redundancy, not end-to-end path guarantees. Tracking and preemption policy affect ownership recovery.
Conforming / verification
show standby brief. Confirm one active owner, one standby and host ARP resolves virtual rather than physical gateway MAC.
HSRP virtual IP 10.10.10.1
Inspect
LAN hosts
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 404
IP CONNECTIVITY · VERIFICATION BRIDGE
FHRP virtual-gateway ownership · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
404
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Two gateway routers -> LAN hosts | HSRP virtual IP 10.10.10.1
Mechanism / state | Hosts keep same default gateway | Group 10 virtual MAC0000.0c07.ac0a
Result / boundary | show standby brief. Confirm one active owner, one standby and host ARP resolves virtual rather than physical gateway MAC. | FHRP provides gateway redundancy, not end-to-end path guarantees. Tracking and preemption policy affect ownership recovery.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 405
IP CONNECTIVITY · ARCHITECTURE
End-to-end routed fault isolation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
405
Source host
Address/mask/default-gateway decision
Transit routers
Installed route and neighbor resolution
Destination host
Return path and service listener
Source 10.10.10.10/24 gw 10.10.10.1
Both directions need routes
Boundary to inspect
One-way routes can produce request arrival with no response
Collect source settings, forward route, return route and filtering evidence; isolate first failing control point.

## Slide 406
IP CONNECTIVITY · MECHANISM
End-to-end routed fault isolation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
406
1
Host chooses local/remote
2
Gateway forwards by longest match
3
Each hop resolves adjacency
4
Return route carries response
State/input
Source 10.10.10.10/24 gw 10.10.10.1
Observable consequence
Both directions need routes
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 407
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
End-to-end routed fault isolation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
407
Source 10.10.10.10/24 gw 10.10.10.1
Target 10.20.20.20/24 gw 10.20.20.1
Both directions need routes
INPUT / IDENTITY
Source host · Host chooses local/remote
DECISION / STATE
Each hop resolves adjacency
READBACK / RESULT
Return route carries response
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 408
IP CONNECTIVITY · DIAGNOSIS
End-to-end routed fault isolation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
408
Does the observed state satisfy the contract?
Mismatch / control
One-way routes can produce request arrival with no response. ACL and NAT may alter observed reachability independently.
Conforming / verification
Collect source settings, forward route, return route and filtering evidence; isolate first failing control point.
Source 10.10.10.10/24 gw 10.10.10.1
Inspect
Destination host
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 409
IP CONNECTIVITY · VERIFICATION BRIDGE
End-to-end routed fault isolation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
409
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Source host -> Destination host | Source 10.10.10.10/24 gw 10.10.10.1
Mechanism / state | Return route carries response | Both directions need routes
Result / boundary | Collect source settings, forward route, return route and filtering evidence; isolate first failing control point. | One-way routes can produce request arrival with no response. ACL and NAT may alter observed reachability independently.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 410
IP CONNECTIVITY · ARCHITECTURE
IPv6 floating static failover · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
410
Primary IPv6 route
Preferred installed IPv6 source
Backup next hop
Secondary scoped gateway adjacency
Administrative distance
Locally configured source preference
ipv6 route 2001:db8:20::/64 Gi0/0 fe80::2 200
show ipv6 route
Boundary to inspect
If primary route remains installed despite remote failure, an untracked floating route may not activate
Compare /64 route source and next hop before/after controlled primary withdrawal; show ipv 6 neighbors confirms backup adjacency.

## Slide 411
IP CONNECTIVITY · MECHANISM
IPv6 floating static failover · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
411
1
Primary source installs prefix
2
Higher-distance static stays candidate
3
Primary route withdraws
4
Backup resolves and installs
State/input
ipv 6 route 2001:db8:20::/64 Gi0/0 fe80::2 200
Observable consequence
show ipv 6 route
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 412
IP CONNECTIVITY · ANNOTATED TECHNICAL EXHIBIT
IPv6 floating static failover · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
412
ipv6 route 2001:db8:20::/64 Gi0/0 fe80::2 200
Primary OSPFv3 AD 110
Backup AD 200
show ipv6 route
INPUT / IDENTITY
Primary IPv6 route · Primary source installs prefix
DECISION / STATE
Primary route withdraws
READBACK / RESULT
Backup resolves and installs
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 413
IP CONNECTIVITY · DIAGNOSIS
IPv6 floating static failover · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
413
Does the observed state satisfy the contract?
Mismatch / control
If primary route remains installed despite remote failure, an untracked floating route may not activate. Link-local next hop requires interface scope.
Conforming / verification
Compare /64 route source and next hop before/after controlled primary withdrawal; show ipv 6 neighbors confirms backup adjacency.
ipv 6 route 2001:db8:20::/64 Gi0/0 fe80::2 200
Inspect
Administrative distance
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 414
IP CONNECTIVITY · VERIFICATION BRIDGE
IPv6 floating static failover · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
414
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Primary IPv6 route -> Administrative distance | ipv 6 route 2001:db8:20::/64 Gi0/0 fe80::2 200
Mechanism / state | Backup resolves and installs | show ipv 6 route
Result / boundary | Compare /64 route source and next hop before/after controlled primary withdrawal; show ipv 6 neighbors confirms backup adjacency. | If primary route remains installed despite remote failure, an untracked floating route may not activate. Link-local next hop requires interface scope.
Bridge: Activity 6: static/IPv6 routes or Activity 7: OSPF/gateway failover
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 415
10% · CURRENT CCNA V 1.1
IP Services
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
415
IP Services
Named boundaries -> runtime trace -> exact contract -> failure/control -> acceptance evidence

## Slide 416
IP SERVICES · ARCHITECTURE
Static NAT mapping · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
416
Inside local host
Private source before translation
Inside global address
Public source identity after translation
NAT router
Applies reversible static mapping
ip nat inside source static 10.10.10.10 203.0.113.10
Inside global 203.0.113.10
Boundary to inspect
NAT requires inside/outside interface roles and routing
show ip nat translations; inspect original/translated endpoints and both route directions.

## Slide 417
IP SERVICES · MECHANISM
Static NAT mapping · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
417
1
Inside packet matches mapping
2
Source changes to global
3
Outside reply matches reverse mapping
4
Destination returns to local
State/input
ip nat inside source static 10.10.10.10 203.0.113.10
Observable consequence
Inside global 203.0.113.10
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 418
IP SERVICES · ANNOTATED TECHNICAL EXHIBIT
Static NAT mapping · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
418
ip nat inside source static 10.10.10.10 203.0.113.10
Inside local 10.10.10.10
Inside global 203.0.113.10
INPUT / IDENTITY
Inside local host · Inside packet matches mapping
DECISION / STATE
Outside reply matches reverse mapping
READBACK / RESULT
Destination returns to local
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 419
IP SERVICES · DIAGNOSIS
Static NAT mapping · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
419
Does the observed state satisfy the contract?
Mismatch / control
NAT requires inside/outside interface roles and routing. A mapping is not an inbound security policy.
Conforming / verification
show ip nat translations; inspect original/translated endpoints and both route directions.
ip nat inside source static 10.10.10.10 203.0.113.10
Inspect
NAT router
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 420
IP SERVICES · VERIFICATION BRIDGE
Static NAT mapping · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
420
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Inside local host -> NAT router | ip nat inside source static 10.10.10.10 203.0.113.10
Mechanism / state | Destination returns to local | Inside global 203.0.113.10
Result / boundary | show ip nat translations; inspect original/translated endpoints and both route directions. | NAT requires inside/outside interface roles and routing. A mapping is not an inbound security policy.
Bridge: Activity 8: NAT, DHCP, DNS and time
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 421
IP SERVICES · ARCHITECTURE
Dynamic NAT pool allocation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
421
Inside address ACL
Selects inside translation candidates
Global pool
Available global address inventory
Translation table
Tracks reversible allocated mappings
ip nat pool PUBLIC 203.0.113.10 203.0.113.20 netmask 255.255.255.0
ip nat inside source list 1 pool PUBLIC
Boundary to inspect
Pool has 11 addresses; more simultaneous unique inside mappings can exhaust it
show ip nat statistics and translations

## Slide 422
IP SERVICES · MECHANISM
Dynamic NAT pool allocation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
422
1
Permitted inside source starts traffic
2
Free global address assigned
3
Entry persists while active
4
Pool exhaustion rejects new mapping
State/input
ip nat pool PUBLIC 203.0.113.10 203.0.113.20 netmask 255.255.255.0
Observable consequence
ip nat inside source list 1 pool PUBLIC
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 423
IP SERVICES · ANNOTATED TECHNICAL EXHIBIT
Dynamic NAT pool allocation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
423
ip nat pool PUBLIC 203.0.113.10 203.0.113.20 netmask 255.255.255.0
ip nat inside source list 1 pool PUBLIC
INPUT / IDENTITY
Inside address ACL · Permitted inside source starts traffic
DECISION / STATE
Entry persists while active
READBACK / RESULT
Pool exhaustion rejects new mapping
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 424
IP SERVICES · DIAGNOSIS
Dynamic NAT pool allocation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
424
Does the observed state satisfy the contract?
Mismatch / control
Pool has 11 addresses; more simultaneous unique inside mappings can exhaust it. ACL selects translation candidates, not interface filtering.
Conforming / verification
show ip nat statistics and translations. Compare allocated addresses with pool capacity and identify unmatched ACL sources.
ip nat pool PUBLIC 203.0.113.10 203.0.113.20 netmask 255.255.255.0
Inspect
Translation table
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 425
IP SERVICES · VERIFICATION BRIDGE
Dynamic NAT pool allocation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
425
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Inside address ACL -> Translation table | ip nat pool PUBLIC 203.0.113.10 203.0.113.20 netmask 255.255.255.0
Mechanism / state | Pool exhaustion rejects new mapping | ip nat inside source list 1 pool PUBLIC
Result / boundary | show ip nat statistics and translations. Compare allocated addresses with pool capacity and identify unmatched ACL sources. | Pool has 11 addresses; more simultaneous unique inside mappings can exhaust it. ACL selects translation candidates, not interface filtering.
Bridge: Activity 8: NAT, DHCP, DNS and time
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 426
IP SERVICES · ARCHITECTURE
PAT port disambiguation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
426
Inside clients
Original endpoint source tuples
Shared public IP
Common translated source address
Port mapping table
Disambiguates protocol/address/port state
10.10.10.10:49152 ->203.0.113.2:30001
ip nat inside source list 1 interface Gi0/0 overload
Boundary to inspect
PAT depends on tuple state and protocol behavior
show ip nat translations

## Slide 427
IP SERVICES · MECHANISM
PAT port disambiguation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
427
1
Client sends unique source tuple
2
NAT selects translated source port
3
Reply matches global tuple
4
Original tuple is restored
State/input
10.10.10.10:49152 ->203.0.113.2:30001
Observable consequence
ip nat inside source list 1 interface Gi0/0 overload
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 428
IP SERVICES · ANNOTATED TECHNICAL EXHIBIT
PAT port disambiguation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
428
10.10.10.10:49152 ->203.0.113.2:30001
10.10.10.11:49152 ->203.0.113.2:30002
ip nat inside source list 1 interface Gi0/0 overload
INPUT / IDENTITY
Inside clients · Client sends unique source tuple
DECISION / STATE
Reply matches global tuple
READBACK / RESULT
Original tuple is restored
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 429
IP SERVICES · DIAGNOSIS
PAT port disambiguation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
429
Does the observed state satisfy the contract?
Mismatch / control
PAT depends on tuple state and protocol behavior. An address-only inspection cannot distinguish concurrent sessions.
Conforming / verification
show ip nat translations. Compare inside local/global address and port; correlate remote endpoint and protocol.
10.10.10.10:49152 ->203.0.113.2:30001
Inspect
Port mapping table
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 430
IP SERVICES · VERIFICATION BRIDGE
PAT port disambiguation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
430
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Inside clients -> Port mapping table | 10.10.10.10:49152 ->203.0.113.2:30001
Mechanism / state | Original tuple is restored | ip nat inside source list 1 interface Gi0/0 overload
Result / boundary | show ip nat translations. Compare inside local/global address and port; correlate remote endpoint and protocol. | PAT depends on tuple state and protocol behavior. An address-only inspection cannot distinguish concurrent sessions.
Bridge: Activity 8: NAT, DHCP, DNS and time
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 431
IP SERVICES · ARCHITECTURE
NTP synchronization hierarchy · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
431
Time source
Trusted clock upstream
Router client
Offset/stratum association selection
Device logs
Time-correlated device event records
ntp server 192.0.2.123
show ntp associations
Boundary to inspect
A configured server can be unreachable or unsynchronized
show ntp status and associations

## Slide 432
IP SERVICES · MECHANISM
NTP synchronization hierarchy · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
432
1
Client polls NTP server
2
Round-trip estimates offset
3
Eligible source selected
4
Clock supports correlated logs
State/input
ntp server 192.0.2.123
Observable consequence
show ntp associations
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 433
IP SERVICES · ANNOTATED TECHNICAL EXHIBIT
NTP synchronization hierarchy · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
433
ntp server 192.0.2.123
Stratum 0 reference clock
Stratum 1 directly synchronized server
Stratum 2 downstream client
show ntp associations
INPUT / IDENTITY
Time source · Client polls NTP server
DECISION / STATE
Eligible source selected
READBACK / RESULT
Clock supports correlated logs
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 434
IP SERVICES · DIAGNOSIS
NTP synchronization hierarchy · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
434
Does the observed state satisfy the contract?
Mismatch / control
A configured server can be unreachable or unsynchronized. Wrong time undermines incident correlation and certificates.
Conforming / verification
show ntp status and associations. Identify selected peer and synchronized state; compare clock with trusted reference.
ntp server 192.0.2.123
Inspect
Device logs
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 435
IP SERVICES · VERIFICATION BRIDGE
NTP synchronization hierarchy · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
435
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Time source -> Device logs | ntp server 192.0.2.123
Mechanism / state | Clock supports correlated logs | show ntp associations
Result / boundary | show ntp status and associations. Identify selected peer and synchronized state; compare clock with trusted reference. | A configured server can be unreachable or unsynchronized. Wrong time undermines incident correlation and certificates.
Bridge: Activity 8: NAT, DHCP, DNS and time
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 436
IP SERVICES · ARCHITECTURE
DHCP DORA allocation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
436
DHCP client
Requests address and options
Relay/router
Relays request across routed boundary
DHCP server
Selects scope and grants lease
UDP client 68 -> server 67
DORA: Discover Offer Request ACK
Boundary to inspect
A lease without correct router/DNS options yields partial connectivity
Capture DORA and inspect ipconfig/ip address evidence

## Slide 437
IP SERVICES · MECHANISM
DHCP DORA allocation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
437
1
Discover broadcasts need
2
Offer proposes lease
3
Request selects offer
4
ACK confirms options and lifetime
State/input
UDP client 68 -> server 67
Observable consequence
DORA: Discover Offer Request ACK
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 438
IP SERVICES · ANNOTATED TECHNICAL EXHIBIT
DHCP DORA allocation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
438
UDP client 68 -> server 67
Options: mask, router, DNS, lease
DORA: Discover Offer Request ACK
INPUT / IDENTITY
DHCP client · Discover broadcasts need
DECISION / STATE
Request selects offer
READBACK / RESULT
ACK confirms options and lifetime
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 439
IP SERVICES · DIAGNOSIS
DHCP DORA allocation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
439
Does the observed state satisfy the contract?
Mismatch / control
A lease without correct router/DNS options yields partial connectivity. Exhausted pool and blocked relay are distinct faults.
Conforming / verification
Capture DORA and inspect ipconfig/ip address evidence. Confirm assigned subnet, gateway, DNS and lease scope.
UDP client 68 -> server 67
Inspect
DHCP server
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 440
IP SERVICES · VERIFICATION BRIDGE
DHCP DORA allocation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
440
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | DHCP client -> DHCP server | UDP client 68 -> server 67
Mechanism / state | ACK confirms options and lifetime | DORA: Discover Offer Request ACK
Result / boundary | Capture DORA and inspect ipconfig/ip address evidence. Confirm assigned subnet, gateway, DNS and lease scope. | A lease without correct router/DNS options yields partial connectivity. Exhausted pool and blocked relay are distinct faults.
Bridge: Activity 8: NAT, DHCP, DNS and time
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 441
IP SERVICES · ARCHITECTURE
DHCP relay and client roles · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
441
Client VLAN
Broadcast-originating subnet
Relay SVI
Adds giaddr and forwards server request
Remote DHCP server
Selects matching client-subnet scope
interface Vlan 10
Relay giaddr 10.10.10.1
Boundary to inspect
Remote server needs a scope for the relay subnet and return routing
Check giaddr, scope selection and server response; compare client address with VLAN 10 prefix.

## Slide 442
IP SERVICES · MECHANISM
DHCP relay and client roles · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
442
1
Broadcast reaches relay
2
Relay sets giaddr
3
Server chooses corresponding scope
4
Reply returns through relay
State/input
interface Vlan 10
Observable consequence
Relay giaddr 10.10.10.1
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 443
IP SERVICES · ANNOTATED TECHNICAL EXHIBIT
DHCP relay and client roles · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
443
interface Vlan 10
ip helper-address 10.20.0.50
Relay giaddr 10.10.10.1
INPUT / IDENTITY
Client VLAN · Broadcast reaches relay
DECISION / STATE
Server chooses corresponding scope
READBACK / RESULT
Reply returns through relay
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 444
IP SERVICES · DIAGNOSIS
DHCP relay and client roles · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
444
Does the observed state satisfy the contract?
Mismatch / control
Remote server needs a scope for the relay subnet and return routing. Helper configuration does not fix wrong pool options.
Conforming / verification
Check giaddr, scope selection and server response; compare client address with VLAN 10 prefix.
interface Vlan 10
Inspect
Remote DHCP server
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 445
IP SERVICES · VERIFICATION BRIDGE
DHCP relay and client roles · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
445
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Client VLAN -> Remote DHCP server | interface Vlan 10
Mechanism / state | Reply returns through relay | Relay giaddr 10.10.10.1
Result / boundary | Check giaddr, scope selection and server response; compare client address with VLAN 10 prefix. | Remote server needs a scope for the relay subnet and return routing. Helper configuration does not fix wrong pool options.
Bridge: Activity 8: NAT, DHCP, DNS and time
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 446
IP SERVICES · ARCHITECTURE
DNS record and cache evidence · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
446
Stub resolver
Chooses resolver and requested name
Recursive DNS
Recurses and caches answers
Authoritative zone
Owns published zone records
A app.example.test 192.0.2.50 TTL 300
CNAME portal -> app
Boundary to inspect
NXDOMAIN differs from timeout and wrong answer
nslookup/dig result: server, status, answer and TTL

## Slide 447
IP SERVICES · MECHANISM
DNS record and cache evidence · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
447
1
Client queries resolver
2
Resolver checks cache
3
Authoritative data answers miss
4
TTL limits cache lifetime
State/input
A app.example.test 192.0.2.50 TTL 300
Observable consequence
CNAME portal -> app
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 448
IP SERVICES · ANNOTATED TECHNICAL EXHIBIT
DNS record and cache evidence · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
448
A app.example.test 192.0.2.50 TTL 300
AAAA app.example.test2001:db8::50
CNAME portal -> app
INPUT / IDENTITY
Stub resolver · Client queries resolver
DECISION / STATE
Authoritative data answers miss
READBACK / RESULT
TTL limits cache lifetime
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 449
IP SERVICES · DIAGNOSIS
DNS record and cache evidence · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
449
Does the observed state satisfy the contract?
Mismatch / control
NXDOMAIN differs from timeout and wrong answer. Ping by IP can succeed while name resolution fails.
Conforming / verification
nslookup/dig result: server, status, answer and TTL. Test intended A/AAAA record and resolver reachability separately.
A app.example.test 192.0.2.50 TTL 300
Inspect
Authoritative zone
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 450
IP SERVICES · VERIFICATION BRIDGE
DNS record and cache evidence · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
450
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Stub resolver -> Authoritative zone | A app.example.test 192.0.2.50 TTL 300
Mechanism / state | TTL limits cache lifetime | CNAME portal -> app
Result / boundary | nslookup/dig result: server, status, answer and TTL. Test intended A/AAAA record and resolver reachability separately. | NXDOMAIN differs from timeout and wrong answer. Ping by IP can succeed while name resolution fails.
Bridge: Activity 8: NAT, DHCP, DNS and time
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 451
IP SERVICES · ARCHITECTURE
SNMP manager and agent state · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
451
NMS manager
Polls and correlates operational data
Device agent
Exposes managed object values
MIB/OID
Names managed object identifiers and structure
SNMP queries UDP 161
SNMPv 3 authPriv protects messages
Boundary to inspect
SNMPv 1/v 2 c community strings do not provide modern encryption
Correlate OID value, timestamp, agent reachability and local show output

## Slide 452
IP SERVICES · MECHANISM
SNMP manager and agent state · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
452
1
Manager polls object
2
Agent returns value
3
Trap/inform reports event
4
NMS correlates state over time
State/input
SNMP queries UDP 161
Observable consequence
SNMPv 3 authPriv protects messages
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 453
IP SERVICES · ANNOTATED TECHNICAL EXHIBIT
SNMP manager and agent state · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
453
SNMP queries UDP 161
Notifications UDP 162
ifOperStatus: up(1), down(2)
SNMPv 3 authPriv protects messages
INPUT / IDENTITY
NMS manager · Manager polls object
DECISION / STATE
Trap/inform reports event
READBACK / RESULT
NMS correlates state over time
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 454
IP SERVICES · DIAGNOSIS
SNMP manager and agent state · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
454
Does the observed state satisfy the contract?
Mismatch / control
SNMPv 1/v 2 c community strings do not provide modern encryption. A stale polling value is not the same as live interface status.
Conforming / verification
Correlate OID value, timestamp, agent reachability and local show output. Restrict management source and use SNMPv 3.
SNMP queries UDP 161
Inspect
MIB/OID
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 455
IP SERVICES · VERIFICATION BRIDGE
SNMP manager and agent state · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
455
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | NMS manager -> MIB/OID | SNMP queries UDP 161
Mechanism / state | NMS correlates state over time | SNMPv 3 authPriv protects messages
Result / boundary | Correlate OID value, timestamp, agent reachability and local show output. Restrict management source and use SNMPv 3. | SNMPv 1/v 2 c community strings do not provide modern encryption. A stale polling value is not the same as live interface status.
Bridge: Activity 8: NAT, DHCP, DNS and time
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 456
IP SERVICES · ARCHITECTURE
Syslog severity and facility · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
456
Device event
Originating operational event
Syslog message
Facility, severity, mnemonic, timestamp
Collector
Receives and filters log records
%LINK-3-UPDOWN
logging trap warnings
Boundary to inspect
Threshold 4 includes 0-4, not 5-7
Identify facility, severity and mnemonic

## Slide 457
IP SERVICES · MECHANISM
Syslog severity and facility · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
457
1
Event selects facility/severity
2
Message receives timestamp
3
Transport sends collector record
4
Collector filters by configured threshold
State/input
%LINK-3-UPDOWN
Observable consequence
logging trap warnings
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 458
IP SERVICES · ANNOTATED TECHNICAL EXHIBIT
Syslog severity and facility · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
458
%LINK-3-UPDOWN
Severity 0 emergencies ->7 debugging
logging host 192.0.2.60
logging trap warnings
INPUT / IDENTITY
Device event · Event selects facility/severity
DECISION / STATE
Transport sends collector record
READBACK / RESULT
Collector filters by configured threshold
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 459
IP SERVICES · DIAGNOSIS
Syslog severity and facility · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
459
Does the observed state satisfy the contract?
Mismatch / control
Threshold 4 includes 0-4, not 5-7. UDP syslog can lose messages; correlated timestamps require reliable time.
Conforming / verification
Identify facility, severity and mnemonic. Compare configured threshold with the missing event level.
%LINK-3-UPDOWN
Inspect
Collector
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 460
IP SERVICES · VERIFICATION BRIDGE
Syslog severity and facility · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
460
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Device event -> Collector | %LINK-3-UPDOWN
Mechanism / state | Collector filters by configured threshold | logging trap warnings
Result / boundary | Identify facility, severity and mnemonic. Compare configured threshold with the missing event level. | Threshold 4 includes 0-4, not 5-7. UDP syslog can lose messages; correlated timestamps require reliable time.
Bridge: Activity 8: NAT, DHCP, DNS and time
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 461
IP SERVICES · ARCHITECTURE
QoS classification and management transfer · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
461
Class map
Traffic match and DSCP policy
Queue/scheduler
Congestion queue and scheduling policy
Management channel
Secure administration/transfer transport
EF DSCP 46; AF 41 DSCP 34
SSH 22; TFTP 69; FTP 21 control
Boundary to inspect
QoS does not create bandwidth
Compare offered rate with policy counters, queue drops and latency

## Slide 462
IP SERVICES · MECHANISM
QoS classification and management transfer · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
462
1
Classification identifies traffic
2
Marking assigns DSCP
3
Congestion invokes queue/drop policy
4
Secure management transfers configuration
State/input
EF DSCP 46; AF 41 DSCP 34
Observable consequence
SSH 22; TFTP 69; FTP 21 control
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 463
IP SERVICES · ANNOTATED TECHNICAL EXHIBIT
QoS classification and management transfer · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
463
EF DSCP 46; AF 41 DSCP 34
Policing can drop/remark excess
Shaping buffers/delays excess
SSH 22; TFTP 69; FTP 21 control
INPUT / IDENTITY
Class map · Classification identifies traffic
DECISION / STATE
Congestion invokes queue/drop policy
READBACK / RESULT
Secure management transfers configuration
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 464
IP SERVICES · DIAGNOSIS
QoS classification and management transfer · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
464
Does the observed state satisfy the contract?
Mismatch / control
QoS does not create bandwidth. Strict priority needs limits; TFTP lacks authentication; FTP data channels differ from control.
Conforming / verification
Compare offered rate with policy counters, queue drops and latency. Use SSH-based management and verify transferred file integrity.
EF DSCP 46; AF 41 DSCP 34
Inspect
Management channel
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 465
IP SERVICES · VERIFICATION BRIDGE
QoS classification and management transfer · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
465
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Class map -> Management channel | EF DSCP 46; AF 41 DSCP 34
Mechanism / state | Secure management transfers configuration | SSH 22; TFTP 69; FTP 21 control
Result / boundary | Compare offered rate with policy counters, queue drops and latency. Use SSH-based management and verify transferred file integrity. | QoS does not create bandwidth. Strict priority needs limits; TFTP lacks authentication; FTP data channels differ from control.
Bridge: Activity 8: NAT, DHCP, DNS and time
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 466
IP SERVICES · ARCHITECTURE
NTP server and client association · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
466
Trusted upstream
Trusted upstream synchronized source
IOS time service
Provides selected synchronized time
Downstream client
Associates and estimates clock offset
ntp server 192.0.2.123
Unsynchronized stratum 16 is unusable
Boundary to inspect
A server's configured source may be unreachable; serving an unsynchronized clock is not evidence of trusted time
Read selected peer, synchronization state, stratum and clock on both server/client; compare log timestamps with trusted reference.

## Slide 467
IP SERVICES · MECHANISM
NTP server and client association · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
467
1
IOS synchronizes to upstream
2
Downstream queries IOS server
3
Stratum increases per synchronization level
4
Offset/status determines usable time
State/input
ntp server 192.0.2.123
Observable consequence
Unsynchronized stratum 16 is unusable
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 468
IP SERVICES · ANNOTATED TECHNICAL EXHIBIT
NTP server and client association · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
468
ntp server 192.0.2.123
show ntp status
Downstream ntp server 10.10.10.1
Unsynchronized stratum 16 is unusable
INPUT / IDENTITY
Trusted upstream · IOS synchronizes to upstream
DECISION / STATE
Stratum increases per synchronization level
READBACK / RESULT
Offset/status determines usable time
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 469
IP SERVICES · DIAGNOSIS
NTP server and client association · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
469
Does the observed state satisfy the contract?
Mismatch / control
A server's configured source may be unreachable; serving an unsynchronized clock is not evidence of trusted time. Do not use arbitrary ntp master to hide upstream failure.
Conforming / verification
Read selected peer, synchronization state, stratum and clock on both server/client; compare log timestamps with trusted reference.
ntp server 192.0.2.123
Inspect
Downstream client
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 470
IP SERVICES · VERIFICATION BRIDGE
NTP server and client association · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
470
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Trusted upstream -> Downstream client | ntp server 192.0.2.123
Mechanism / state | Offset/status determines usable time | Unsynchronized stratum 16 is unusable
Result / boundary | Read selected peer, synchronization state, stratum and clock on both server/client; compare log timestamps with trusted reference. | A server's configured source may be unreachable; serving an unsynchronized clock is not evidence of trusted time. Do not use arbitrary ntp master to hide upstream failure.
Bridge: Activity 8: NAT, DHCP, DNS and time
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 471
IP SERVICES · ARCHITECTURE
IOS DHCP client interface state · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
471
WAN interface
Lease-consuming routed interface
Provider DHCP service
Address/options provider
Installed default/options
Address, route and lease evidence
interface Gi0/0
show ip interface brief
Boundary to inspect
DHCP client role differs from server pool and relay
Record interface leased address, lease lifetime and received options; inspect route table and provider next-hop reachability.

## Slide 472
IP SERVICES · MECHANISM
IOS DHCP client interface state · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
472
1
Client interface requests lease
2
Server supplies address/mask/options
3
IOS installs leased address
4
Lease renews before expiry
State/input
interface Gi0/0
Observable consequence
show ip interface brief
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 473
IP SERVICES · ANNOTATED TECHNICAL EXHIBIT
IOS DHCP client interface state · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
473
interface Gi0/0
ip address dhcp
no shutdown
show dhcp lease
show ip interface brief
INPUT / IDENTITY
WAN interface · Client interface requests lease
DECISION / STATE
IOS installs leased address
READBACK / RESULT
Lease renews before expiry
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 474
IP SERVICES · DIAGNOSIS
IOS DHCP client interface state · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
474
Does the observed state satisfy the contract?
Mismatch / control
DHCP client role differs from server pool and relay. Lease acceptance does not prove DNS/default route/options are intended.
Conforming / verification
Record interface leased address, lease lifetime and received options; inspect route table and provider next-hop reachability.
interface Gi0/0
Inspect
Installed default/options
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 475
IP SERVICES · VERIFICATION BRIDGE
IOS DHCP client interface state · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
475
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | WAN interface -> Installed default/options | interface Gi0/0
Mechanism / state | Lease renews before expiry | show ip interface brief
Result / boundary | Record interface leased address, lease lifetime and received options; inspect route table and provider next-hop reachability. | DHCP client role differs from server pool and relay. Lease acceptance does not prove DNS/default route/options are intended.
Bridge: Activity 8: NAT, DHCP, DNS and time
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 476
IP SERVICES · ARCHITECTURE
QoS congestion decisions · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
476
Classifier/marker
Assigns traffic class and per-hop marking
Egress queues
Scheduling and congestion-drop state
Congestion-avoidance policy
Chooses excess-traffic behavior
Classification -> marking -> queuing
Policing drop/remark; shaping delay
Boundary to inspect
A queue scheduler and congestion-avoidance algorithm serve different roles
Inspect class matches, offered/dropped rates, queue depth and latency; compare baseline with congested test rather than asserting QoS creates bandwidth.

## Slide 477
IP SERVICES · MECHANISM
QoS congestion decisions · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
477
1
Packet matches class
2
DSCP marks per-hop behavior
3
Queue schedules during congestion
4
Avoidance drops selected packets before hard queue exhaustion
State/input
Classification -> marking -> queuing
Observable consequence
Policing drop/remark; shaping delay
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 478
IP SERVICES · ANNOTATED TECHNICAL EXHIBIT
QoS congestion decisions · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
478
Classification -> marking -> queuing
Tail drop: queue full
WRED: probabilistic early discard
Policing drop/remark; shaping delay
INPUT / IDENTITY
Classifier/marker · Packet matches class
DECISION / STATE
Queue schedules during congestion
READBACK / RESULT
Avoidance drops selected packets before hard queue exhaustion
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 479
IP SERVICES · DIAGNOSIS
QoS congestion decisions · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
479
Does the observed state satisfy the contract?
Mismatch / control
A queue scheduler and congestion-avoidance algorithm serve different roles. Marked priority has no effect unless downstream policy recognizes it.
Conforming / verification
Inspect class matches, offered/dropped rates, queue depth and latency; compare baseline with congested test rather than asserting QoS creates bandwidth.
Classification -> marking -> queuing
Inspect
Congestion-avoidance policy
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 480
IP SERVICES · VERIFICATION BRIDGE
QoS congestion decisions · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
480
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Classifier/marker -> Congestion-avoidance policy | Classification -> marking -> queuing
Mechanism / state | Avoidance drops selected packets before hard queue exhaustion | Policing drop/remark; shaping delay
Result / boundary | Inspect class matches, offered/dropped rates, queue depth and latency; compare baseline with congested test rather than asserting QoS creates bandwidth. | A queue scheduler and congestion-avoidance algorithm serve different roles. Marked priority has no effect unless downstream policy recognizes it.
Bridge: Activity 8: NAT, DHCP, DNS and time
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 481
15% · CURRENT CCNA V 1.1
Security Fundamentals
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
481
Security Fundamentals
Named boundaries -> runtime trace -> exact contract -> failure/control -> acceptance evidence

## Slide 482
SECURITY FUNDAMENTALS · ARCHITECTURE
Threat-vulnerability-exploit chain · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
482
Asset
Resource with business/technical value
Weak control
Exploitable configuration weakness
Adversary action
Unauthorized action exploiting weakness
Asset: VTY management
Control: SSH + ACL + AAA
Boundary to inspect
Threat is an actor/event, vulnerability is a weakness, exploit is a method
Show observed connection, account/audit event and relevant control; distinguish risk hypothesis from confirmed evidence.

## Slide 483
SECURITY FUNDAMENTALS · MECHANISM
Threat-vulnerability-exploit chain · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
483
1
Exposure identifies reachable asset
2
Vulnerability enables technique
3
Exploit triggers unauthorized action
4
Control reduces likelihood or impact
State/input
Asset: VTY management
Observable consequence
Control: SSH + ACL + AAA
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 484
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Threat-vulnerability-exploit chain · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
484
Asset: VTY management
Weakness: Telnet + weak password
Exploit: credential interception
Control: SSH + ACL + AAA
INPUT / IDENTITY
Asset · Exposure identifies reachable asset
DECISION / STATE
Exploit triggers unauthorized action
READBACK / RESULT
Control reduces likelihood or impact
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 485
SECURITY FUNDAMENTALS · DIAGNOSIS
Threat-vulnerability-exploit chain · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
485
Does the observed state satisfy the contract?
Mismatch / control
Threat is an actor/event, vulnerability is a weakness, exploit is a method. Avoid treating labels as proof of compromise.
Conforming / verification
Show observed connection, account/audit event and relevant control; distinguish risk hypothesis from confirmed evidence.
Asset: VTY management
Inspect
Adversary action
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 486
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
Threat-vulnerability-exploit chain · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
486
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Asset -> Adversary action | Asset: VTY management
Mechanism / state | Control reduces likelihood or impact | Control: SSH + ACL + AAA
Result / boundary | Show observed connection, account/audit event and relevant control; distinguish risk hypothesis from confirmed evidence. | Threat is an actor/event, vulnerability is a weakness, exploit is a method. Avoid treating labels as proof of compromise.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 487
SECURITY FUNDAMENTALS · ARCHITECTURE
Security program evidence · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
487
Policy owner
Defines and owns required behavior
User behavior
Awareness and trained incident action
Technical control
Enforces and measures compliance
Policy: MFA required for admins
Evidence: MFA enforcement + report record
Boundary to inspect
A written policy is not evidence that enforcement works
Collect policy, control setting, exercise output and remediation owner; track exceptions explicitly.

## Slide 488
SECURITY FUNDAMENTALS · MECHANISM
Security program evidence · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
488
1
Policy defines requirement
2
Awareness communicates expectation
3
Training rehearses action
4
Audit tests whether controls operate
State/input
Policy: MFA required for admins
Observable consequence
Evidence: MFA enforcement + report record
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 489
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Security program evidence · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
489
Policy: MFA required for admins
Training: phishing report procedure
Evidence: MFA enforcement + report record
INPUT / IDENTITY
Policy owner · Policy defines requirement
DECISION / STATE
Training rehearses action
READBACK / RESULT
Audit tests whether controls operate
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 490
SECURITY FUNDAMENTALS · DIAGNOSIS
Security program evidence · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
490
Does the observed state satisfy the contract?
Mismatch / control
A written policy is not evidence that enforcement works. User awareness complements but does not replace technical control.
Conforming / verification
Collect policy, control setting, exercise output and remediation owner; track exceptions explicitly.
Policy: MFA required for admins
Inspect
Technical control
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 491
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
Security program evidence · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
491
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Policy owner -> Technical control | Policy: MFA required for admins
Mechanism / state | Audit tests whether controls operate | Evidence: MFA enforcement + report record
Result / boundary | Collect policy, control setting, exercise output and remediation owner; track exceptions explicitly. | A written policy is not evidence that enforcement works. User awareness complements but does not replace technical control.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 492
SECURITY FUNDAMENTALS · ARCHITECTURE
Local user and enable secrets · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
492
Local user DB
Configured device identity credentials
Privilege level
Permitted command privilege scope
CLI session
Authenticated operational context
username learner privilege 1 secret <unique-training-secret>
service password-encryption
Boundary to inspect
service password-encryption obfuscates some passwords and is not strong cryptographic protection
show running-config filtered for user/enable settings; test allowed commands without publishing secret values.

## Slide 493
SECURITY FUNDAMENTALS · MECHANISM
Local user and enable secrets · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
493
1
User authenticates
2
Privilege level authorizes commands
3
Enable secret controls escalation
4
Config stores protected secret representation
State/input
username learner privilege 1 secret <unique-training-secret>
Observable consequence
service password-encryption
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 494
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Local user and enable secrets · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
494
username learner privilege 1 secret <unique-training-secret>
enable secret <unique-training-secret>
service password-encryption
INPUT / IDENTITY
Local user DB · User authenticates
DECISION / STATE
Enable secret controls escalation
READBACK / RESULT
Config stores protected secret representation
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 495
SECURITY FUNDAMENTALS · DIAGNOSIS
Local user and enable secrets · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
495
Does the observed state satisfy the contract?
Mismatch / control
service password-encryption obfuscates some passwords and is not strong cryptographic protection. Never embed live credentials in course files.
Conforming / verification
show running-config filtered for user/enable settings; test allowed commands without publishing secret values.
username learner privilege 1 secret <unique-training-secret>
Inspect
CLI session
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 496
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
Local user and enable secrets · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
496
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Local user DB -> CLI session | username learner privilege 1 secret <unique-training-secret>
Mechanism / state | Config stores protected secret representation | service password-encryption
Result / boundary | show running-config filtered for user/enable settings; test allowed commands without publishing secret values. | service password-encryption obfuscates some passwords and is not strong cryptographic protection. Never embed live credentials in course files.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 497
SECURITY FUNDAMENTALS · ARCHITECTURE
SSH management prerequisites · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
497
Hostname/domain
Unique device naming and SSH prerequisites
RSA key
Server public-key cryptographic identity
VTY access
Allowed session methods and sources
hostname R1
transport input ssh
Boundary to inspect
Avoid enabling Telnet as a fallback
show ip ssh; test authenticated SSH from permitted source and rejected access from an unauthorized source.

## Slide 498
SECURITY FUNDAMENTALS · MECHANISM
SSH management prerequisites · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
498
1
Device key supports SSH server
2
Local or AAA authenticates user
3
VTY permits SSH transport
4
ACL restricts source
State/input
hostname R1
Observable consequence
transport input ssh
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 499
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
SSH management prerequisites · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
499
hostname R1
ip domain-name training.example
crypto key generate rsa modulus 2048
line vty 0 4
login local
transport input ssh
INPUT / IDENTITY
Hostname/domain · Device key supports SSH server
DECISION / STATE
VTY permits SSH transport
READBACK / RESULT
ACL restricts source
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 500
SECURITY FUNDAMENTALS · DIAGNOSIS
SSH management prerequisites · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
500
Does the observed state satisfy the contract?
Mismatch / control
Avoid enabling Telnet as a fallback. Keys, SSH version, user method and VTY lines must align.
Conforming / verification
show ip ssh; test authenticated SSH from permitted source and rejected access from an unauthorized source.
hostname R1
Inspect
VTY access
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 501
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
SSH management prerequisites · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
501
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Hostname/domain -> VTY access | hostname R1
Mechanism / state | ACL restricts source | transport input ssh
Result / boundary | show ip ssh; test authenticated SSH from permitted source and rejected access from an unauthorized source. | Avoid enabling Telnet as a fallback. Keys, SSH version, user method and VTY lines must align.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 502
SECURITY FUNDAMENTALS · ARCHITECTURE
Password and MFA policy · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
502
Knowledge factor
Secret known by user
Possession factor
Independent physical/token factor
Identity verifier
Checks identity and issues session
Password + hardware/security-key factor
MFA protects management identity
Boundary to inspect
MFA is not implemented by merely configuring two local passwords
Inspect identity policy, enrollment and successful/failed audit records; identify bypass paths and role scope.

## Slide 503
SECURITY FUNDAMENTALS · MECHANISM
Password and MFA policy · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
503
1
User presents credential
2
Verifier checks password
3
Second independent factor validates possession
4
Session receives authorized role
State/input
Password + hardware/security-key factor
Observable consequence
MFA protects management identity
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 504
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Password and MFA policy · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
504
Password + hardware/security-key factor
Two passwords are one factor type
MFA protects management identity
INPUT / IDENTITY
Knowledge factor · User presents credential
DECISION / STATE
Second independent factor validates possession
READBACK / RESULT
Session receives authorized role
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 505
SECURITY FUNDAMENTALS · DIAGNOSIS
Password and MFA policy · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
505
Does the observed state satisfy the contract?
Mismatch / control
MFA is not implemented by merely configuring two local passwords. Recovery and fallback methods must preserve the intended assurance.
Conforming / verification
Inspect identity policy, enrollment and successful/failed audit records; identify bypass paths and role scope.
Password + hardware/security-key factor
Inspect
Identity verifier
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 506
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
Password and MFA policy · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
506
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Knowledge factor -> Identity verifier | Password + hardware/security-key factor
Mechanism / state | Session receives authorized role | MFA protects management identity
Result / boundary | Inspect identity policy, enrollment and successful/failed audit records; identify bypass paths and role scope. | MFA is not implemented by merely configuring two local passwords. Recovery and fallback methods must preserve the intended assurance.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 507
SECURITY FUNDAMENTALS · ARCHITECTURE
AAA responsibility split · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
507
Authentication service
Proves user/device identity
Authorization policy
Decides permitted role or command
Accounting log
Records session and action evidence
Authentication: who are you?
Accounting: who changed VLAN 20 at14:02?
Boundary to inspect
Successful login does not grant every action
Use separate evidence for accepted identity, command permission and logged action; compare role to required task.

## Slide 508
SECURITY FUNDAMENTALS · MECHANISM
AAA responsibility split · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
508
1
Authentication proves identity
2
Authorization limits action
3
Accounting records action
4
Audit links account/time/command
State/input
Authentication: who are you?
Observable consequence
Accounting: who changed VLAN 20 at14:02?
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 509
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
AAA responsibility split · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
509
Authentication: who are you?
Authorization: may you configure VLAN?
Accounting: who changed VLAN 20 at14:02?
INPUT / IDENTITY
Authentication service · Authentication proves identity
DECISION / STATE
Accounting records action
READBACK / RESULT
Audit links account/time/command
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 510
SECURITY FUNDAMENTALS · DIAGNOSIS
AAA responsibility split · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
510
Does the observed state satisfy the contract?
Mismatch / control
Successful login does not grant every action. Accounting records support diagnosis but do not enforce authorization by themselves.
Conforming / verification
Use separate evidence for accepted identity, command permission and logged action; compare role to required task.
Authentication: who are you?
Inspect
Accounting log
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 511
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
AAA responsibility split · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
511
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Authentication service -> Accounting log | Authentication: who are you?
Mechanism / state | Audit links account/time/command | Accounting: who changed VLAN 20 at14:02?
Result / boundary | Use separate evidence for accepted identity, command permission and logged action; compare role to required task. | Successful login does not grant every action. Accounting records support diagnosis but do not enforce authorization by themselves.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 512
SECURITY FUNDAMENTALS · ARCHITECTURE
RADIUS and TACACS+ boundaries · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
512
Network device
Sends authentication/authorization request
AAA server
Evaluates centralized identity/policy
Admin or supplicant
Consumes permitted session/access
RADIUS UDP 1812 auth, 1813 accounting
RADIUS common for network access AAA
Boundary to inspect
Protocol roles and encryption scope differ
Confirm AAA server reachability and reject behavior; document local fallback without turning failures into unrestricted access.

## Slide 513
SECURITY FUNDAMENTALS · MECHANISM
RADIUS and TACACS+ boundaries · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
513
1
Device sends AAA request
2
Server checks identity/policy
3
Decision returns to device
4
Device enforces access/command role
State/input
RADIUS UDP 1812 auth, 1813 accounting
Observable consequence
RADIUS common for network access AAA
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 514
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
RADIUS and TACACS+ boundaries · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
514
RADIUS UDP 1812 auth, 1813 accounting
TACACS+ TCP 49
RADIUS common for network access AAA
INPUT / IDENTITY
Network device · Device sends AAA request
DECISION / STATE
Decision returns to device
READBACK / RESULT
Device enforces access/command role
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 515
SECURITY FUNDAMENTALS · DIAGNOSIS
RADIUS and TACACS+ boundaries · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
515
Does the observed state satisfy the contract?
Mismatch / control
Protocol roles and encryption scope differ. Network access and device administration are distinct authorization problems.
Conforming / verification
Confirm AAA server reachability and reject behavior; document local fallback without turning failures into unrestricted access.
RADIUS UDP 1812 auth, 1813 accounting
Inspect
Admin or supplicant
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 516
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
RADIUS and TACACS+ boundaries · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
516
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Network device -> Admin or supplicant | RADIUS UDP 1812 auth, 1813 accounting
Mechanism / state | Device enforces access/command role | RADIUS common for network access AAA
Result / boundary | Confirm AAA server reachability and reject behavior; document local fallback without turning failures into unrestricted access. | Protocol roles and encryption scope differ. Network access and device administration are distinct authorization problems.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 517
SECURITY FUNDAMENTALS · ARCHITECTURE
Site-to-site IPsec trust · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
517
Site A gateway
Protects source site network
Encrypted tunnel
Encrypted transit and peer authentication
Site B gateway
Decrypts and routes to remote site
Local 10.10.0.0/16
IKE UDP 500; NAT-T UDP 4500
Boundary to inspect
Tunnel-up is not proof both subnet routes and policies work
Correlate protected-subnet selectors, security associations, packet counters and remote application reachability.

## Slide 518
SECURITY FUNDAMENTALS · MECHANISM
Site-to-site IPsec trust · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
518
1
Interesting traffic matches policy
2
Peers authenticate and negotiate
3
IPsec protects transit payload
4
Remote gateway decrypts and routes
State/input
Local 10.10.0.0/16
Observable consequence
IKE UDP 500; NAT-T UDP 4500
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 519
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Site-to-site IPsec trust · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
519
Local 10.10.0.0/16
Remote 10.20.0.0/16
ESP IP protocol 50
IKE UDP 500; NAT-T UDP 4500
INPUT / IDENTITY
Site A gateway · Interesting traffic matches policy
DECISION / STATE
IPsec protects transit payload
READBACK / RESULT
Remote gateway decrypts and routes
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 520
SECURITY FUNDAMENTALS · DIAGNOSIS
Site-to-site IPsec trust · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
520
Does the observed state satisfy the contract?
Mismatch / control
Tunnel-up is not proof both subnet routes and policies work. Encryption protects transit, not compromised endpoints.
Conforming / verification
Correlate protected-subnet selectors, security associations, packet counters and remote application reachability.
Local 10.10.0.0/16
Inspect
Site B gateway
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 521
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
Site-to-site IPsec trust · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
521
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Site A gateway -> Site B gateway | Local 10.10.0.0/16
Mechanism / state | Remote gateway decrypts and routes | IKE UDP 500; NAT-T UDP 4500
Result / boundary | Correlate protected-subnet selectors, security associations, packet counters and remote application reachability. | Tunnel-up is not proof both subnet routes and policies work. Encryption protects transit, not compromised endpoints.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 522
SECURITY FUNDAMENTALS · ARCHITECTURE
Remote-access VPN roles · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
522
Remote user
Authenticates individual external client
VPN headend
VPN access and route-policy boundary
Internal service
Applies destination authorization
Remote client -> TLS/IPsec VPN
Allowed service10.20.0.50:443
Boundary to inspect
VPN authentication does not authorize every internal service
Verify client routes, assigned address, headend policy and service access; record identity and tunnel evidence separately.

## Slide 523
SECURITY FUNDAMENTALS · MECHANISM
Remote-access VPN roles · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
523
1
User authenticates to headend
2
VPN policy assigns tunnel/access
3
Traffic follows full/split route policy
4
Internal service applies own authorization
State/input
Remote client -> TLS/IPsec VPN
Observable consequence
Allowed service10.20.0.50:443
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 524
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Remote-access VPN roles · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
524
Remote client -> TLS/IPsec VPN
Assigned client pool 10.30.0.0/24
Allowed service10.20.0.50:443
INPUT / IDENTITY
Remote user · User authenticates to headend
DECISION / STATE
Traffic follows full/split route policy
READBACK / RESULT
Internal service applies own authorization
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 525
SECURITY FUNDAMENTALS · DIAGNOSIS
Remote-access VPN roles · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
525
Does the observed state satisfy the contract?
Mismatch / control
VPN authentication does not authorize every internal service. Split tunneling changes which traffic crosses enterprise controls.
Conforming / verification
Verify client routes, assigned address, headend policy and service access; record identity and tunnel evidence separately.
Remote client -> TLS/IPsec VPN
Inspect
Internal service
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 526
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
Remote-access VPN roles · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
526
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Remote user -> Internal service | Remote client -> TLS/IPsec VPN
Mechanism / state | Internal service applies own authorization | Allowed service10.20.0.50:443
Result / boundary | Verify client routes, assigned address, headend policy and service access; record identity and tunnel evidence separately. | VPN authentication does not authorize every internal service. Split tunneling changes which traffic crosses enterprise controls.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 527
SECURITY FUNDAMENTALS · ARCHITECTURE
Standard ACL source matching · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
527
Source address
Address field matched by standard ACL
Wildcard mask
Compare 0 bits and ignore 1 bits
Ordered rules
First-match permit/deny policy
access-list 10 permit 10.10.10.0 0.0.0.255
ip access-group 10 out
Boundary to inspect
Standard ACL matches source only
show access-lists; verify hit counters and direction

## Slide 528
SECURITY FUNDAMENTALS · MECHANISM
Standard ACL source matching · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
528
1
Packet reaches ACL binding
2
Rules evaluate top-down
3
First match permits/denies
4
Implicit deny handles no match
State/input
access-list 10 permit 10.10.10.0 0.0.0.255
Observable consequence
ip access-group 10 out
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 529
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Standard ACL source matching · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
529
access-list 10 permit 10.10.10.0 0.0.0.255
interface Gi0/1
ip access-group 10 out
INPUT / IDENTITY
Source address · Packet reaches ACL binding
DECISION / STATE
First match permits/denies
READBACK / RESULT
Implicit deny handles no match
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 530
SECURITY FUNDAMENTALS · DIAGNOSIS
Standard ACL source matching · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
530
Does the observed state satisfy the contract?
Mismatch / control
Standard ACL matches source only. Placement near destination avoids unnecessarily blocking that source from unrelated destinations.
Conforming / verification
show access-lists; verify hit counters and direction. Explain which flows share source and would be affected.
access-list 10 permit 10.10.10.0 0.0.0.255
Inspect
Ordered rules
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 531
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
Standard ACL source matching · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
531
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Source address -> Ordered rules | access-list 10 permit 10.10.10.0 0.0.0.255
Mechanism / state | Implicit deny handles no match | ip access-group 10 out
Result / boundary | show access-lists; verify hit counters and direction. Explain which flows share source and would be affected. | Standard ACL matches source only. Placement near destination avoids unnecessarily blocking that source from unrelated destinations.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 532
SECURITY FUNDAMENTALS · ARCHITECTURE
Extended ACL tuple control · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
532
IP/protocol tuple
Source/destination/protocol fields
Destination port
Transport service identifier
Ordered ACEs
Ordered first-match decisions
ip access-list extended WEB_ONLY
deny ip any any log
Boundary to inspect
The source port is usually ephemeral; HTTPS destination port 443 identifies service
Test allowed 443 and denied 22 with same source/destination; compare ACE counters and intended interface direction.

## Slide 533
SECURITY FUNDAMENTALS · MECHANISM
Extended ACL tuple control · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
533
1
Packet tuple evaluated
2
Protocol/address/port all match
3
First matching ACE decides
4
Unmatched traffic meets implicit deny
State/input
ip access-list extended WEB_ONLY
Observable consequence
deny ip any any log
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 534
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Extended ACL tuple control · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
534
ip access-list extended WEB_ONLY
permit tcp 10.10.10.0 0.0.0.255 host 10.20.20.50 eq 443
deny ip any any log
INPUT / IDENTITY
IP/protocol tuple · Packet tuple evaluated
DECISION / STATE
First matching ACE decides
READBACK / RESULT
Unmatched traffic meets implicit deny
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 535
SECURITY FUNDAMENTALS · DIAGNOSIS
Extended ACL tuple control · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
535
Does the observed state satisfy the contract?
Mismatch / control
The source port is usually ephemeral; HTTPS destination port 443 identifies service. Rule order changes behavior.
Conforming / verification
Test allowed 443 and denied 22 with same source/destination; compare ACE counters and intended interface direction.
ip access-list extended WEB_ONLY
Inspect
Ordered ACEs
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 536
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
Extended ACL tuple control · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
536
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | IP/protocol tuple -> Ordered ACEs | ip access-list extended WEB_ONLY
Mechanism / state | Unmatched traffic meets implicit deny | deny ip any any log
Result / boundary | Test allowed 443 and denied 22 with same source/destination; compare ACE counters and intended interface direction. | The source port is usually ephemeral; HTTPS destination port 443 identifies service. Rule order changes behavior.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 537
SECURITY FUNDAMENTALS · ARCHITECTURE
ACL wildcard mathematics · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
537
Address bits
Input IPv4 value
Wildcard bits
Bitwise matching care/ignore pattern
Match predicate
Equal compared bits cause match
10.10.10.0 wildcard 0.0.0.255
host 10.10.10.5 = wildcard 0.0.0.0
Boundary to inspect
Wildcard is not always a subnet mask and need not be contiguous
For /27 mask 255.255.255.224, wildcard 0.0.0.31

## Slide 538
SECURITY FUNDAMENTALS · MECHANISM
ACL wildcard mathematics · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
538
1
Wildcard 0 means compare bit
2
Wildcard 1 means ignore bit
3
Address undergoes mask comparison
4
Matching tuple advances to ACE action
State/input
10.10.10.0 wildcard 0.0.0.255
Observable consequence
host 10.10.10.5 = wildcard 0.0.0.0
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 539
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
ACL wildcard mathematics · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
539
10.10.10.0 wildcard 0.0.0.255
Matches 10.10.10.0-255
host 10.10.10.5 = wildcard 0.0.0.0
INPUT / IDENTITY
Address bits · Wildcard 0 means compare bit
DECISION / STATE
Address undergoes mask comparison
READBACK / RESULT
Matching tuple advances to ACE action
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 540
SECURITY FUNDAMENTALS · DIAGNOSIS
ACL wildcard mathematics · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
540
Does the observed state satisfy the contract?
Mismatch / control
Wildcard is not always a subnet mask and need not be contiguous. Inverting a mask is valid for subnet-based matching.
Conforming / verification
For /27 mask 255.255.255.224, wildcard 0.0.0.31. Check boundary .32-.63 before applying.
10.10.10.0 wildcard 0.0.0.255
Inspect
Match predicate
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 541
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
ACL wildcard mathematics · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
541
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Address bits -> Match predicate | 10.10.10.0 wildcard 0.0.0.255
Mechanism / state | Matching tuple advances to ACE action | host 10.10.10.5 = wildcard 0.0.0.0
Result / boundary | For /27 mask 255.255.255.224, wildcard 0.0.0.31. Check boundary .32-.63 before applying. | Wildcard is not always a subnet mask and need not be contiguous. Inverting a mask is valid for subnet-based matching.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 542
SECURITY FUNDAMENTALS · ARCHITECTURE
Port-security admission and violations · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
542
Access port
Physical edge admission boundary
Secure MAC list
Permitted learned/static identities
Violation policy
Drop, counter or err-disable response
interface Gi1/0/10
switchport port-security violation restrict
Boundary to inspect
Protect drops silently; restrict drops and records; shutdown err-disables
show port-security interface

## Slide 543
SECURITY FUNDAMENTALS · MECHANISM
Port-security admission and violations · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
543
1
MAC source is learned or fixed
2
Maximum count limits devices
3
Violation action applies
4
Counter/log records event
State/input
interface Gi1/0/10
Observable consequence
switchport port-security violation restrict
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 544
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Port-security admission and violations · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
544
interface Gi1/0/10
switchport port-security
switchport port-security maximum 1
switchport port-security mac-address sticky
switchport port-security violation restrict
INPUT / IDENTITY
Access port · MAC source is learned or fixed
DECISION / STATE
Violation action applies
READBACK / RESULT
Counter/log records event
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 545
SECURITY FUNDAMENTALS · DIAGNOSIS
Port-security admission and violations · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
545
Does the observed state satisfy the contract?
Mismatch / control
Protect drops silently; restrict drops and records; shutdown err-disables. Sticky entries learned in running config need save to persist.
Conforming / verification
show port-security interface. Compare secure count, violation mode/counter and port state after an extra source MAC.
interface Gi1/0/10
Inspect
Violation policy
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 546
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
Port-security admission and violations · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
546
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Access port -> Violation policy | interface Gi1/0/10
Mechanism / state | Counter/log records event | switchport port-security violation restrict
Result / boundary | show port-security interface. Compare secure count, violation mode/counter and port state after an extra source MAC. | Protect drops silently; restrict drops and records; shutdown err-disables. Sticky entries learned in running config need save to persist.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 547
SECURITY FUNDAMENTALS · ARCHITECTURE
DHCP snooping and ARP inspection · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
547
Trusted DHCP uplink
Server-reply trust boundary
Binding table
Lease-derived IP/MAC/VLAN/port data
DAI access port
Rejects invalid ARP address claims
ip dhcp snooping
Trusted uplink: DHCP server direction
Boundary to inspect
Trust only the proper uplink; DAI depends on binding knowledge or explicit ARP ACL for static hosts
show ip dhcp snooping binding; show ip arp inspection statistics

## Slide 548
SECURITY FUNDAMENTALS · MECHANISM
DHCP snooping and ARP inspection · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
548
1
Snooping rejects untrusted server replies
2
Lease creates IP/MAC/VLAN/port binding
3
DAI checks ARP claim
4
Invalid claim is dropped
State/input
ip dhcp snooping
Observable consequence
Trusted uplink: DHCP server direction
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 549
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
DHCP snooping and ARP inspection · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
549
ip dhcp snooping
ip dhcp snooping vlan 10
ip arp inspection vlan 10
Trusted uplink: DHCP server direction
INPUT / IDENTITY
Trusted DHCP uplink · Snooping rejects untrusted server replies
DECISION / STATE
DAI checks ARP claim
READBACK / RESULT
Invalid claim is dropped
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 550
SECURITY FUNDAMENTALS · DIAGNOSIS
DHCP snooping and ARP inspection · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
550
Does the observed state satisfy the contract?
Mismatch / control
Trust only the proper uplink; DAI depends on binding knowledge or explicit ARP ACL for static hosts. Trusting all ports defeats protection.
Conforming / verification
show ip dhcp snooping binding; show ip arp inspection statistics. Map claimed IP/MAC to lease binding and ingress port.
ip dhcp snooping
Inspect
DAI access port
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 551
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
DHCP snooping and ARP inspection · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
551
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Trusted DHCP uplink -> DAI access port | ip dhcp snooping
Mechanism / state | Invalid claim is dropped | Trusted uplink: DHCP server direction
Result / boundary | show ip dhcp snooping binding; show ip arp inspection statistics. Map claimed IP/MAC to lease binding and ingress port. | Trust only the proper uplink; DAI depends on binding knowledge or explicit ARP ACL for static hosts. Trusting all ports defeats protection.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 552
SECURITY FUNDAMENTALS · ARCHITECTURE
Wireless WPA and authentication · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
552
Supplicant
EAP or shared-secret client identity
AP/WLC
WLAN security/network policy endpoint
PSK or AAA backend
Enterprise identity or PSK secret
WPA2-Personal: shared PSK
WPA2 AES/CCMP
Boundary to inspect
A hidden SSID is not an authentication control
Inspect SSID security settings and client authentication status; verify intended VLAN and authorized connectivity after association.

## Slide 553
SECURITY FUNDAMENTALS · MECHANISM
Wireless WPA and authentication · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
553
1
Client selects WLAN
2
Authentication proves credential
3
Key exchange derives session protection
4
Encrypted data follows authorized VLAN
State/input
WPA2-Personal: shared PSK
Observable consequence
WPA2 AES/CCMP
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 554
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Wireless WPA and authentication · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
554
WPA2-Personal: shared PSK
WPA2-Enterprise: 802.1 X/EAP + AAA
WPA3-Personal: SAE
WPA2 AES/CCMP
INPUT / IDENTITY
Supplicant · Client selects WLAN
DECISION / STATE
Key exchange derives session protection
READBACK / RESULT
Encrypted data follows authorized VLAN
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 555
SECURITY FUNDAMENTALS · DIAGNOSIS
Wireless WPA and authentication · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
555
Does the observed state satisfy the contract?
Mismatch / control
A hidden SSID is not an authentication control. Shared PSKs reduce identity attribution; choose WLAN method consistent with users/devices.
Conforming / verification
Inspect SSID security settings and client authentication status; verify intended VLAN and authorized connectivity after association.
WPA2-Personal: shared PSK
Inspect
PSK or AAA backend
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 556
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
Wireless WPA and authentication · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
556
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Supplicant -> PSK or AAA backend | WPA2-Personal: shared PSK
Mechanism / state | Encrypted data follows authorized VLAN | WPA2 AES/CCMP
Result / boundary | Inspect SSID security settings and client authentication status; verify intended VLAN and authorized connectivity after association. | A hidden SSID is not an authentication control. Shared PSKs reduce identity attribution; choose WLAN method consistent with users/devices.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 557
SECURITY FUNDAMENTALS · ARCHITECTURE
Physical access and identity controls · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
557
Secure equipment room
Controls access to physical equipment
Console interface
Local management bypass boundary
Administrator identity
Authenticated authorized operator
Controls: locked rack + visitor log
Biometric: inherence factor
Boundary to inspect
Physical possession can bypass network-layer assumptions; certificates require trust/validity/revocation checks
Compare access record, identity verification and command audit; verify least privilege and documented recovery path.

## Slide 558
SECURITY FUNDAMENTALS · MECHANISM
Physical access and identity controls · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
558
1
Physical control restricts device access
2
Identity verifier checks factor
3
Authorization scopes configuration
4
Audit correlates entry and change
State/input
Controls: locked rack + visitor log
Observable consequence
Biometric: inherence factor
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 559
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
Physical access and identity controls · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
559
Controls: locked rack + visitor log
Identity: password, certificate, biometric
Certificate: issuer/subject/validity
Biometric: inherence factor
INPUT / IDENTITY
Secure equipment room · Physical control restricts device access
DECISION / STATE
Authorization scopes configuration
READBACK / RESULT
Audit correlates entry and change
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 560
SECURITY FUNDAMENTALS · DIAGNOSIS
Physical access and identity controls · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
560
Does the observed state satisfy the contract?
Mismatch / control
Physical possession can bypass network-layer assumptions; certificates require trust/validity/revocation checks. A biometric plus password uses different factors.
Conforming / verification
Compare access record, identity verification and command audit; verify least privilege and documented recovery path.
Controls: locked rack + visitor log
Inspect
Administrator identity
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 561
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
Physical access and identity controls · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
561
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Secure equipment room -> Administrator identity | Controls: locked rack + visitor log
Mechanism / state | Audit correlates entry and change | Biometric: inherence factor
Result / boundary | Compare access record, identity verification and command audit; verify least privilege and documented recovery path. | Physical possession can bypass network-layer assumptions; certificates require trust/validity/revocation checks. A biometric plus password uses different factors.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 562
SECURITY FUNDAMENTALS · ARCHITECTURE
WPA lineage and WPA2 PSK WLAN evidence · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
562
WLAN security object
Cipher/authentication and VLAN mapping
Shared PSK
Shared synthetic authentication material
Client key exchange
Session-key derivation and protection
SSID TRAINING
Policy Profile VLAN 20
Boundary to inspect
Legacy WPA/TKIP is obsolete protection
Read actual WLAN security state and connected-client authentication; validate correct PSK acceptance and incorrect PSK rejection in isolated simulator.

## Slide 563
SECURITY FUNDAMENTALS · MECHANISM
WPA lineage and WPA2 PSK WLAN evidence · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
563
1
Legacy WPA used TKIP transition security
2
WPA2 selects AES/CCMP
3
PSK authenticates shared-secret possession
4
Handshake derives session keys
State/input
SSID TRAINING
Observable consequence
Policy Profile VLAN 20
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 564
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
WPA lineage and WPA2 PSK WLAN evidence · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
564
SSID TRAINING
Security WPA2-Personal / AES-CCMP
PSK <synthetic-training-only>
Policy Profile VLAN 20
INPUT / IDENTITY
WLAN security object · Legacy WPA used TKIP transition security
DECISION / STATE
PSK authenticates shared-secret possession
READBACK / RESULT
Handshake derives session keys
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 565
SECURITY FUNDAMENTALS · DIAGNOSIS
WPA lineage and WPA2 PSK WLAN evidence · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
565
Does the observed state satisfy the contract?
Mismatch / control
Legacy WPA/TKIP is obsolete protection. A WPA2PSK GUI task requires verifying security mode, cipher and policy VLAN, not only SSID visibility.
Conforming / verification
Read actual WLAN security state and connected-client authentication; validate correct PSK acceptance and incorrect PSK rejection in isolated simulator.
SSID TRAINING
Inspect
Client key exchange
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 566
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
WPA lineage and WPA2 PSK WLAN evidence · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
566
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | WLAN security object -> Client key exchange | SSID TRAINING
Mechanism / state | Handshake derives session keys | Policy Profile VLAN 20
Result / boundary | Read actual WLAN security state and connected-client authentication; validate correct PSK acceptance and incorrect PSK rejection in isolated simulator. | Legacy WPA/TKIP is obsolete protection. A WPA2PSK GUI task requires verifying security mode, cipher and policy VLAN, not only SSID visibility.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 567
SECURITY FUNDAMENTALS · ARCHITECTURE
IPsec tunnel and transport boundaries · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
567
Original IP packet
Inner source/destination and payload
IPsec security association
Algorithms, keys, selectors and peer state
Outer routed packet
Transport header or tunnel outer endpoints
ESP IP protocol50: confidentiality/integrity policy
Transport: original IP + protected upper-layer data
Boundary to inspect
AH does not provide confidentiality and is problematic across address-changing NAT
Identify mode, selectors, peer endpoints, ESP/AH choice and counters; verify remote-access/site-to-site routing plus traffic protection evidence.

## Slide 568
SECURITY FUNDAMENTALS · MECHANISM
IPsec tunnel and transport boundaries · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
568
1
Peers authenticate and negotiate SA
2
ESP protects selected payload
3
Tunnel encapsulates original IP packet
4
Transport retains original outer IP header
State/input
ESP IP protocol50: confidentiality/integrity policy
Observable consequence
Transport: original IP + protected upper-layer data
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 569
SECURITY FUNDAMENTALS · ANNOTATED TECHNICAL EXHIBIT
IPsec tunnel and transport boundaries · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
569
ESP IP protocol50: confidentiality/integrity policy
AH IP protocol51: authentication/integrity, no encryption
Tunnel: new outer IP + protected original packet
Transport: original IP + protected upper-layer data
INPUT / IDENTITY
Original IP packet · Peers authenticate and negotiate SA
DECISION / STATE
Tunnel encapsulates original IP packet
READBACK / RESULT
Transport retains original outer IP header
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 570
SECURITY FUNDAMENTALS · DIAGNOSIS
IPsec tunnel and transport boundaries · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
570
Does the observed state satisfy the contract?
Mismatch / control
AH does not provide confidentiality and is problematic across address-changing NAT. IPsec protection depends on negotiated algorithms and policy, not protocol name alone.
Conforming / verification
Identify mode, selectors, peer endpoints, ESP/AH choice and counters; verify remote-access/site-to-site routing plus traffic protection evidence.
ESP IP protocol50: confidentiality/integrity policy
Inspect
Outer routed packet
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 571
SECURITY FUNDAMENTALS · VERIFICATION BRIDGE
IPsec tunnel and transport boundaries · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
571
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Original IP packet -> Outer routed packet | ESP IP protocol50: confidentiality/integrity policy
Mechanism / state | Transport retains original outer IP header | Transport: original IP + protected upper-layer data
Result / boundary | Identify mode, selectors, peer endpoints, ESP/AH choice and counters; verify remote-access/site-to-site routing plus traffic protection evidence. | AH does not provide confidentiality and is problematic across address-changing NAT. IPsec protection depends on negotiated algorithms and policy, not protocol name alone.
Bridge: Activity 9: ACL/management or Activity 10: L2/wireless security
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 572
10% · CURRENT CCNA V 1.1
Automation and Programmability
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
572
Automation and Programmability
Named boundaries -> runtime trace -> exact contract -> failure/control -> acceptance evidence

## Slide 573
AUTOMATION AND PROGRAMMABILITY · ARCHITECTURE
Traditional and controller operation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
573
Device CLI
Individual device configuration channel
Controller API
Intent/state northbound contract
Southbound channel
Device programming southbound contract
Northbound: application->controller API
Desired state != observed state
Boundary to inspect
Centralization reduces coordination work but creates control-system dependencies
Read device state after controller operation; compare target inventory, requested policy and observed forwarding.

## Slide 574
AUTOMATION AND PROGRAMMABILITY · MECHANISM
Traditional and controller operation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
574
1
Traditional change targets each device
2
Controller accepts intent
3
Southbound programs device state
4
Telemetry returns observed operation
State/input
Northbound: application->controller API
Observable consequence
Desired state != observed state
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 575
AUTOMATION AND PROGRAMMABILITY · ANNOTATED TECHNICAL EXHIBIT
Traditional and controller operation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
575
Northbound: application->controller API
Southbound: controller->device
Desired state != observed state
INPUT / IDENTITY
Device CLI · Traditional change targets each device
DECISION / STATE
Southbound programs device state
READBACK / RESULT
Telemetry returns observed operation
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 576
AUTOMATION AND PROGRAMMABILITY · DIAGNOSIS
Traditional and controller operation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
576
Does the observed state satisfy the contract?
Mismatch / control
Centralization reduces coordination work but creates control-system dependencies. A controller acknowledgement does not prove device convergence.
Conforming / verification
Read device state after controller operation; compare target inventory, requested policy and observed forwarding.
Northbound: application->controller API
Inspect
Southbound channel
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 577
AUTOMATION AND PROGRAMMABILITY · VERIFICATION BRIDGE
Traditional and controller operation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
577
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Device CLI -> Southbound channel | Northbound: application->controller API
Mechanism / state | Telemetry returns observed operation | Desired state != observed state
Result / boundary | Read device state after controller operation; compare target inventory, requested policy and observed forwarding. | Centralization reduces coordination work but creates control-system dependencies. A controller acknowledgement does not prove device convergence.
Bridge: Activity 11: REST/JSON/automation or Activity 12: integrated verification
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 578
AUTOMATION AND PROGRAMMABILITY · ARCHITECTURE
Control and data plane separation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
578
Control process
Route/policy computation and exception handling
Forwarding table
Installed packet-forwarding contract
Packet ASIC
Fast forwarding execution engine
RIB -> FIB
Packet lookup: destination prefix + next-hop rewrite
Boundary to inspect
High control-plane CPU and data-plane congestion have different causes
Compare route computation, installed FIB and interface forwarding counters; identify whether failure is computation or packet execution.

## Slide 579
AUTOMATION AND PROGRAMMABILITY · MECHANISM
Control and data plane separation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
579
1
Control plane computes route/policy
2
Programs FIB/adjacency
3
Data plane forwards packets
4
Exceptions may punt to CPU
State/input
RIB -> FIB
Observable consequence
Packet lookup: destination prefix + next-hop rewrite
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 580
AUTOMATION AND PROGRAMMABILITY · ANNOTATED TECHNICAL EXHIBIT
Control and data plane separation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
580
RIB -> FIB
ARP/ND -> adjacency
Packet lookup: destination prefix + next-hop rewrite
INPUT / IDENTITY
Control process · Control plane computes route/policy
DECISION / STATE
Data plane forwards packets
READBACK / RESULT
Exceptions may punt to CPU
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 581
AUTOMATION AND PROGRAMMABILITY · DIAGNOSIS
Control and data plane separation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
581
Does the observed state satisfy the contract?
Mismatch / control
High control-plane CPU and data-plane congestion have different causes. Separation can be logical within the same device.
Conforming / verification
Compare route computation, installed FIB and interface forwarding counters; identify whether failure is computation or packet execution.
RIB -> FIB
Inspect
Packet ASIC
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 582
AUTOMATION AND PROGRAMMABILITY · VERIFICATION BRIDGE
Control and data plane separation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
582
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Control process -> Packet ASIC | RIB -> FIB
Mechanism / state | Exceptions may punt to CPU | Packet lookup: destination prefix + next-hop rewrite
Result / boundary | Compare route computation, installed FIB and interface forwarding counters; identify whether failure is computation or packet execution. | High control-plane CPU and data-plane congestion have different causes. Separation can be logical within the same device.
Bridge: Activity 11: REST/JSON/automation or Activity 12: integrated verification
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 583
AUTOMATION AND PROGRAMMABILITY · ARCHITECTURE
Overlay underlay and fabric roles · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
583
Underlay routed links
Tunnel endpoint IP reachability
Overlay virtual network
Tenant encapsulation and segmentation
Fabric edge/control
Endpoint/policy/control ownership
Inner tenant packet
Cisco DNA/SD-Access roles: edge, border, control plane
Boundary to inspect
Underlay reachability alone does not prove overlay policy or endpoint resolution
Check endpoint reachability, fabric role and policy mapping; inspect inner/outer address distinction in a sourced architecture exhibit.

## Slide 584
AUTOMATION AND PROGRAMMABILITY · MECHANISM
Overlay underlay and fabric roles · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
584
1
Underlay reaches tunnel endpoints
2
Overlay encapsulates tenant packet
3
Fabric policy maps identity/segment
4
Remote edge decapsulates
State/input
Inner tenant packet
Observable consequence
Cisco DNA/SD-Access roles: edge, border, control plane
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 585
AUTOMATION AND PROGRAMMABILITY · ANNOTATED TECHNICAL EXHIBIT
Overlay underlay and fabric roles · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
585
Inner tenant packet
Outer underlay IP + tunnel header
Cisco DNA/SD-Access roles: edge, border, control plane
INPUT / IDENTITY
Underlay routed links · Underlay reaches tunnel endpoints
DECISION / STATE
Fabric policy maps identity/segment
READBACK / RESULT
Remote edge decapsulates
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 586
AUTOMATION AND PROGRAMMABILITY · DIAGNOSIS
Overlay underlay and fabric roles · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
586
Does the observed state satisfy the contract?
Mismatch / control
Underlay reachability alone does not prove overlay policy or endpoint resolution. MTU must accommodate encapsulation overhead.
Conforming / verification
Check endpoint reachability, fabric role and policy mapping; inspect inner/outer address distinction in a sourced architecture exhibit.
Inner tenant packet
Inspect
Fabric edge/control
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 587
AUTOMATION AND PROGRAMMABILITY · VERIFICATION BRIDGE
Overlay underlay and fabric roles · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
587
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Underlay routed links -> Fabric edge/control | Inner tenant packet
Mechanism / state | Remote edge decapsulates | Cisco DNA/SD-Access roles: edge, border, control plane
Result / boundary | Check endpoint reachability, fabric role and policy mapping; inspect inner/outer address distinction in a sourced architecture exhibit. | Underlay reachability alone does not prove overlay policy or endpoint resolution. MTU must accommodate encapsulation overhead.
Bridge: Activity 11: REST/JSON/automation or Activity 12: integrated verification
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 588
AUTOMATION AND PROGRAMMABILITY · ARCHITECTURE
REST resource and HTTP verbs · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
588
API client
Authenticated resource request origin
Resource endpoint
URI identifying target state
Controller state
Current resource representation
GET read; POST create/action
200 OK;201 Created;401 unauthenticated
Boundary to inspect
Do not blindly repeat non-idempotent POST on timeout
Read back resource after mutation

## Slide 589
AUTOMATION AND PROGRAMMABILITY · MECHANISM
REST resource and HTTP verbs · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
589
1
Client identifies URI
2
Method requests resource operation
3
Server authorizes/evaluates
4
Status and representation describe result
State/input
GET read; POST create/action
Observable consequence
200 OK;201 Created;401 unauthenticated
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 590
AUTOMATION AND PROGRAMMABILITY · ANNOTATED TECHNICAL EXHIBIT
REST resource and HTTP verbs · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
590
GET read; POST create/action
PUT replace target representation
PATCH partial update; DELETE remove
200 OK;201 Created;401 unauthenticated
INPUT / IDENTITY
API client · Client identifies URI
DECISION / STATE
Server authorizes/evaluates
READBACK / RESULT
Status and representation describe result
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 591
AUTOMATION AND PROGRAMMABILITY · DIAGNOSIS
REST resource and HTTP verbs · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
591
Does the observed state satisfy the contract?
Mismatch / control
Do not blindly repeat non-idempotent POST on timeout. Preserve existing fields when endpoint semantics require complete replacement.
Conforming / verification
Read back resource after mutation. Distinguish 200 response from semantic correctness and 401 from 403 authorization failure.
GET read; POST create/action
Inspect
Controller state
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 592
AUTOMATION AND PROGRAMMABILITY · VERIFICATION BRIDGE
REST resource and HTTP verbs · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
592
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | API client -> Controller state | GET read; POST create/action
Mechanism / state | Status and representation describe result | 200 OK;201 Created;401 unauthenticated
Result / boundary | Read back resource after mutation. Distinguish 200 response from semantic correctness and 401 from 403 authorization failure. | Do not blindly repeat non-idempotent POST on timeout. Preserve existing fields when endpoint semantics require complete replacement.
Bridge: Activity 11: REST/JSON/automation or Activity 12: integrated verification
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 593
AUTOMATION AND PROGRAMMABILITY · ARCHITECTURE
REST authentication and HTTPS · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
593
API identity
Client credential and scoped role
TLS connection
Server trust and encrypted transit
Authorization policy
Permitted resource/method decisions
Authorization: Bearer <training-token>
HTTPS certificate validation enabled
Boundary to inspect
Never put live API keys into activity data or public repos
Use local mock tokens; verify 401 for missing token, 403 for insufficient role and allowed scoped GET with correct identity.

## Slide 594
AUTOMATION AND PROGRAMMABILITY · MECHANISM
REST authentication and HTTPS · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
594
1
TLS authenticates server/protects transit
2
Credential identifies client
3
Policy checks operation scope
4
Audit records action/result
State/input
Authorization: Bearer <training-token>
Observable consequence
HTTPS certificate validation enabled
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 595
AUTOMATION AND PROGRAMMABILITY · ANNOTATED TECHNICAL EXHIBIT
REST authentication and HTTPS · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
595
Authorization: Bearer <training-token>
Basic credential only over TLS
Token scope + expiry
HTTPS certificate validation enabled
INPUT / IDENTITY
API identity · TLS authenticates server/protects transit
DECISION / STATE
Policy checks operation scope
READBACK / RESULT
Audit records action/result
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 596
AUTOMATION AND PROGRAMMABILITY · DIAGNOSIS
REST authentication and HTTPS · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
596
Does the observed state satisfy the contract?
Mismatch / control
Never put live API keys into activity data or public repos. Authentication token possession does not imply unlimited authorization.
Conforming / verification
Use local mock tokens; verify 401 for missing token, 403 for insufficient role and allowed scoped GET with correct identity.
Authorization: Bearer <training-token>
Inspect
Authorization policy
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 597
AUTOMATION AND PROGRAMMABILITY · VERIFICATION BRIDGE
REST authentication and HTTPS · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
597
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | API identity -> Authorization policy | Authorization: Bearer <training-token>
Mechanism / state | Audit records action/result | HTTPS certificate validation enabled
Result / boundary | Use local mock tokens; verify 401 for missing token, 403 for insufficient role and allowed scoped GET with correct identity. | Never put live API keys into activity data or public repos. Authentication token possession does not imply unlimited authorization.
Bridge: Activity 11: REST/JSON/automation or Activity 12: integrated verification
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 598
AUTOMATION AND PROGRAMMABILITY · ARCHITECTURE
JSON typed data contracts · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
598
JSON object
String-keyed typed record
Array of interfaces
Ordered typed interface records
Parser
Syntax/type validation boundary
Object key hostname = "R1"
interfaces[0]: enabled = true; mtu = 1500
Boundary to inspect
JSON booleans are lowercase true/false; trailing commas/comments are invalid
Parse with python json.loads; check enabled is boolean and mtu integer; validate required interface keys before acting.

## Slide 599
AUTOMATION AND PROGRAMMABILITY · MECHANISM
JSON typed data contracts · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
599
1
Parser reads valid syntax
2
Object maps string keys
3
Array preserves sequence
4
Type controls consumer behavior
State/input
Object key hostname = "R1"
Observable consequence
interfaces[0]: enabled = true; mtu = 1500
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 600
AUTOMATION AND PROGRAMMABILITY · ANNOTATED TECHNICAL EXHIBIT
JSON typed data contracts · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
600
{"hostname":"R1","interfaces":[{"name":"Gi0/0","enabled":true,"mtu":1500}],"note":null}
INPUT / IDENTITY
JSON object · Parser reads valid syntax
DECISION / STATE
Array preserves sequence
READBACK / RESULT
Type controls consumer behavior
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 601
AUTOMATION AND PROGRAMMABILITY · DIAGNOSIS
JSON typed data contracts · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
601
Does the observed state satisfy the contract?
Mismatch / control
JSON booleans are lowercase true/false; trailing commas/comments are invalid. Numeric strings differ from numbers.
Conforming / verification
Parse with python json.loads; check enabled is boolean and mtu integer; validate required interface keys before acting.
Object key hostname = "R1"
Inspect
Parser
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 602
AUTOMATION AND PROGRAMMABILITY · VERIFICATION BRIDGE
JSON typed data contracts · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
602
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | JSON object -> Parser | Object key hostname = "R1"
Mechanism / state | Type controls consumer behavior | interfaces[0]: enabled = true; mtu = 1500
Result / boundary | Parse with python json.loads; check enabled is boolean and mtu integer; validate required interface keys before acting. | JSON booleans are lowercase true/false; trailing commas/comments are invalid. Numeric strings differ from numbers.
Bridge: Activity 11: REST/JSON/automation or Activity 12: integrated verification
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 603
AUTOMATION AND PROGRAMMABILITY · ARCHITECTURE
Ansible desired configuration · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
603
Inventory
Approved target identities and groups
Idempotent task
Declarative desired device lines
Device connection
Authenticated network command session
hosts: routers
lines: [hostname R1]
Boundary to inspect
Idempotence depends on module and task behavior; arbitrary shell tasks are not automatically idempotent
Validate inventory and inspect before/after configs; second identical run should report no change for an idempotent task.

## Slide 604
AUTOMATION AND PROGRAMMABILITY · MECHANISM
Ansible desired configuration · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
604
1
Inventory groups targets
2
Module gathers or configures state
3
Task evaluates desired lines
4
Result reports changed/failed
State/input
hosts: routers
Observable consequence
lines: [hostname R1]
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 605
AUTOMATION AND PROGRAMMABILITY · ANNOTATED TECHNICAL EXHIBIT
Ansible desired configuration · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
605
hosts: routers
connection: ansible.netcommon.network_cli
tasks:
- cisco.ios.ios_config:
lines: [hostname R1]
INPUT / IDENTITY
Inventory · Inventory groups targets
DECISION / STATE
Task evaluates desired lines
READBACK / RESULT
Result reports changed/failed
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 606
AUTOMATION AND PROGRAMMABILITY · DIAGNOSIS
Ansible desired configuration · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
606
Does the observed state satisfy the contract?
Mismatch / control
Idempotence depends on module and task behavior; arbitrary shell tasks are not automatically idempotent. Inventory secrets stay outside public files.
Conforming / verification
Validate inventory and inspect before/after configs; second identical run should report no change for an idempotent task.
hosts: routers
Inspect
Device connection
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 607
AUTOMATION AND PROGRAMMABILITY · VERIFICATION BRIDGE
Ansible desired configuration · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
607
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Inventory -> Device connection | hosts: routers
Mechanism / state | Result reports changed/failed | lines: [hostname R1]
Result / boundary | Validate inventory and inspect before/after configs; second identical run should report no change for an idempotent task. | Idempotence depends on module and task behavior; arbitrary shell tasks are not automatically idempotent. Inventory secrets stay outside public files.
Bridge: Activity 11: REST/JSON/automation or Activity 12: integrated verification
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 608
AUTOMATION AND PROGRAMMABILITY · ARCHITECTURE
Terraform plan and state · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
608
HCL desired resources
Desired resource declaration
Provider API
Remote resource API and identity
State file
Resource-address/remote-ID mapping
terraform init
State maps resource address to provider identity
Boundary to inspect
State can hold sensitive values; never publish state or credentials
Review create/update/destroy actions, apply result and provider readback; protect state and record resource identity.

## Slide 609
AUTOMATION AND PROGRAMMABILITY · MECHANISM
Terraform plan and state · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
609
1
Configuration defines desired objects
2
Provider reads current state
3
Plan displays difference
4
Apply persists resulting state
State/input
terraform init
Observable consequence
State maps resource address to provider identity
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 610
AUTOMATION AND PROGRAMMABILITY · ANNOTATED TECHNICAL EXHIBIT
Terraform plan and state · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
610
terraform init
terraform plan
terraform apply
State maps resource address to provider identity
INPUT / IDENTITY
HCL desired resources · Configuration defines desired objects
DECISION / STATE
Plan displays difference
READBACK / RESULT
Apply persists resulting state
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 611
AUTOMATION AND PROGRAMMABILITY · DIAGNOSIS
Terraform plan and state · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
611
Does the observed state satisfy the contract?
Mismatch / control
State can hold sensitive values; never publish state or credentials. A plan is reviewable evidence, not proof an apply converged.
Conforming / verification
Review create/update/destroy actions, apply result and provider readback; protect state and record resource identity.
terraform init
Inspect
State file
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 612
AUTOMATION AND PROGRAMMABILITY · VERIFICATION BRIDGE
Terraform plan and state · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
612
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | HCL desired resources -> State file | terraform init
Mechanism / state | Apply persists resulting state | State maps resource address to provider identity
Result / boundary | Review create/update/destroy actions, apply result and provider readback; protect state and record resource identity. | State can hold sensitive values; never publish state or credentials. A plan is reviewable evidence, not proof an apply converged.
Bridge: Activity 11: REST/JSON/automation or Activity 12: integrated verification
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 613
AUTOMATION AND PROGRAMMABILITY · ARCHITECTURE
Generative and predictive AI evidence · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
613
Operational telemetry
Measured operational input data
AI model
Prediction or generated recommendation
Human decision
Evidence-based controlled change gate
Predictive: anomaly probability 0.92
Required evidence: counters + topology + official syntax
Boundary to inspect
Generated config can hallucinate commands or weaken controls
Require source trace, simulator test, rollback and reviewer approval before live change; compare prediction with actual observed event.

## Slide 614
AUTOMATION AND PROGRAMMABILITY · MECHANISM
Generative and predictive AI evidence · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
614
1
Predictive model estimates event/risk
2
Generative model drafts explanation/config
3
Human checks evidence and syntax
4
Controlled test validates outcome
State/input
Predictive: anomaly probability 0.92
Observable consequence
Required evidence: counters + topology + official syntax
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 615
AUTOMATION AND PROGRAMMABILITY · ANNOTATED TECHNICAL EXHIBIT
Generative and predictive AI evidence · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
615
Predictive: anomaly probability 0.92
Generative: suggested ACL/change
Required evidence: counters + topology + official syntax
INPUT / IDENTITY
Operational telemetry · Predictive model estimates event/risk
DECISION / STATE
Human checks evidence and syntax
READBACK / RESULT
Controlled test validates outcome
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 616
AUTOMATION AND PROGRAMMABILITY · DIAGNOSIS
Generative and predictive AI evidence · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
616
Does the observed state satisfy the contract?
Mismatch / control
Generated config can hallucinate commands or weaken controls. Correlation and model score do not establish incident cause.
Conforming / verification
Require source trace, simulator test, rollback and reviewer approval before live change; compare prediction with actual observed event.
Predictive: anomaly probability 0.92
Inspect
Human decision
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 617
AUTOMATION AND PROGRAMMABILITY · VERIFICATION BRIDGE
Generative and predictive AI evidence · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
617
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Operational telemetry -> Human decision | Predictive: anomaly probability 0.92
Mechanism / state | Controlled test validates outcome | Required evidence: counters + topology + official syntax
Result / boundary | Require source trace, simulator test, rollback and reviewer approval before live change; compare prediction with actual observed event. | Generated config can hallucinate commands or weaken controls. Correlation and model score do not establish incident cause.
Bridge: Activity 11: REST/JSON/automation or Activity 12: integrated verification
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 618
AUTOMATION AND PROGRAMMABILITY · ARCHITECTURE
Automation change verification · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
618
Baseline snapshot
Known initial configuration and identity
Proposed diff
Reviewed narrowly scoped change
Observed readback
Actual post-change preserved state
Baseline VLANs 10, 20
Evidence: post-state + tests
Boundary to inspect
A successful API response or tool exit is insufficient
Validate target identity, preserved fields, intended change and end-to-end checks; retain rollback artifact without secrets.

## Slide 619
AUTOMATION AND PROGRAMMABILITY · MECHANISM
Automation change verification · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
619
1
Capture baseline and identity
2
Review intended delta
3
Execute scoped change
4
Read back and compare semantic fields
State/input
Baseline VLANs 10, 20
Observable consequence
Evidence: post-state + tests
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 620
AUTOMATION AND PROGRAMMABILITY · ANNOTATED TECHNICAL EXHIBIT
Automation change verification · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
620
Baseline VLANs 10, 20
Proposed addVLAN 30
Expected unchanged: VLAN 10/20, uplink, AAA
Evidence: post-state + tests
INPUT / IDENTITY
Baseline snapshot · Capture baseline and identity
DECISION / STATE
Execute scoped change
READBACK / RESULT
Read back and compare semantic fields
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 621
AUTOMATION AND PROGRAMMABILITY · DIAGNOSIS
Automation change verification · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
621
Does the observed state satisfy the contract?
Mismatch / control
A successful API response or tool exit is insufficient. Partial updates can erase fields if endpoint expects replacement.
Conforming / verification
Validate target identity, preserved fields, intended change and end-to-end checks; retain rollback artifact without secrets.
Baseline VLANs 10, 20
Inspect
Observed readback
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 622
AUTOMATION AND PROGRAMMABILITY · VERIFICATION BRIDGE
Automation change verification · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
622
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Baseline snapshot -> Observed readback | Baseline VLANs 10, 20
Mechanism / state | Read back and compare semantic fields | Evidence: post-state + tests
Result / boundary | Validate target identity, preserved fields, intended change and end-to-end checks; retain rollback artifact without secrets. | A successful API response or tool exit is insufficient. Partial updates can erase fields if endpoint expects replacement.
Bridge: Activity 11: REST/JSON/automation or Activity 12: integrated verification
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 623
ROUTING METRIC
OSPF default cost compresses fast links
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
623
Chart: 
| 10 Mb/s | 100 Mb/s | 1 Gb/s | 10 Gb/s
OSPF cost | 10 | 1 | 1 | 1
Default reference 100 Mb/s
Cost = reference / bandwidth
Minimum cost 1
Consistent updated reference is needed to distinguish high speeds.
What the data shows: Default reference 100 Mb/s

## Slide 624
ANNOUNCED TRANSITION
Announced v2.0: five-domain model
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
624
Chart: 
| Infrastructure | Switch/access | IP routing | Services/security | AI/operations
Exam weighting (%) | 25 | 25 | 20 | 20 | 10
Network Infrastructure and Connectivity 25%
Switching and Network Access 25%
IP Routing 20%
Network Services and Security 20%
AI, and Network Operations and Management 10%
Effective 3 Feb 2027.
What the data shows: Network Infrastructure and Connectivity 25%

## Slide 625
EFFECTIVE 3 FEB 2027 · CURRENT EXAM STILL V 1.1
Announced CCNA v2.0 transition
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
625
Apply operational evidence to the newly announced objectives
OSPFv3, VRRP, AAA clients, secure transfers, expanded DNS diagnosis, storm/RA controls and agentic AI.
Simulator/platform support varies; verify IOS XE syntax before execution.

## Slide 626
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
DHCPv 4 IOS server fault isolation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
626
IOS DHCP pool
Network, router, DNS and lease policy
Excluded addresses
Addresses withheld from allocation
Client VLAN
Origin subnet used for scope selection
ip dhcp excluded-address 10.10.10.1 10.10.10.20
dns-server 10.20.0.53
Boundary to inspect
Pool subnet must match client/relay scope
show ip dhcp pool; show ip dhcp binding; show ip dhcp conflict

## Slide 627
ANNOUNCED V 2.0 TRANSITION · MECHANISM
DHCPv 4 IOS server fault isolation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
627
1
Pool selects subnet
2
Excluded range prevents collision
3
Lease allocates free address
4
Options guide client connectivity
State/input
ip dhcp excluded-address 10.10.10.1 10.10.10.20
Observable consequence
dns-server 10.20.0.53
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 628
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
DHCPv 4 IOS server fault isolation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
628
ip dhcp excluded-address 10.10.10.1 10.10.10.20
ip dhcp pool USERS
network 10.10.10.0 255.255.255.0
default-router 10.10.10.1
dns-server 10.20.0.53
INPUT / IDENTITY
IOS DHCP pool · Pool selects subnet
DECISION / STATE
Lease allocates free address
READBACK / RESULT
Options guide client connectivity
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 629
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
DHCPv 4 IOS server fault isolation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
629
Does the observed state satisfy the contract?
Mismatch / control
Pool subnet must match client/relay scope. Excluding all usable addresses produces exhaustion without any physical-link failure.
Conforming / verification
show ip dhcp pool; show ip dhcp binding; show ip dhcp conflict. Compare free count and option correctness.
ip dhcp excluded-address 10.10.10.1 10.10.10.20
Inspect
Client VLAN
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 630
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
DHCPv 4 IOS server fault isolation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
630
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | IOS DHCP pool -> Client VLAN | ip dhcp excluded-address 10.10.10.1 10.10.10.20
Mechanism / state | Options guide client connectivity | dns-server 10.20.0.53
Result / boundary | show ip dhcp pool; show ip dhcp binding; show ip dhcp conflict. Compare free count and option correctness. | Pool subnet must match client/relay scope. Excluding all usable addresses produces exhaustion without any physical-link failure.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 631
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
OSPFv3 IPv6 interface activation · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
631
IPv6 interface
IPv6 addresses and link-local transport
OSPFv3 process
32-bit router ID and IPv6 protocol state
Area 0 neighbor
Peer and area compatibility
ipv6 unicast-routing
ipv6 ospf 10 area 0
Boundary to inspect
Legacy ipv 6 ospf syntax varies by IOS XE release; newer deployments may use ospfv 3 process/address-family
show ipv 6 ospf neighbor; show ipv 6 route ospf

## Slide 632
ANNOUNCED V 2.0 TRANSITION · MECHANISM
OSPFv3 IPv6 interface activation · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
632
1
IPv6 unicast routing enabled
2
Process has 32-bit router ID
3
Interface joins IPv6 OSPF area
4
Neighbor synchronizes IPv6 routes
State/input
ipv 6 unicast-routing
Observable consequence
ipv 6 ospf 10 area 0
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 633
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
OSPFv3 IPv6 interface activation · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
633
ipv6 unicast-routing
ipv6 router ospf 10
router-id 1.1.1.1
interface Gi0/0
ipv6 ospf 10 area 0
INPUT / IDENTITY
IPv6 interface · IPv6 unicast routing enabled
DECISION / STATE
Interface joins IPv6 OSPF area
READBACK / RESULT
Neighbor synchronizes IPv6 routes
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 634
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
OSPFv3 IPv6 interface activation · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
634
Does the observed state satisfy the contract?
Mismatch / control
Legacy ipv 6 ospf syntax varies by IOS XE release; newer deployments may use ospfv 3 process/address-family. Verify platform syntax before execution.
Conforming / verification
show ipv 6 ospf neighbor; show ipv 6 route ospf. Expected adjacency is Full and remote2001:db8:20::/64 is installed.
ipv 6 unicast-routing
Inspect
Area 0 neighbor
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 635
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
OSPFv3 IPv6 interface activation · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
635
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | IPv6 interface -> Area 0 neighbor | ipv 6 unicast-routing
Mechanism / state | Neighbor synchronizes IPv6 routes | ipv 6 ospf 10 area 0
Result / boundary | show ipv 6 ospf neighbor; show ipv 6 route ospf. Expected adjacency is Full and remote2001:db8:20::/64 is installed. | Legacy ipv 6 ospf syntax varies by IOS XE release; newer deployments may use ospfv 3 process/address-family. Verify platform syntax before execution.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 636
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
OSPFv3 neighbor transport · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
636
Link-local source
On-link OSPFv3 source identity
OSPFv3 multicast
FF02::5 and FF02::6 receiver groups
IPv6 LSDB
Area-wide link-state and prefix information
IPv6 next hop fe80::2 Gi0/0
Neighbor uses link-local reachability
Boundary to inspect
A dotted-decimal router ID is an identifier, not IPv4 transport
Check link-local neighbor entry, area/timers/network type and Full state; separate transport failure from missing IPv6 advertisement.

## Slide 637
ANNOUNCED V 2.0 TRANSITION · MECHANISM
OSPFv3 neighbor transport · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
637
1
Hello leaves link-local address
2
FF02::5 reaches OSPF routers
3
DR/BDR uses FF02::6
4
IPv6 prefixes are carried in LSAs
State/input
IPv6 next hop fe80::2 Gi0/0
Observable consequence
Neighbor uses link-local reachability
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 638
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
OSPFv3 neighbor transport · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
638
IPv6 next hop fe80::2 Gi0/0
OSPF IP protocol 89
Router ID stays 32-bit dotted decimal
Neighbor uses link-local reachability
INPUT / IDENTITY
Link-local source · Hello leaves link-local address
DECISION / STATE
DR/BDR uses FF02::6
READBACK / RESULT
IPv6 prefixes are carried in LSAs
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 639
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
OSPFv3 neighbor transport · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
639
Does the observed state satisfy the contract?
Mismatch / control
A dotted-decimal router ID is an identifier, not IPv4 transport. ICMPv 6/ND and IPv6 link state must work.
Conforming / verification
Check link-local neighbor entry, area/timers/network type and Full state; separate transport failure from missing IPv6 advertisement.
IPv6 next hop fe80::2 Gi0/0
Inspect
IPv6 LSDB
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 640
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
OSPFv3 neighbor transport · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
640
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Link-local source -> IPv6 LSDB | IPv6 next hop fe80::2 Gi0/0
Mechanism / state | IPv6 prefixes are carried in LSAs | Neighbor uses link-local reachability
Result / boundary | Check link-local neighbor entry, area/timers/network type and Full state; separate transport failure from missing IPv6 advertisement. | A dotted-decimal router ID is an identifier, not IPv4 transport. ICMPv 6/ND and IPv6 link state must work.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 641
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
HSRP operational status diagnosis · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
641
Active router
Current virtual-gateway forwarder
Standby router
Peer ready for ownership transfer
Tracked uplink
Upstream reachability influence on priority
show standby brief
Tracked decrement 20 -> priority 90
Boundary to inspect
Higher configured priority alone does not guarantee current ownership without preemption/election context
Read group, virtual IP, active/standby identities and effective priority before testing tracked uplink failure.

## Slide 642
ANNOUNCED V 2.0 TRANSITION · MECHANISM
HSRP operational status diagnosis · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
642
1
Priority selects preferred active
2
Hello monitors peer
3
Tracking can reduce priority
4
Preempt policy controls takeover
State/input
show standby brief
Observable consequence
Tracked decrement 20 -> priority 90
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 643
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
HSRP operational status diagnosis · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
643
show standby brief
Grp 10 Pri 110 State Active Active local
Standby 10.10.10.3 VIP 10.10.10.1
Tracked decrement 20 -> priority 90
INPUT / IDENTITY
Active router · Priority selects preferred active
DECISION / STATE
Tracking can reduce priority
READBACK / RESULT
Preempt policy controls takeover
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 644
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
HSRP operational status diagnosis · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
644
Does the observed state satisfy the contract?
Mismatch / control
Higher configured priority alone does not guarantee current ownership without preemption/election context. A failed upstream link can leave LAN interface alive.
Conforming / verification
Read group, virtual IP, active/standby identities and effective priority before testing tracked uplink failure.
show standby brief
Inspect
Tracked uplink
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 645
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
HSRP operational status diagnosis · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
645
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Active router -> Tracked uplink | show standby brief
Mechanism / state | Preempt policy controls takeover | Tracked decrement 20 -> priority 90
Result / boundary | Read group, virtual IP, active/standby identities and effective priority before testing tracked uplink failure. | Higher configured priority alone does not guarantee current ownership without preemption/election context. A failed upstream link can leave LAN interface alive.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 646
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
VRRP master and backup evidence · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
646
VRRP master
Current virtual-address owner
Backup router
Monitors master advertisements
Virtual gateway
Unchanged host next-hop identity
show vrrp brief
VRRPv 2 multicast 224.0.0.18 protocol 112
Boundary to inspect
VRRP terminology is master/backup, unlike HSRP active/standby
Confirm same group/VIP on peers and one master; compare virtual MAC0000.5e00.010a for group 10 in VRRPv 2.

## Slide 647
ANNOUNCED V 2.0 TRANSITION · MECHANISM
VRRP master and backup evidence · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
647
1
Master advertises ownership
2
Backup tracks advertisement
3
Master failure promotes backup
4
Clients keep virtual IP
State/input
show vrrp brief
Observable consequence
VRRPv 2 multicast 224.0.0.18 protocol 112
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 648
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
VRRP master and backup evidence · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
648
show vrrp brief
Group 10 Virtual IP 10.10.10.1
R1 priority 110 MASTER
VRRPv 2 multicast 224.0.0.18 protocol 112
INPUT / IDENTITY
VRRP master · Master advertises ownership
DECISION / STATE
Master failure promotes backup
READBACK / RESULT
Clients keep virtual IP
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 649
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
VRRP master and backup evidence · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
649
Does the observed state satisfy the contract?
Mismatch / control
VRRP terminology is master/backup, unlike HSRP active/standby. Owner/preemption behavior can affect which router currently forwards.
Conforming / verification
Confirm same group/VIP on peers and one master; compare virtual MAC0000.5e00.010a for group 10 in VRRPv 2.
show vrrp brief
Inspect
Virtual gateway
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 650
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
VRRP master and backup evidence · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
650
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | VRRP master -> Virtual gateway | show vrrp brief
Mechanism / state | Clients keep virtual IP | VRRPv 2 multicast 224.0.0.18 protocol 112
Result / boundary | Confirm same group/VIP on peers and one master; compare virtual MAC0000.5e00.010a for group 10 in VRRPv 2. | VRRP terminology is master/backup, unlike HSRP active/standby. Owner/preemption behavior can affect which router currently forwards.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 651
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
TACACS+ IOS AAA client · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
651
VTY SSH client
Remote SSH management initiator
IOS AAA method list
Selects server group and fallback
TACACS+ server
Central device identity/command service
aaa new-model
aaa authentication login default group tacacs+ local
Boundary to inspect
Syntax and authorization requirements vary by software
Verify server TCP 49 reachability, accepted identity and tested fallback under authorized maintenance; preserve console access.

## Slide 652
ANNOUNCED V 2.0 TRANSITION · MECHANISM
TACACS+ IOS AAA client · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
652
1
VTY selects method list
2
Device contacts server
3
Server authenticates identity
4
Authorization/accounting policies apply separately
State/input
aaa new-model
Observable consequence
aaa authentication login default group tacacs+ local
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 653
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
TACACS+ IOS AAA client · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
653
aaa new-model
tacacs server TRAINING
address ipv4 192.0.2.70
key <training-only-secret>
aaa authentication login default group tacacs+ local
INPUT / IDENTITY
VTY SSH client · VTY selects method list
DECISION / STATE
Server authenticates identity
READBACK / RESULT
Authorization/accounting policies apply separately
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 654
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
TACACS+ IOS AAA client · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
654
Does the observed state satisfy the contract?
Mismatch / control
Syntax and authorization requirements vary by software. Local fallback usually applies when server errors/unreachable, not merely when credentials are rejected.
Conforming / verification
Verify server TCP 49 reachability, accepted identity and tested fallback under authorized maintenance; preserve console access.
aaa new-model
Inspect
TACACS+ server
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 655
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
TACACS+ IOS AAA client · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
655
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | VTY SSH client -> TACACS+ server | aaa new-model
Mechanism / state | Authorization/accounting policies apply separately | aaa authentication login default group tacacs+ local
Result / boundary | Verify server TCP 49 reachability, accepted identity and tested fallback under authorized maintenance; preserve console access. | Syntax and authorization requirements vary by software. Local fallback usually applies when server errors/unreachable, not merely when credentials are rejected.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 656
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
RADIUS IOS management client · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
656
IOS device
Sends scoped management AAA requests
RADIUS server
Authentication/accounting decision service
Local fallback DB
Maintains controlled emergency identity
radius server TRAINING
aaa authentication login default group radius local
Boundary to inspect
Do not confuse management AAA client configuration with a WLAN supplicant
Read method-list binding and RADIUS server statistics; test acceptance, rejection and unreachable-server behavior separately.

## Slide 657
ANNOUNCED V 2.0 TRANSITION · MECHANISM
RADIUS IOS management client · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
657
1
Device sends access request
2
Server returns accept/reject
3
Device enforces login decision
4
Accounting can record session
State/input
radius server TRAINING
Observable consequence
aaa authentication login default group radius local
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 658
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
RADIUS IOS management client · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
658
radius server TRAINING
address ipv4 192.0.2.71 auth-port 1812 acct-port 1813
key <training-only-secret>
aaa authentication login default group radius local
INPUT / IDENTITY
IOS device · Device sends access request
DECISION / STATE
Device enforces login decision
READBACK / RESULT
Accounting can record session
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 659
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
RADIUS IOS management client · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
659
Does the observed state satisfy the contract?
Mismatch / control
Do not confuse management AAA client configuration with a WLAN supplicant. Shared secret is sensitive and must stay out of public course files.
Conforming / verification
Read method-list binding and RADIUS server statistics; test acceptance, rejection and unreachable-server behavior separately.
radius server TRAINING
Inspect
Local fallback DB
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 660
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
RADIUS IOS management client · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
660
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | IOS device -> Local fallback DB | radius server TRAINING
Mechanism / state | Accounting can record session | aaa authentication login default group radius local
Result / boundary | Read method-list binding and RADIUS server statistics; test acceptance, rejection and unreachable-server behavior separately. | Do not confuse management AAA client configuration with a WLAN supplicant. Shared secret is sensitive and must stay out of public course files.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 661
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
SCP and SFTP secure file evidence · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
661
Device file system
Running/startup/image storage scope
SSH transport
Encrypted authenticated TCP 22 channel
Transfer server
Authorized source/destination file endpoint
SCP over SSH TCP 22
sha 256 source == sha 256 destination
Boundary to inspect
SCP and SFTP are distinct protocols even though both use SSH
Compare source/destination filename, size, hash and device image compatibility; restrict privileges and protect configs containing secrets.

## Slide 662
ANNOUNCED V 2.0 TRANSITION · MECHANISM
SCP and SFTP secure file evidence · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
662
1
SSH verifies/authenticates peer
2
SCP/SFTP moves bytes
3
Destination stores file
4
Integrity/readback validates artifact
State/input
SCP over SSH TCP 22
Observable consequence
sha 256 source == sha 256 destination
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 663
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
SCP and SFTP secure file evidence · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
663
SCP over SSH TCP 22
SFTP uses SSH file-transfer subsystem
copy running-config scp:
sha 256 source == sha 256 destination
INPUT / IDENTITY
Device file system · SSH verifies/authenticates peer
DECISION / STATE
Destination stores file
READBACK / RESULT
Integrity/readback validates artifact
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 664
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
SCP and SFTP secure file evidence · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
664
Does the observed state satisfy the contract?
Mismatch / control
SCP and SFTP are distinct protocols even though both use SSH. Server/subsystem support varies; filename transfer success does not prove correct content.
Conforming / verification
Compare source/destination filename, size, hash and device image compatibility; restrict privileges and protect configs containing secrets.
SCP over SSH TCP 22
Inspect
Transfer server
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 665
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
SCP and SFTP secure file evidence · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
665
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Device file system -> Transfer server | SCP over SSH TCP 22
Mechanism / state | Integrity/readback validates artifact | sha 256 source == sha 256 destination
Result / boundary | Compare source/destination filename, size, hash and device image compatibility; restrict privileges and protect configs containing secrets. | SCP and SFTP are distinct protocols even though both use SSH. Server/subsystem support varies; filename transfer success does not prove correct content.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 666
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
DNS mail and authority diagnosis · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
666
MX record
Mail exchanger preference and hostname
NS authority
Published authoritative zone server
PTR reverse zone
Reverse address-to-name namespace
example.test MX 10 mail.example.test
25.2.0.192.in-addr.arpa PTRmail.example.test
Boundary to inspect
An MX target must resolve appropriately; reverse DNS lives in a distinct zone
Query MX, target A/AAAA, NS and PTR; distinguish NXDOMAIN, SERVFAIL, timeout and a valid but unintended answer.

## Slide 667
ANNOUNCED V 2.0 TRANSITION · MECHANISM
DNS mail and authority diagnosis · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
667
1
MX points mail domain to host
2
A/AAAA resolves mail host
3
NS points zone to authority
4
PTR maps reverse address to name
State/input
example.test MX 10 mail.example.test
Observable consequence
25.2.0.192.in-addr.arpa PTRmail.example.test
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 668
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
DNS mail and authority diagnosis · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
668
example.test MX 10 mail.example.test
mail.example.test A192.0.2.25
example.test NSns 1.example.test
25.2.0.192.in-addr.arpa PTRmail.example.test
INPUT / IDENTITY
MX record · MX points mail domain to host
DECISION / STATE
NS points zone to authority
READBACK / RESULT
PTR maps reverse address to name
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 669
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
DNS mail and authority diagnosis · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
669
Does the observed state satisfy the contract?
Mismatch / control
An MX target must resolve appropriately; reverse DNS lives in a distinct zone. CNAME aliases, forward and reverse answers are separate evidence.
Conforming / verification
Query MX, target A/AAAA, NS and PTR; distinguish NXDOMAIN, SERVFAIL, timeout and a valid but unintended answer.
example.test MX 10 mail.example.test
Inspect
PTR reverse zone
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 670
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
DNS mail and authority diagnosis · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
670
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | MX record -> PTR reverse zone | example.test MX 10 mail.example.test
Mechanism / state | PTR maps reverse address to name | 25.2.0.192.in-addr.arpa PTRmail.example.test
Result / boundary | Query MX, target A/AAAA, NS and PTR; distinguish NXDOMAIN, SERVFAIL, timeout and a valid but unintended answer. | An MX target must resolve appropriately; reverse DNS lives in a distinct zone. CNAME aliases, forward and reverse answers are separate evidence.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 671
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
Broadcast storm-control thresholds · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
671
Ingress access port
Traffic category and measurement point
Broadcast traffic meter
Rising/falling utilization state
Drop policy
Suppresses excess selected traffic
interface Gi1/0/10
Measurement specifics platform-dependent
Boundary to inspect
Do not set a threshold without baseline traffic
show storm-control; compare counter deltas and legitimate protocol success before/after a controlled traffic spike.

## Slide 672
ANNOUNCED V 2.0 TRANSITION · MECHANISM
Broadcast storm-control thresholds · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
672
1
Meter measures broadcast utilization
2
Traffic exceeds rising threshold
3
Excess broadcast is suppressed
4
Falling threshold permits recovery
State/input
interface Gi1/0/10
Observable consequence
Measurement specifics platform-dependent
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 673
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
Broadcast storm-control thresholds · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
673
interface Gi1/0/10
storm-control broadcast level 5.00 3.00
Rising 5%; falling 3%
Measurement specifics platform-dependent
INPUT / IDENTITY
Ingress access port · Meter measures broadcast utilization
DECISION / STATE
Excess broadcast is suppressed
READBACK / RESULT
Falling threshold permits recovery
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 674
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
Broadcast storm-control thresholds · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
674
Does the observed state satisfy the contract?
Mismatch / control
Do not set a threshold without baseline traffic. Legitimate ARP/DHCP can be disrupted; multicast/unicast controls are distinct categories.
Conforming / verification
show storm-control; compare counter deltas and legitimate protocol success before/after a controlled traffic spike.
interface Gi1/0/10
Inspect
Drop policy
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 675
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
Broadcast storm-control thresholds · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
675
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Ingress access port -> Drop policy | interface Gi1/0/10
Mechanism / state | Falling threshold permits recovery | Measurement specifics platform-dependent
Result / boundary | show storm-control; compare counter deltas and legitimate protocol success before/after a controlled traffic spike. | Do not set a threshold without baseline traffic. Legitimate ARP/DHCP can be disrupted; multicast/unicast controls are distinct categories.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 676
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
IPv6 RA guard trust boundary · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
676
Endpoint port
Non-router host attachment
Router advertisement
Default-router/prefix control message
Authorized router uplink
Permitted router advertisement source
ipv6 nd raguard policy HOST_POLICY
ipv6 nd raguard attach-policy HOST_POLICY
Boundary to inspect
Platform support and policy syntax vary
Compare received RA source, policy binding and IPv6 default router; verify authorized RA accepted and endpoint-originated RA rejected.

## Slide 677
ANNOUNCED V 2.0 TRANSITION · MECHANISM
IPv6 RA guard trust boundary · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
677
1
Host expects RA from router
2
Endpoint sends rogue RA
3
RA guard policy blocks unauthorized advertisement
4
Trusted router remains allowed
State/input
ipv 6 nd raguard policy HOST_POLICY
Observable consequence
ipv 6 nd raguard attach-policy HOST_POLICY
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 678
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
IPv6 RA guard trust boundary · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
678
ipv6 nd raguard policy HOST_POLICY
device-role host
interface Gi1/0/10
ipv6 nd raguard attach-policy HOST_POLICY
INPUT / IDENTITY
Endpoint port · Host expects RA from router
DECISION / STATE
RA guard policy blocks unauthorized advertisement
READBACK / RESULT
Trusted router remains allowed
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 679
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
IPv6 RA guard trust boundary · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
679
Does the observed state satisfy the contract?
Mismatch / control
Platform support and policy syntax vary. RA guard must not block authorized router-facing advertisements or break legitimate IPv6 access.
Conforming / verification
Compare received RA source, policy binding and IPv6 default router; verify authorized RA accepted and endpoint-originated RA rejected.
ipv 6 nd raguard policy HOST_POLICY
Inspect
Authorized router uplink
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 680
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
IPv6 RA guard trust boundary · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
680
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Endpoint port -> Authorized router uplink | ipv 6 nd raguard policy HOST_POLICY
Mechanism / state | Trusted router remains allowed | ipv 6 nd raguard attach-policy HOST_POLICY
Result / boundary | Compare received RA source, policy binding and IPv6 default router; verify authorized RA accepted and endpoint-originated RA rejected. | Platform support and policy syntax vary. RA guard must not block authorized router-facing advertisements or break legitimate IPv6 access.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 681
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
Extended ping and packet-capture inference · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
681
Selected source address
Explicit test-origin identity
ICMP path
Forward path and ICMP filtering
Reply route
Destination route back to selected source
Extended ping source 10.10.10.1
Potential return route/policy fault
Boundary to inspect
A router ping from WAN source may pass while LAN-sourced traffic fails
Compare default-source and explicit-source results; capture at boundaries to locate where request or response disappears.

## Slide 682
ANNOUNCED V 2.0 TRANSITION · MECHANISM
Extended ping and packet-capture inference · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
682
1
Operator chooses source/interface
2
Echo traverses routed path
3
Target selects return route
4
Reply result tests both directions
State/input
Extended ping source 10.10.10.1
Observable consequence
Potential return route/policy fault
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 683
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
Extended ping and packet-capture inference · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
683
Extended ping source 10.10.10.1
Target 10.20.20.20
Capture request arrives; no reply seen
Potential return route/policy fault
INPUT / IDENTITY
Selected source address · Operator chooses source/interface
DECISION / STATE
Target selects return route
READBACK / RESULT
Reply result tests both directions
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 684
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
Extended ping and packet-capture inference · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
684
Does the observed state satisfy the contract?
Mismatch / control
A router ping from WAN source may pass while LAN-sourced traffic fails. ICMP filtering can make traceroute incomplete despite forwarding.
Conforming / verification
Compare default-source and explicit-source results; capture at boundaries to locate where request or response disappears.
Extended ping source 10.10.10.1
Inspect
Reply route
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 685
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
Extended ping and packet-capture inference · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
685
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Selected source address -> Reply route | Extended ping source 10.10.10.1
Mechanism / state | Reply result tests both directions | Potential return route/policy fault
Result / boundary | Compare default-source and explicit-source results; capture at boundaries to locate where request or response disappears. | A router ping from WAN source may pass while LAN-sourced traffic fails. ICMP filtering can make traceroute incomplete despite forwarding.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 686
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
Agentic AI operational boundary · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
686
Telemetry input
Sanitized evidence and known topology
Planning agent
Plans diagnostics and calls bounded tools
Human change gate
Authorizes reviewed verified write change
Allowed tools: show_route, show_interface
Output: hypothesis, evidence, confidence, next_test
Boundary to inspect
An autonomous plan can amplify a mistaken diagnosis
Check tool-call audit, referenced evidence and preserved security policy; reject unsupported recommendation even if fluent/confident.

## Slide 687
ANNOUNCED V 2.0 TRANSITION · MECHANISM
Agentic AI operational boundary · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
687
1
Agent collects evidence
2
Plans candidate diagnosis
3
Calls scoped read-only tool
4
Human authorizes verified write plan
State/input
Allowed tools: show_route, show_interface
Observable consequence
Output: hypothesis, evidence, confidence, next_test
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 688
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
Agentic AI operational boundary · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
688
Allowed tools: show_route, show_interface
Forbidden autonomous write: remove_acl
Output: hypothesis, evidence, confidence, next_test
INPUT / IDENTITY
Telemetry input · Agent collects evidence
DECISION / STATE
Calls scoped read-only tool
READBACK / RESULT
Human authorizes verified write plan
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 689
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
Agentic AI operational boundary · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
689
Does the observed state satisfy the contract?
Mismatch / control
An autonomous plan can amplify a mistaken diagnosis. Tool permissions, data classification and write gates must be explicit.
Conforming / verification
Check tool-call audit, referenced evidence and preserved security policy; reject unsupported recommendation even if fluent/confident.
Allowed tools: show_route, show_interface
Inspect
Human change gate
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 690
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
Agentic AI operational boundary · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
690
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Telemetry input -> Human change gate | Allowed tools: show_route, show_interface
Mechanism / state | Human authorizes verified write plan | Output: hypothesis, evidence, confidence, next_test
Result / boundary | Check tool-call audit, referenced evidence and preserved security policy; reject unsupported recommendation even if fluent/confident. | An autonomous plan can amplify a mistaken diagnosis. Tool permissions, data classification and write gates must be explicit.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 691
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
Network AI prompt selection · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
691
Data classification
Secret/PII restrictions on supplied data
Response schema
Required typed response fields
Evidence instruction
Demand traceable evidence and uncertainty
Role: CCNA troubleshooting reviewer
Do not execute changes; cite supplied evidence
Boundary to inspect
A broad prompt to fix network with all credentials invites unsafe disclosure and uncontrolled change
Select prompt with classification, exact output, read-only constraint and uncertainty rule; compare proposed diagnosis to supplied counters.

## Slide 692
ANNOUNCED V 2.0 TRANSITION · MECHANISM
Network AI prompt selection · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
692
1
Remove secrets/PII
2
Name troubleshooting role
3
Provide measured logs/topology
4
Require bounded structured recommendations
State/input
Role: CCNA troubleshooting reviewer
Observable consequence
Do not execute changes; cite supplied evidence
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 693
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
Network AI prompt selection · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
693
Role: CCNA troubleshooting reviewer
Data: synthetic/anonymized interface counters
Return JSON {hypothesis, evidence, next_test}
Do not execute changes; cite supplied evidence
INPUT / IDENTITY
Data classification · Remove secrets/PII
DECISION / STATE
Provide measured logs/topology
READBACK / RESULT
Require bounded structured recommendations
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 694
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
Network AI prompt selection · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
694
Does the observed state satisfy the contract?
Mismatch / control
A broad prompt to fix network with all credentials invites unsafe disclosure and uncontrolled change. Persona does not substitute for evidence.
Conforming / verification
Select prompt with classification, exact output, read-only constraint and uncertainty rule; compare proposed diagnosis to supplied counters.
Role: CCNA troubleshooting reviewer
Inspect
Evidence instruction
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 695
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
Network AI prompt selection · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
695
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Data classification -> Evidence instruction | Role: CCNA troubleshooting reviewer
Mechanism / state | Require bounded structured recommendations | Do not execute changes; cite supplied evidence
Result / boundary | Select prompt with classification, exact output, read-only constraint and uncertainty rule; compare proposed diagnosis to supplied counters. | A broad prompt to fix network with all credentials invites unsafe disclosure and uncontrolled change. Persona does not substitute for evidence.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 696
ANNOUNCED V 2.0 TRANSITION · ARCHITECTURE
Ansible execute and verify commands · boundaries
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
696
Inventory group
Approved target group and credentials
ios_command module
Read-only network command execution
Result register
Stored output and exact acceptance checks
cisco.ios.ios_command:
Expected neighbor state: FULL
Boundary to inspect
Read-only command execution differs from configuration convergence
Validate target router ID, neighbor identity, state and interface

## Slide 697
ANNOUNCED V 2.0 TRANSITION · MECHANISM
Ansible execute and verify commands · runtime trace
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
697
1
Task connects to approved routers
2
Read-only show command executes
3
Registered output stores evidence
4
Assertion evaluates acceptance
State/input
cisco.ios.ios_command:
Observable consequence
Expected neighbor state: FULL
Trace each transition against the named fields; do not infer a working end-to-end service from a single state.

## Slide 698
ANNOUNCED V 2.0 TRANSITION · ANNOTATED TECHNICAL EXHIBIT
Ansible execute and verify commands · exact contract
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
698
cisco.ios.ios_command:
commands: [show ip ospf neighbor]
register: ospf_output
Expected neighbor state: FULL
INPUT / IDENTITY
Inventory group · Task connects to approved routers
DECISION / STATE
Registered output stores evidence
READBACK / RESULT
Assertion evaluates acceptance
Interpret the exhibit; full command sequence, fixtures and execution steps are in the Learner Guide.

## Slide 699
ANNOUNCED V 2.0 TRANSITION · DIAGNOSIS
Ansible execute and verify commands · fault and control
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
699
Does the observed state satisfy the contract?
Mismatch / control
Read-only command execution differs from configuration convergence. Parse output carefully; substring matches alone can accept wrong neighbors.
Conforming / verification
Validate target router ID, neighbor identity, state and interface. Retain command output/time and avoid embedding inventory secrets.
cisco.ios.ios_command:
Inspect
Result register
Select a diagnosis from measured evidence. The same visible symptom can arise at different boundaries.

## Slide 700
ANNOUNCED V 2.0 TRANSITION · VERIFICATION BRIDGE
Ansible execute and verify commands · acceptance evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
700
Evidence dimension | Expected interpretation | Control / exact field
Identity / scope | Inventory group -> Result register | cisco.ios.ios_command:
Mechanism / state | Assertion evaluates acceptance | Expected neighbor state: FULL
Result / boundary | Validate target router ID, neighbor identity, state and interface. Retain command output/time and avoid embedding inventory secrets. | Read-only command execution differs from configuration convergence. Parse output carefully; substring matches alone can accept wrong neighbors.
Bridge: v2.0 transition fixtures in Activities 6-12; simulator support varies by feature
Retain target identity, observed values and test time; a tool exit code or single ping is insufficient.

## Slide 701
PRACTICE BRIDGE · 90 MIN
Activity 1 · Addressing and endpoint paths
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
701
Scenario / scope
Allocate non-overlapping VLSM subnets and explain remote packet versus next-hop frame addressing.
Technical output
Corrected JSON/CSV case, checker output, config specimen, diagnosis and acceptance checklist.
Acceptance
Fixture checker validates synthetic evidence; trainer checks simulator/hardware results separately.
Full instructions, exact commands and checklists: Learner Guide + independent activity folder.

## Slide 702
PRACTICE BRIDGE · 90 MIN
Activity 2 · Physical and VLAN evidence
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
702
Scenario / scope
Use interface counter deltas and endpoint VLAN membership to separate physical faults from segmentation errors.
Technical output
Corrected JSON/CSV case, checker output, config specimen, diagnosis and acceptance checklist.
Acceptance
Fixture checker validates synthetic evidence; trainer checks simulator/hardware results separately.
Full instructions, exact commands and checklists: Learner Guide + independent activity folder.

## Slide 703
PRACTICE BRIDGE · 100 MIN
Activity 3 · Trunks and inter-VLAN routing
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
703
Scenario / scope
Diagnose a missing allowed VLAN and native VLAN mismatch, then verify SVI gateway mapping.
Technical output
Corrected JSON/CSV case, checker output, config specimen, diagnosis and acceptance checklist.
Acceptance
Fixture checker validates synthetic evidence; trainer checks simulator/hardware results separately.
Full instructions, exact commands and checklists: Learner Guide + independent activity folder.

## Slide 704
PRACTICE BRIDGE · 100 MIN
Activity 4 · EtherChannel and STP resilience
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
704
Scenario / scope
Check LACP negotiation and spanning-tree redundancy without confusing blocked paths with failed links.
Technical output
Corrected JSON/CSV case, checker output, config specimen, diagnosis and acceptance checklist.
Acceptance
Fixture checker validates synthetic evidence; trainer checks simulator/hardware results separately.
Full instructions, exact commands and checklists: Learner Guide + independent activity folder.

## Slide 705
PRACTICE BRIDGE · 90 MIN
Activity 5 · Wireless WLAN and policy mapping
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
705
Scenario / scope
Connect SSID, authentication, VLAN and client addressing while inspecting RF channel and WLC data-path choices.
Technical output
Corrected JSON/CSV case, checker output, config specimen, diagnosis and acceptance checklist.
Acceptance
Fixture checker validates synthetic evidence; trainer checks simulator/hardware results separately.
Full instructions, exact commands and checklists: Learner Guide + independent activity folder.

## Slide 706
PRACTICE BRIDGE · 100 MIN
Activity 6 · Static routing and IPv6
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
706
Scenario / scope
Apply longest-prefix match, a floating route and interface-scoped IPv6 link-local next hops.
Technical output
Corrected JSON/CSV case, checker output, config specimen, diagnosis and acceptance checklist.
Acceptance
Fixture checker validates synthetic evidence; trainer checks simulator/hardware results separately.
Full instructions, exact commands and checklists: Learner Guide + independent activity folder.

## Slide 707
PRACTICE BRIDGE · 120 MIN
Activity 7 · OSPF and gateway failover
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
707
Scenario / scope
Diagnose OSPF adjacency, path costs and a virtual gateway; distinguish current v1.1 FHRP explanation from refresh practice.
Technical output
Corrected JSON/CSV case, checker output, config specimen, diagnosis and acceptance checklist.
Acceptance
Fixture checker validates synthetic evidence; trainer checks simulator/hardware results separately.
Full instructions, exact commands and checklists: Learner Guide + independent activity folder.

## Slide 708
PRACTICE BRIDGE · 100 MIN
Activity 8 · NAT DHCP DNS and time
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
708
Scenario / scope
Correlate translated transport tuples, DHCP scope options, DNS records and synchronized logging.
Technical output
Corrected JSON/CSV case, checker output, config specimen, diagnosis and acceptance checklist.
Acceptance
Fixture checker validates synthetic evidence; trainer checks simulator/hardware results separately.
Full instructions, exact commands and checklists: Learner Guide + independent activity folder.

## Slide 709
PRACTICE BRIDGE · 110 MIN
Activity 9 · ACL and secure management
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
709
Scenario / scope
Evaluate ordered ACL rules and secure VTY access, including AAA client/server roles and safe fallback.
Technical output
Corrected JSON/CSV case, checker output, config specimen, diagnosis and acceptance checklist.
Acceptance
Fixture checker validates synthetic evidence; trainer checks simulator/hardware results separately.
Full instructions, exact commands and checklists: Learner Guide + independent activity folder.

## Slide 710
PRACTICE BRIDGE · 90 MIN
Activity 10 · Layer 2 and wireless security
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
710
Scenario / scope
Map trusted infrastructure ports and untrusted edge ports to DHCP snooping, DAI, port security and wireless authentication.
Technical output
Corrected JSON/CSV case, checker output, config specimen, diagnosis and acceptance checklist.
Acceptance
Fixture checker validates synthetic evidence; trainer checks simulator/hardware results separately.
Full instructions, exact commands and checklists: Learner Guide + independent activity folder.

## Slide 711
PRACTICE BRIDGE · 80 MIN
Activity 11 · REST JSON and configuration automation
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
711
Scenario / scope
Validate REST status and JSON types, produce an idempotent plan and select a bounded agentic AI prompt.
Technical output
Corrected JSON/CSV case, checker output, config specimen, diagnosis and acceptance checklist.
Acceptance
Fixture checker validates synthetic evidence; trainer checks simulator/hardware results separately.
Full instructions, exact commands and checklists: Learner Guide + independent activity folder.

## Slide 712
PRACTICE BRIDGE · 70 MIN
Activity 12 · Integrated incident and change verification
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
712
Scenario / scope
Use time-correlated service evidence to isolate a trunk fault and verify a narrow change with regression tests and rollback.
Technical output
Corrected JSON/CSV case, checker output, config specimen, diagnosis and acceptance checklist.
Acceptance
Fixture checker validates synthetic evidence; trainer checks simulator/hardware results separately.
Full instructions, exact commands and checklists: Learner Guide + independent activity folder.

## Slide 713
LIVE PRACTICE PLATFORM · CURRENT V 1.1
Practice exam: CCNA readiness
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
713
Six practice exams
100 questions each ·120 minutes each
Use domain-level results to target revision.
https://exams.tertiaryinfotech.com/practice-exams/cisco/cisco-ccna
Platform threshold 82% is a practice-site rule; it is not an official Cisco passing score.

## Slide 714
COURSE ADMINISTRATION
Assessment
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
714
Written Assessment
1 hour · open book
Knowledge evidence K1-K6.
Practical Performance
1 hour · open book
Implementation and verification A1-A6.
Submission
Use assigned candidate papers and trainer-issued LMS submission links.

## Slide 715
WSQ ASSESSMENT ADMINISTRATION
Assessment Flow
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
715
Attendance
Training entry
Assessment attendance
Record entry
WA then PP
Approved duration
LMS submission
Upload answers
Summary Record
Review and sign
Trainer confirms attendance, assessment evidence, submission and record completion.

## Slide 716
COURSE ADMINISTRATION
Digital Attendance (Mandatory)
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
716
Digital attendance
Record required attendance using the provider-issued attendance link or process.
Assessment session
Confirm the correct course title and TGS code; record the assessment session.
TRAQOM feedback
Complete the separate training-quality feedback survey using the provider-issued TRAQOM link.

## Slide 717
CCNA · CONTINUE WITH VERIFIED PRACTICE
Thank You
CCNA · TGS-2023037854
© 2026 Tertiary Infotech Academy Pte Ltd
717
Observe. Explain. Configure. Verify.
Tertiary Infotech Academy Pte Ltd
enquiry@tertiaryinfotech.com · +65 6100 0613